## Slide 1: A Completely Serious Overview of Network Performance for Scientific Networking
Jason Zurawski, Science Engagement Engineer
ESnet
Focused Technical Workshop
Lawrence Berkeley National Lab, Berkeley, CA
July 18th 2013

## Slide 2: Outline (Completely Serious)
Endgame – Efficient networks to support science
Use Case
Expectations & Realities
Problem Definition
Solution Space
Conclusions
© 2013 Muppet Wiki

## Slide 3: Endgame = Scientific Network Use
What we have seen so far yesterday, and today:
    Network Infrastructure
    Storage and Processing
    Workflow
    Applications
What we are missing:
    Preparing for the worst, e.g. sometimes it just doesn’t work
    Addressing problems (deliberate and non-deliberate)
    “Festivus”
      e.g. data movement/network design strategies for the rest of us – may involve feats of strength and airing of grievances

## Slide 4: Outline
Endgame
Use Case – Meet our actors and action
Expectations & Realities
Problem Definition
Solution Space
Conclusions

## Slide 5: Use Case = End to End Exchange
Alice & Bob are collaborators
    Experts in their field
    Physically separated (common)
    Rely on networks, but are not IT experts (common & expected)
    They know their local IT staff. May also have an adversarial relationship with them (e.g. Alice and Bob are ‘troublemakers’ since they use the network, and expect it to work)
Alice & Bob want to embark on a new project
    Instrumentation @ one end, processing/analysis @ the other
    Keep in mind they know about the science, not about the technology in the middle
    Use infrastructure they are comfortable with, perhaps cobbled together by local support staff

## Slide 6: Meet Alice & Bob - They are Science Cats
INTERNETS
© 2013 Susan's School Days
© 2013 icanhascheezburger.com
HAI, I CAN HAZ DATA?
MOAR DATA 4 U
K THX BAI

## Slide 7: Outline
Endgame
Use Case
Expectations & Realities – What could possibly go wrong?
Problem Definition
Solution Space
Conclusions
© 2013 funnyasduck.net

## Slide 8: Expectations & Realities
© Dog Shaming 2012
"In any large system, there is always something broken.”
Jon Postel
Modern networks are large and complicated
Many users will encounter unforeseen (and therefore challenging) situations:
  Upgrading networks breaks them (loss of configuration, etc.)
  Synergy between the new and the old
  Statistical anomalies, e.g. that 7 year old interface will stop working eventually…
Mitigating the risk can be done in a number of ways:
    Analysis and alteration to architecture
    Careful thought to security/data policies in target areas
  Integration of software designed to exercise the network, and alert/visualize

## Slide 9: Meet Alice & Bob; Sad Reality
INTERNETS
© 2013 Susan's School Days
© 2013 icanhascheezburger.com
HAI, I CAN HAZ DATA?
MOAR DATA 4 U
SOOO SLOOOW!
I CAN HAZ TECH SUPPORT?
© 2013 Berkeley Breathed
I CAN HAZ FEDEX?
© 2013 Renee Richardson photography

## Slide 10: “The Network Is Working Fine”
    Trouble prompted a call to support (e.g. know when you are in too deep)
    The response can be frustrating (we all have been there…)
      The engineers look at magic (and secret) monitoring tools, and tell you, firmly, that things are as they should be.
    In fairness – the network *may* be fine locally. e.g. We don’t see the signs of stress for the pieces we control
    In reality we need ‘end to end’ visibility, its what you experienced after all

## Slide 11: Identification of Problems
Use Case = End to End
    All collaboration is multi-domain, which implies you need to care about how others are running their networks as well
    Many problems may fall between the cracks as the RTT increases (N.B. work by many, including M. Mathis)
Two behaviors that need adjustment:
    “Not My Network, Not My Problem”
    Patience of Researcher
Notes: Note that there was an attempt here to ‘complain’, and then a workaround.

## Slide 12: Outline
Endgame – Efficient Use of the Network to Support Science
Use Case
Expectations & Realities
Problem Definition – More than meets the eye
Solution Space
Conclusions

## Slide 13: Abstraction Helps & Hurts
INTERNETS
Notes: Need to look at our environment from different angles
    Networks are large and complex, but well structured
    The environment itself has mechanisms that can be used to address problems

## Slide 14: Abstraction Helps & Hurts
MY INTERNETS
YOUR INTERNETS
THEIR INTERNETS
OTHER INTERNETS
??? INTERNETS
MOAR INTERNETS
Notes: Need to look at our environment from different angles
    Networks are large and complex, but well structured
    The environment itself has mechanisms that can be used to address problems

## Slide 15: Abstraction Helps & Hurts
© 2013 University of Washington
Notes: Need to look at our environment from different angles
    Networks are large and complex, but well structured
    The environment itself has mechanisms that can be used to address problems

## Slide 16: Abstraction Helps & Hurts
Protocols, Etc.
Notes: Need to look at our environment from different angles
    Networks are large and complex, but well structured
    The environment itself has mechanisms that can be used to address problems

## Slide 17: Failure in the Layers
Redundancy Helps With Redundancy
Protocols Adjust to Failure Transparently
Severed Connections Are Easy to Find/Fix
“Slow” Connections are Harder…
IM DROPN UR
PACKETS LOL

## Slide 18: Outline
Endgame – Efficient Use of the Network to Support Science
Use Case
Expectations & Realities
Problem Definition
Solution Space – It’s not as bleak as it seems
Conclusions

## Slide 19: Solution Space
Basic idea:
    Architectural changes
    Solution for Monitoring/Emulation of User Behavior
    Workflow Analysis/Adoption of New Tools (but we have heard that part already)
Architecture
    Split out enterprise concerns from data intensive ones
    Directed security policies, instead of blanket enforcement
    E.g. the Science DMZ
Monitoring:
    Dedicated resources at different vantage points in the network
    Running some standard and useful types of measurement
    Integrated with tools that allow you to see/hear when a problem arises

## Slide 20: Science DMZ Overview
Significant commonality in issues encountered with science collaborations … and similar solution set
  The causes of poor data transfer performance fit into a few categories with similar solutions
    Un-tuned/under-powered hosts
    Packet loss issues
    Security devices
  A successful model has emerged – the Science DMZ
    This model successfully in use by CMS/ATLAS, ESG, NERSC, ORNL, ALS, and others
The Science DMZ is a blueprint for network design.
  Not all implementations look the same, but share common features
  Some choices don’t make sense for everyone, caveat emptor

## Slide 21: The Science DMZ in 1 Slide
Consists of three key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
© 2013 Globus

## Slide 22: Science DMZ – Simple Abstract Cartoon
Notes: Note security policy control points

## Slide 23
Network Monitoring
E.g. everyone has some form on their network. Addresses needs of local staff for understanding state of the network
    Would this information be useful to external users?
    Can these tools function on a multi-domain basis?
Beyond passive methods, there are active tools.
    E.g. often we want a ‘throughput’ number. Can we automate that idea?
    Wouldn’t it be nice to get some sort of plot of performance over the course of a day? Week? Year? Multiple endpoints?
perfSONAR = Measurement Middleware
Perf-what?

## Slide 24: What is perfSONAR?
http://psps.perfsonar.net
perfSONAR is a tool to:
Set network performance expectations
Find network problems (“soft failures”)
Help fix these problems
All in multi-domain environments
These problems are all harder when multiple networks are involved
perfSONAR is provides a standard way to publish active and passive monitoring data
This data is interesting to network researchers as well as network operators
Notes: Enables Federation
  Service oriented
  Designed with ‘multi-domain’ in mind
Brings together useful tools to address different needs
  Several active and passive tools
  Interface to configure regular testing
  Diagnostic tools ready with ‘0 configuration’
Easy to install, easy to use
  ISO image can be burned to CD/USB key
  ‘Wizard’ interface for configuration
Encouraging people to deploy ‘known good’ measurement points near domain boundaries
  “known good” = hosts that are well configured, enough memory and CPU to drive the network, proper TCP tuning, clean path, etc.
Community Adoption
  Over 600 instances seen world wide as of early May
  20+ countries
  100s of domains

## Slide 25: World-Wide perfSONAR-PS Deployments: 572 bwctl nodes, 552 owamp nodes as of Jun ‘13

## Slide 26: Visualizations & Alarms – Automation is the key http://ps-dashboard.es.net

## Slide 27: One motivation for Science DMZ & perfSONAR models: Soft Network Failures
Soft failures are where basic connectivity functions, but high performance is not possible.
TCP was intentionally designed to hide all transmission errors from the user:
    “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From IEN 129, RFC 716)
Some soft failures only affect high bandwidth long RTT flows.
Hard failures are easy to detect & fix
    Soft failures can lie hidden for years!
One network problem can often mask others
Notes: Random Packet Loss
  Bad/dirty fibers or connectors
  Low light levels due to amps/interfaces failing
  Duplex mismatch
Small Router/Switch Buffers
  Switches not able to handle the long packet trains prevalent in long RTT sessions and local cross traffic at the same time
Un-intentional Rate Limiting
  Processor-based switching on routers due to faults, acl’s, or mis-configuration
  Security Devices
    E.g.: 10X improvement by turning off Cisco Reflexive ACL

## Slide 28: Affect of Broken Firewall on Traffic
© 2013 Clever Noob
© 2013 REDBUBBLE

## Slide 29: Outline
Endgame – Efficient Use of the Network to Support Science
Use Case
Expectations & Realities
Problem Definition
Solution Space
Conclusions

## Slide 30: Conclusions
Goals:
    Efficient end to end use of the network, no matter the use case (bulk data movement to video)
    ‘Happy’ users & operators
Problems:
    Network design may need work, sometimes things just break
    How to find/fix the problems that are out there
Solutions
    Architectural changes
    Adoption of new solutions
Continued Conversation:
    perfSONAR:
      http://psps.perfsonar.net
      perfsonar-node-users@internet2.edu
      https://lists.internet2.edu/sympa/info/performance-node-users
    Science DMZ:
      http://fasterdata.es.net
      sciencedmz@es.net
      https://gab.es.net/mailman/listinfo/sciencedmz

## Slide 31: A Completely Serious Overview of Network Performance for Scientific Networking
Questions?
Jason Zurawski – zurawski@es.net
http://www.es.net/
http://fasterdata.es.net/