## Slide 1: Network and Host Design to Facilitate High Performance Data Transfer
Jason Zurawski - ESnet Engineering & Outreach
engage@es.net
globusWorld 2014
April 15th 2014
With contributions from S. Balasubramanian, G. Bell, E. Dart, M. Hester, B. Johnston, A. Lake, E. Pouyoul, L. Rotman, B. Tierney and others @ ESnet

## Slide 2: Overview
Motivations
The Science DMZ Model
  Network Architecture
  Data Transfer Node Design
Application Integration
Conclusions

## Slide 3: Motivations
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors
  Data movement and data analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult
Notes: Human factors – attention span, ability to manage complexity
It is our hope that this work enables effective use of networking for science

## Slide 4
“Our unity as a nation is sustained by free communication of thought and by easy transportation of people and goods. The ceaseless flow of information throughout the Republic is matched by individual and commercial movement over a vast system of interconnected highways crisscrossing the country and joining at our national borders with friendly neighbors to the north and south.
Together, the united forces of our communication and transportation systems are dynamic elements in the very name we bear—United States. Without them, we would be a mere alliance of many separate parts.”
President Dwight D. Eisenhower - February 22, 1955

## Slide 5: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
What is important?
  Correctness
  Consistency
  Performance
Notes: If networks are so important, we need to make them useful

## Slide 6: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
© Dog Shaming 2012
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)

## Slide 7: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
7 – ESnet Science Engagement (engage@es.net) - 4/15/14
Notes: On a 10 Gb/s LAN path the impact of low packet loss rates is minimal
On a 10 Gb/s WAN path the impact of low packet loss rates is enormous
Beyond your metro area, zero loss is essentially required for performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource
This is why we do the engineering we do for data-intensive science

## Slide 8: Putting A Solution Together
Effective support for TCP-based data transfer
  Design for correct, consistent, high-performance operation
  Design for ease of troubleshooting
  Easy adoption is critical
© 2013 icanhascheezburger.com
  Large laboratories and universities have extensive IT deployments
  Drastic change is prohibitively difficult
Cybersecurity – defensible without compromising performance
Borrow ideas from traditional network security
  Traditional DMZ – separate enclave at network perimeter (“Demilitarized Zone”)
    Specific location for external-facing services
    Clean separation from internal network
  Do the same thing for science – Science DMZ

## Slide 9: Overview
Motivations
The Science DMZ Model
  Network Architecture
  Data Transfer Node Design
Application Integration
Conclusions

## Slide 10: The Science DMZ in 1 Slide
Consists of four key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with users and use cases.
  Education, Partnership, Knowledgebase
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
© 2014 Globus

## Slide 11: Science DMZ Takes Many Forms
There are a lot of ways to combine these things – it all depends on what you need to do
  Small installation for a project or two
  Facility inside a larger institution
  Institutional capability serving multiple departments/divisions
  Science capability that consumes a majority of the infrastructure
Some of these are straightforward, others are less obvious
Key point of concentration: eliminate sources of packet loss / packet friction

## Slide 12: Ad Hoc DTN Deployment
Notes: This is often what gets tried first
Data transfer node deployed where the owner has space
  This is often the easiest thing to do at the time
  Straightforward to turn on, hard to achieve performance
If present, perfSONAR is at the border
  This is a good start
  Need a second one next to the DTN
Entire LAN path has to be sized for data flows
Entire LAN path is part of any troubleshooting exercise
This usually fails to provide the necessary performance.

## Slide 13: Multiple Ingress Data Flows, Common Egress
Hosts will typically send packets at the speed of their interface (1G, 10G, etc.)
  Instantaneous rate, not average rate
  If TCP has window available and data to send, host sends until there is either no data or no window
Hosts moving big data (e.g. DTNs) can send large bursts of back-to-back packets
  This is true even if the average rate as measured over seconds is slower (e.g. 4Gbps)
  On microsecond time scales, there is often congestion
  Router or switch must queue packets or drop them

## Slide 14: Science DMZ Design Pattern (Abstract)
Notes: Dedicated enclave for resources requiring high performance over long distances

## Slide 15: Multiple Projects

## Slide 16: Supercomputer Center
Notes: High-performance networking is assumed in this environment
  Data flows between systems, between systems and storage, wide area, etc.
  Global filesystem often ties resources together
    Portions of this may not run over Ethernet (e.g. IB)
    Implications for Data Transfer Nodes
“Science DMZ” may not look like a discrete entity here
  By the time you get through interconnecting all the resources, you end up with most of the network in the Science DMZ
  This is as it should be – the point is appropriate deployment of tools, configuration, policy control, etc.
Office networks can look like an afterthought, but they aren’t
  Deployed with appropriate security controls
  Office infrastructure need not be sized for science traffic

## Slide 17: Equipment – Routers and Switches
Deep interface queues
  Output queue or VOQ – doesn’t matter
  What TCP sees is what matters – fan-in is *not* your friend
  No, this isn’t buffer bloat
    (but if you know that’s an issue for you, account for it!)
Good counters
  We like the ability to reliably count *every* packet associated with a particular flow, address pair, etc
    Very helpful for debugging packet loss
    Must not affect performance (just count it, don’t punt it)
  If the box is going to drop a packet, it should increment a counter somewhere indicating that it dropped the packet
    Magic vendor permissions and hidden commands should not be necessary
    Some boxes just lie – run away!
Single-flow performance – wire-speed

## Slide 18: Overview
Motivations
The Science DMZ Model
  Network Architecture
  Data Transfer Node Design
Application Integration
Conclusions

## Slide 19: Data Transfer Node
A DTN server is made of several subsystems. Each needs to perform optimally for the DTN workflow:
Storage: capacity, performance, reliability, physical footprint
Networking: protocol support, optimization, reliability
Motherboard: I/O paths, PCIe subsystem, IPMI
Chassis: adequate power supply, extra cooling
Note: the workflow we are optimizing for here is sequential reads/write of large files, and a moderate number of high bandwidth flows.
We assume this host is dedicated to data transfer, and not doing data analysis/manipulation
Notes: A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem
We will focus only on this workflow: while the Data Transfer Node is tuned to perform at its best for this workflow, it may perform poorly for other workflows: the DTN is a dedicated host.

## Slide 20: Motherboard/Chassis/Memory
Full 40GE requires a PCI Express gen 3 (up to 16 GB/sec) motherboard (Intel Sandy Bridge or Ivy Bridge)
    Other considerations are memory speed, number of PCI slots, extra cooling, and an adequate power supply.
    Turbo boost (up to 3.9 Ghz for the i7)
    Faster QPIC for communication between processors
We recommend 32GB of RAM for a DTN node. More is better
Be sure to get the right number of the right type of PCI slots for your needs.
    Form factor: This is the length of the slots, referred as the number of PCI lanes it can support. A 16 lane controller is twice as long as a 8 lane controller.
    Number of wired lanes: not all lanes of the slot may be wired. Some 8 lanes controller may only have 4 lanes wired.
    PCIe 2.0 is 500 MB/sec per lane. A typical host supports 8 lane (x8) cards, or up to 4 GB/sec. A high-end host might have 16 lane (x16) slots, or up to 8 GB/sec.
    PCIe 3.0 = Double the above
Notes: The motherboard not only incorporates the CPU’s and memory, it is also providing all the busses between the various component of the server. An inadequate motherboard can become a major bottleneck. It is, then, very important to correctly select it. The questions to ask while selecting are:
How many PCI cards will I need ? How many lanes each ?
What is the aggregate throughput I need on my PCI cards ?
How many cores do I need ? At what speed ?
What kind of remote access (maintenance) do I need.

## Slide 21: PCI Bus Considerations
Make sure the motherboard you select has the right number of slots with the right number of lanes for you planned usage. For example:
  10GE NICs require a 8 lane PCIe-2 slot
  40G/QDR NICs require a 8 lane PCIe-3 slot
  Most RAID controllers require 8 lane PCIe-2 slot
  A high-end Fusion IO ioDrive may require a 16 lane PCIe-3 slot
Possibilities:
SuperMicro X9DR3-F
Sample Dell Server (Poweredge r320-r720)
Sample HP Server (ProLiant DL380p gen8 High Performance model)

## Slide 22: Storage Architectures
There are multiple options for DTN Storage - this does not really impact DTN node design
Storage system
Fiber, Infiniband
Distributed file system
Infiniband, Ethernet
Local storage
Raid, SSD
DTN
Deciding what storage to use in your DTN is based on what you are optimizing for:
    performance, reliability, and capacity, and cost.
SATA disks historically have been cheaper and higher capacity, while SAS disks typically have been the fastest.
    Technologies have been converging (and its hard to keep up)
Notes: Depending on the deployment environment, a DTN may have different type of storages.
Storage Systems: Those are usually more massive systems (EMC, Netapp, DDN, etc) providing raw volumes to servers. The connectivity is usually fiber, but it can also be infiniband and even ethernet. Typically this architecture benefits storage capacity.
However, it requires, usually, a dedicated HCA and sometimes, a special software stack (OFED)
Dsitributed FileSystem: this is similar to the storage system, except that the exported volumes are not RAW but file system (PNFS, Lustre, GPFS…). This set up is typical of a tiered system: data is acquired and processed, and stored. Then the DTN read from the shared storage.
Local storage: the storage system (just a bunch of drives / JBOD) is packaged with the server. That can from 12 drivers up to 48 drives depending on vendor/model. In addition, external chassis with more drives can be added, connected to the server with SAS or FC. This is ideal for standalone servers since it does not require plumbing for the storage subsystem. However, maintenance is typically more difficult since it does not have all the tooling that usually comes with storage systems.

## Slide 23: RAID Controllers
Often optimized for a given workload, rarely for performance.
RAID0 is the fastest of all RAID levels but is also the least reliable.
The performance of the RAID controller is a factor of the number of drives and its own processing engine.
Be sure your RAID controller has the following:
>= 1GB of on-board cache
PCIe Gen3 support
dual-core RAID-on-Chip (ROC) processor if you will have more than 8 drives

## Slide 24: Network Subsystem Selection
There is a huge performance difference between cheap and expensive 10G NICs.
  E.g. please don’t cheap out on the NIC – it’s important for an optimized DTN host.
NIC features to look for include:
support for interrupt coalescing
support for MSI-X
TCP Offload Engine (TOE)
support for zero-copy protocols such as RDMA (RoCE or iWARP)
Note that many 10G and 40G NICs come in dual ports, but that does not mean if you use both ports at the same time you get double the performance. Often the second port is meant to be used as a backup port.
  True 2x10G capable cards include the Myricom 10G-PCIE2-8C2-2S and the Mellanox MCX312A-XCBT.

## Slide 25: DTN Tuning http://fasterdata.es.net/science-dmz/DTN/tuning/
Defaults are usually not appropriate for performance.
What needs to be tuned:
BIOS
Firmware
Device Drivers
Networking
File System
Application

## Slide 26: Overview
Motivations
The Science DMZ Model
  Network Architecture
  Data Transfer Node Design
Application Integration
Conclusions

## Slide 27: Sample Data Transfer Rates
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/

## Slide 28: Sample Data Transfer Results
Using the right tool is very important
Sample Results: Berkeley, CA to Argonne, IL (near Chicago). RTT = 53 ms, network capacity = 10Gbps.
    Tool Throughput
    scp: 140 Mbps
    HPN patched scp: 1.2 Gbps
    ftp 1.4 Gbps
    GridFTP, 4 streams 6.6 Gbps (disk limited)
    Note that to get more than 1 Gbps (125 MB/s) disk to disk requires RAID.

## Slide 29: Overview
Motivations
The Science DMZ Model
  Network Architecture
  Data Transfer Node Design
Application Integration
Conclusions

## Slide 30: Science DMZ Security
Goal – disentangle security policy and enforcement for science flows from security for business systems
Rationale
  Science data traffic is simple from a security perspective
  Narrow application set on Science DMZ
    Data transfer, data streaming packages
    No printers, document readers, web browsers, building control systems, financial databases, staff desktops, etc.
  Security controls that are typically implemented to protect business resources often cause performance problems
Separation allows each to be optimized

## Slide 31: http://fastdata.es.net
ESnet maintains a knowledge base of tips and tricks for obtaining maximum WAN throughput
Lots of useful stuff there, including:
  Network/TCP tuning information (in cut and paste-friendly form)
  Data Transfer Node (DTN) tuning information
  DTN reference designs
  Science DMZ information
  perfSONAR information

## Slide 32: Network and Host Design to Facilitate High Performance Data Transfer
Questions/Comments/Criticisms?
Jason Zurawski - zurawski@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net