## Slide 1: The perfSONAR Project at 10 Years: Status and Trajectory
Jason Zurawski - ESnet Engineering & Outreach
engage@es.net
GN3 (GÉANT) NA3, Task 2 - Campus Network Monitoring and Security Workshop
April 24th 2014
With contributions from S. Balasubramanian, G. Bell, E. Dart, M. Hester, B. Johnston, A. Lake, E. Pouyoul, L. Rotman, B. Tierney and others @ ESnet

## Slide 2: Overview
Introduction
The Ghost of perfSONAR Past
perfSONAR Present
Use Cases
Future Directions & Unfinished Business

## Slide 3: Overarching Motivation
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors
  Data movement and data analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult
Notes: Human factors – attention span, ability to manage complexity
It is our hope that this work enables effective use of networking for science

## Slide 4: ESnet Supports DOE Office of Science
Notes: This low-res map shows why most of our data flows terminate outside the national lab complex.
  =-=-=-=-=-=-=-=-=-
ESnet - the Energy Sciences Network - is an SC program whose primary mission is to enable the large-scale science of the Office of Science that depends on:
  Multi-institution, world-wide collaboration
  Data mobility: sharing of massive amounts of data
  Distributed data management and processing
  Distributed simulation, visualization, and computational steering
  Collaboration with the US and International Research and Education community
  =-=-=-=-=-=-=-=-=-
ESnet connects the Office of Science National Laboratories and user facilities to each other and to collaborators worldwide
Ames, Argonne, Brookhaven, Fermilab, Lawrence Berkeley, Oak Ridge, Pacific Northwest, Princeton Plasma Physics, SLAC, and Thomas Jefferson National Accelerator Facility,

## Slide 5: ESnet’s Vision
    Scientific progress is completely unconstrained by the physical location of instruments, people, computational resources, or data.

## Slide 6: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
What is important?
  Correctness
  Consistency
  Performance
Notes: If networks are so important, we need to make them useful

## Slide 7: Sample Data Transfer Rates
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/

## Slide 8: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
© 2013 icanhascheezburger.com

## Slide 9: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
9 – ESnet Science Engagement (engage@es.net) - 4/21/14
Notes: On a 10 Gb/s LAN path the impact of low packet loss rates is minimal
On a 10 Gb/s WAN path the impact of low packet loss rates is enormous
Beyond your metro area, zero loss is essentially required for performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource
This is why we do the engineering we do for data-intensive science

## Slide 10: Where Are The Problems?
Source
Campus
Backbone
S
NREN
Congested or faulty links between domains
Congested intra- campus links
D
Destination
Campus
Latency dependant problems inside domains with small RTT
Regional

## Slide 11: Local Testing Will Not Find Everything
Source
Campus
R&E
Backbone
Regional
D
S
Destination
Campus
Regional
Performance is good when RTT is < ~10 ms
Performance is poor when RTT exceeds ~10 ms
Switch with small buffers

## Slide 12: Soft Network Failures
Soft failures are where basic connectivity functions, but high performance is not possible.
TCP was intentionally designed to hide all transmission errors from the user:
  “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From IEN 129, RFC 716)
Some soft failures only affect high bandwidth long RTT flows.
Hard failures are easy to detect & fix
  soft failures can lie hidden for years!
One network problem can often mask others

## Slide 13
Use the correct tool for the Job
  To determine the correct tool, maybe we need to start with what we want to accomplish …
What do we care about measuring?
  Packet Loss, Duplication, out-of-orderness (transport layer)
  Achievable Bandwidth (e.g. “Throughput”)
  Latency (Round Trip and One Way)
  Jitter (Delay variation)
  Interface Utilization/Discards/Errors (network layer)
  Traveled Route
  MTU Feedback
The Metrics We Care about

## Slide 14: Network Monitoring
All networks do some form monitoring.
  Addresses needs of local staff for understanding state of the network
    Would this information be useful to external users?
    Can these tools function on a multi-domain basis?
Beyond passive methods, there are active tools.
    E.g. often we want a ‘throughput’ number. Can we automate that idea?
    Wouldn’t it be nice to get some sort of plot of performance over the course of a day? Week? Year? Multiple endpoints?
Where is the “Measurement Middleware”? Something to allow for the easy exchange of metrics that are collected locally, on a global scale?

## Slide 15: Overview
Introduction
The Ghost of perfSONAR Past
perfSONAR Present
Use Cases
Future Directions & Unfinished Business

## Slide 16: The Ghost of perfSONAR Past
Internet2 Performance Evaluation and Review Framework (PERF) - ~2002

## Slide 17: The Ghost of perfSONAR Past
Internet2 Performance Evaluation and Review Framework (PERF) - ~2002

## Slide 18: The Ghost of perfSONAR Past
Internet2 E2E piPEs (End-to-End Performance Initiatives Performance Environment System) ~2003/2004

## Slide 19: Problem: Nobody’s Fault
Applications
Developer
System
Administrator
LAN
Administrator
Campus
Networking
Gigapop
Gigapop
Backbone
Campus
Networking
LAN
Administrator
System
Administrator
Applications
Developer
How do you solve
a problem along a path?
Everyone says it is
working fine!
Hey, this is not working right!
The computer
Is working OK
Talk to the other guys
Everything is
AOK
No other
complaints
The network is lightly loaded
All the lights
are green
We don’t see
anything wrong
Looks fine
Others are
getting in ok
Not our problem
Courtesy of E. Boyd @ Internet2
Notes: No one claims that their cloud has a performance problem.
Note that a majority of the clouds are on campus

## Slide 20: The Ghost of perfSONAR Past
GEANT2/JRA1 Framework Layers (~2004)

## Slide 21: The Ghost of perfSONAR Past
Global Grid Forum (~2003)
  Hierarchy of Network Performance Characteristics
    http://www.ogf.org/documents/GFD.23.pdf
  Request Schema Requirements and Sample Implementation
  Report Schema Requirements and Sample Implementation

## Slide 22: The Ghost of perfSONAR Past
~2004/2005
    Merging the efforts of GGF/OGF, Internet2 E2E piPES, GN2/JRA1
      “SONAR”: You could call it piPEs v2.0 (if you’re American) or GFD (if you’re European)
      A Services-Based Measurement Framework for Building Dynamic, Self-Organizing Performance Communities
    Added additional partners from ESnet and RNP
    First release in ~2005
    pS/MDM Offerings in ~2007
    pS Performance Toolkit ~2009
    ~1000 Deployed Instances ~2013

## Slide 23: Overview
Introduction
The Ghost of perfSONAR Past
perfSONAR Present
Use Cases
Future Directions & Unfinished Business

## Slide 24: What is perfSONAR?
perfSONAR is a tool to:
Set network performance expectations
Find network problems (“soft failures”)
Help fix these problems
All in multi-domain environments
These problems are all harder when multiple networks are involved
perfSONAR is provides a standard way to publish active and passive monitoring data
  This data is interesting to network researchers as well as network operators
Notes: Enables Federation
  Service oriented
  Designed with ‘multi-domain’ in mind
Brings together useful tools to address different needs
  Several active and passive tools
  Interface to configure regular testing
  Diagnostic tools ready with ‘0 configuration’
Easy to install, easy to use
  ISO image can be burned to CD/USB key
  ‘Wizard’ interface for configuration
Encouraging people to deploy ‘known good’ measurement points near domain boundaries
  “known good” = hosts that are well configured, enough memory and CPU to drive the network, proper TCP tuning, clean path, etc.
Community Adoption
  Over 600 instances seen world wide as of early May
  20+ countries
  100s of domains

## Slide 25: perfSONAR Toolkit
The “perfSONAR Toolkit” is an open source implementation and packaging of the perfSONAR measurement infrastructure and protocols from ESnet and Internet2
http://psps.perfsonar.net
All components are available as RPMs, and bundled into a CentOS 6-based “netinstall” and a “Live CD”
  perfSONAR tools are much more accurate if run on a dedicated perfSONAR host, not on the DTN
Very easy to install and configure
  Usually takes less than 30 minutes

## Slide 26: perfSONAR Toolkit Services
PS-Toolkit includes these measurement tools:
  BWCTL: network throughput
  OWAMP: network loss, delay, and jitter
  traceroute
Test scheduler:
  runs bwctl, traceroute, and owamp tests on a regular interval
Measurement Archives (data publication)
  SNMP MA – router interface Data
  pSB MA -- results of bwctl, owamp, and traceroute tests
Lookup Service: used to find services
PS-Toolkit includes these web100-based Troubleshooting Tools
  NDT (TCP analysis, duplex mismatch, etc.)
  NPAD (TCP analysis, router queuing analysis, etc)

## Slide 27: perfSONAR Present

## Slide 28: Lookup Service Directory Search: http://stats.es.net/ServicesDirectory/

## Slide 29
perfSONAR Dashboard: http://ps-dashboard.es.net

## Slide 30: Overview
Introduction
The Ghost of perfSONAR Past
perfSONAR Present
Use Cases
Future Directions & Unfinished Business

## Slide 31: Congestion – via OWAMP Loss

## Slide 32: Soft Routing/Interface Failures
Rebooted router with full route table
Gradual failure of optical line card
Gb/s
normal performance
degrading performance
repair
one month

## Slide 33: Failing Optics (BWCTL and Utilization)
Example taken from Internet2 backbone

## Slide 34: Firewalls
When used as a comparison tool – we can see that security devices are impacting performance
Powerful incentive to fix this in the scientific path

## Slide 35: Host Tuning
Simple example – play with the settings in /etc/sysctl.conf when running some BWCTL tests.
See if you can pick out when we raised the memory for the TCP window

## Slide 36: Overview
Introduction
The Ghost of perfSONAR Past
perfSONAR Present
Use Cases
Future Directions & Unfinished Business

## Slide 37: Future Directions & Unfinished Business
Deployment
    Installation via ISO/Live CD was the greatest catalyst for deployment. This brought measurement tools to the unsophisticated user
    What does perfSONAR on a small appliance (cubox, Intel NUC, Raspberry PI) look like, and what do we need to do to support it?
Tools
    There will always be new tools – the data abstraction supports sharing
    SDN integration? How can monitoring data be used to fundamentally change networking protocols?
Use Cases
    Designed by engineers for engineers – except when the Scientists and CEOs discovered what it can do
    Can a simple web page be made that allows a live tests between anything in the world?
    Could we get the same software used on the server, integrated into the routing device?
Adoption
    Scaling to 1000+ instances was great – how can we scale to 10000? Greater emphasis on the project means more helpers needed

## Slide 38: The perfSONAR Project at 10 Years: Status and Trajectory
Questions/Comments/Criticisms?
Jason Zurawski - zurawski@es.net
ESnet Science Engagement – engage@es.net
http://psps.perfsonar.net