## Slide 1: The Science DMZ: Network Monitoring w/ perfSONAR
An Overview in Emerging (and not) Networking Technologies
Terena Networking Conference (TNC2014)
Dublin, Ireland
May 19th 2014
Jason Zurawski, Brian Tierney, Mary Hester
ESnet Science Engagement
With contributions from S. Balasubramanian, B. Johnston, A. Lake, E. Dart, L. Rotman, E. Pouyoul and others @ ESnet

## Slide 2: Section Objectives
  Discuss Soft Network Failures
  Review the role of Network Monitoring
  Introduce perfSONAR as an end-to-end Network Monitoring Solution
  Review the Behavior of perfSONAR during Network Abnormalities
  Explore perfSONAR Deployment Options
Notes: This should not be news. The news is that there is convergence on how to support things in the network space.

## Slide 3: Overview
Part 1:
  What is ESnet?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
Part 4:
  PerfSONAR
Conclusions & Discussion

## Slide 4: The Data Transfer Superfecta: “Science DMZ” Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase

## Slide 5: Test and Measurement – Keeping the Network Clean
The wide area network, the Science DMZ, and all its systems can be functioning perfectly
Eventually something is going to break
  Networks and systems are built with many, many components
  Sometimes things just break – this is why we buy support contracts
Other problems arise as well – bugs, mistakes, whatever
We must be able to find and fix problems when they occur
Why is this so important? Because we use TCP!
Notes: Remember one of the pieces was perfSONAR?

## Slide 6: Soft Network Failures
Soft failures are where basic connectivity functions, but high performance is not possible.
TCP was intentionally designed to hide all transmission errors from the user:
  “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From IEN 129, RFC 716)
Some soft failures only affect high bandwidth long RTT flows.
Hard failures are easy to detect & fix
  soft failures can lie hidden for years!
One network problem can often mask others

## Slide 7: Congestion

## Slide 8: Design Considerations – Traffic Flow
Courtesy of Ryan Reese – UCSC/SCIPP

## Slide 9: Design Considerations – Traffic Flow
Courtesy of Ryan Reese – UCSC/SCIPP

## Slide 10: Network Monitoring
All networks do some form monitoring.
  Addresses needs of local staff for understanding state of the network
    Would this information be useful to external users?
    Can these tools function on a multi-domain basis?
Beyond passive methods, there are active tools.
    E.g. often we want a ‘throughput’ number. Can we automate that idea?
    Wouldn’t it be nice to get some sort of plot of performance over the course of a day? Week? Year? Multiple endpoints?
perfSONAR = Measurement Middleware

## Slide 11: What is perfSONAR?
perfSONAR is a tool to:
Set network performance expectations
Find network problems (“soft failures”)
Help fix these problems
All in multi-domain environments
These problems are all harder when multiple networks are involved
perfSONAR is provides a standard way to publish active and passive monitoring data
  This data is interesting to network researchers as well as network operators
Notes: Enables Federation
  Service oriented
  Designed with ‘multi-domain’ in mind
Brings together useful tools to address different needs
  Several active and passive tools
  Interface to configure regular testing
  Diagnostic tools ready with ‘0 configuration’
Easy to install, easy to use
  ISO image can be burned to CD/USB key
  ‘Wizard’ interface for configuration
Encouraging people to deploy ‘known good’ measurement points near domain boundaries
  “known good” = hosts that are well configured, enough memory and CPU to drive the network, proper TCP tuning, clean path, etc.
Community Adoption
  Over 600 instances seen world wide as of early May
  20+ countries
  100s of domains

## Slide 12: Importance of Regular Testing
We can’t wait for users to report problems and then fix them (soft failures can go unreported for years!)
Things just break sometimes
  Failing optics
  Somebody messed around in a patch panel and kinked a fiber
  Hardware goes bad
Problems that get fixed have a way of coming back
  System defaults come back after hardware/software upgrades
  New employees may not know why the previous employee set things up a certain way and back out fixes
Important to continually collect, archive, and alert on active throughput test results

## Slide 13: Success Stories
#1 Failing Optic(s)
#2 Penn State University Firewall
#3 Vanderbilt Host Tuning
#4 Office to Office Video

## Slide 14: Success Stories - #1 Failing Optic(s) ex 1
Comes in many flavors. End to end first (and using NDT to start)
Vanderbilt University to PIC (Spain). Multi-domain International path. End to end and end to US Demarcation at Internet2/GEANT results:
Vanderbilt (client) -> PIC (server)
      running 10s outbound test (client to server) . . . . . 522.24 Mb/s
      running 10s inbound test (server to client) . . . . . . 169.89 kb/s
Vanderbilt (client) -> WASH (server)
      running 10s outbound test (client to server) . . . . . 922.47 Mb/s
      running 10s inbound test (server to client) . . . . . . 1.35 Mb/s
Vanderbilt to where it demarcates with Internet2 w/ SOX
Vanderbilt (client) -> ATLA (server)
      running 10s outbound test (client to server) . . . . . 935.98 Mb/s
      running 10s inbound test (server to client) . . . . . . 933.82 Mb/s

## Slide 15: Success Stories - #1 Failing Optic(s) ex 1
Graphically:

## Slide 16: Success Stories - #1 Failing Optic(s) ex 1
OWAMP shows us lots and lots of loss – applications are suffering (note SNMP was not showing these drops @ Layer 3)

## Slide 17: Success Stories - #1 Failing Optic(s) ex 1
Utilization and BW return after swap:

## Slide 18: Success Stories - #1 Failing Optic(s) ex 2
Second example – another one featuring a backbone
    Similar to frog boiling, hard alarms don’t notice gradual failure
Gb/s
normal performance
degrading performance
repair
one month

## Slide 19: Success Stories - #1 Failing Optic(s) ex 2
5/19/14
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Throughput vs. increasing latency on a 10Gb/s link with 0.0046% packet loss

## Slide 20: Success Stories - #2 PSU
PSU = Firewalls for some. The college of engineering has one, central IT does not

## Slide 21: Success Stories - #2 PSU
Initial Report from network users: performance poor both directions
    Outbound and inbound (normal issue is inbound through protection mechanisms)
From previous diagram – CoE firewalll was tested
    Machine outside/inside of firewall. Test to point 10ms away (Internet2 Washington)
Note: no retransmissions. Contrast this with the earlier example @ Brown
jzurawski@ssstatecollege:~> nuttcp -T 30 -i 1 -p 5679 -P 5678 64.57.16.22
5.8125 MB / 1.00 sec = 48.7565 Mbps 0 retrans
6.1875 MB / 1.00 sec = 51.8886 Mbps 0 retrans
…
6.1250 MB / 1.00 sec = 51.3957 Mbps 0 retrans
6.1250 MB / 1.00 sec = 51.3927 Mbps 0 retrans
184.3515 MB / 30.17 sec = 51.2573 Mbps 0 %TX 1 %RX 0 retrans 9.85 msRTT

## Slide 22: Success Stories - #2 PSU
Observation: net.ipv4.tcp_window_scaling did not seem to be working
    64K of buffer is default. Over a 10ms path, this means we can hope to see only 50Mbps of throughput:
    BDP (50 Mbit/sec, 10.0 ms) = 0.06 Mbyte
Implication: something in the path was not respecting the specification in RFC 1323, and was not allowing TCP window to grow
    TCP window of 64 KByte and RTT of 1.0 ms <= 500.00 Mbit/sec.
    TCP window of 64 KByte and RTT of 5.0 ms <= 100.00 Mbit/sec.
    TCP window of 64 KByte and RTT of 10.0 ms <= 50.00 Mbit/sec.
    TCP window of 64 KByte and RTT of 50.0 ms <= 10.00 Mbit/sec.
Reading documentation for firewall:
    TCP flow sequence checking was enabled
    What would happen if this was turn off (both directions?

## Slide 23: Success Stories - #2 PSU
jzurawski@ssstatecollege:~> nuttcp -T 30 -i 1 -p 5679 -P 5678 64.57.16.22
55.6875 MB / 1.00 sec = 467.0481 Mbps 0 retrans
74.3750 MB / 1.00 sec = 623.5704 Mbps 0 retrans
87.4375 MB / 1.00 sec = 733.4004 Mbps 0 retrans
…
91.7500 MB / 1.00 sec = 770.0544 Mbps 0 retrans
88.6875 MB / 1.00 sec = 743.5676 Mbps 28 retrans
69.0625 MB / 1.00 sec = 578.9509 Mbps 0 retrans
2300.8495 MB / 30.17 sec = 639.7338 Mbps 4 %TX 17 %RX 730 retrans 9.88 msRTT

## Slide 24: Success Stories - #2 PSU
Was this impacting people – oh yes it was:

## Slide 25: Success Stories - #3 Vanderbilt
Simple example – play with the settings in /etc/sysctl.conf when running some BWCTL tests.
See if you can pick out when we raised the memory for the TCP window

## Slide 26: Success Stories - #4 Office to Office Video
Report: Video between two offices started to degrade.
Symptoms: Poor quality between 2 of the 4 offices (others were not showing problem
Measurement and Monitoring: perfSONAR Dashboard established between facilities already:

## Slide 27: Success Stories - #4 Office to Office Video
Closer look @ packet loss:
Notes:   Opened ticket with Connecticut Education Network (CEN), ISP for one of the offices
  Initiated perfSONAR tests to their instance
    Testing showed similar lost pattern between CEN and other Internet2 Offices and PoPs
    Upstream ticket opened by CEN with Northern Crossroads (NOX)
  NOX started troubleshooting without perfSONAR, as they did not have a server available, using a tool called MTR. This tool did not reveal any loss.
    Using the perfSONAR Information Services Interface a suitable node was found on the campus of MIT.
    Additional troubleshooting using this resource showed similar loss patterns for the path to the New York peering with Internet2.
  Isolated the report into 3 possible causes:
    Dirty Fiber
    Ciena Line Card Replacement
    Brocade Line Card Replacement

## Slide 28: Success Stories
Key Message(s):
The monitoring infrastructure is sensitive for a reason – so that it finds the problems in all layers of the OSI stack.
End-to-end Video transmission (or just about any other use case) suffers because of a problems that may be unseen or not understood.
Understanding comes from learning to use the tools, learning to trust them, and having universal availability.
Comprehensive solutions will save time in the end – and perfSONAR is that solution

## Slide 29
perfSONAR Dashboard: http://ps-dashboard.es.net

## Slide 30: Regular perfSONAR Tests
We run regular tests to check for two things
  TCP throughput
  One way delay and packet loss
perfSONAR has mechanisms for managing regular testing between perfSONAR hosts
  Statistics collection and archiving
  Graphs
  Dashboard display
  Integrate with NAGIOS
This infrastructure is deployed now – perfSONAR hosts at facilities can take advantage of it
At-a-glance health check for data infrastructure

## Slide 31: Develop a Test Plan
What are you going to measure?
  Achievable bandwidth
    2-3 regional destinations
    4-8 important collaborators
    4-8 (more if you are willing, especially to start) times per day to each destination
    20-30 second tests within a region, longer across oceans and continents
  Loss/Availability/Latency
    OWAMP: ~10-20 collaborators over diverse paths
  Interface Utilization & Errors (via SNMP)

## Slide 32: Host Considerations
http://psps.perfsonar.net/toolkit/hardware.html
Dedicated perfSONAR hardware is best
  Server class is a good choice
  Desktop/Laptop/Mini (Mac, Shuttle) can be problematic, but work in a diagnostic capacity
  Other applications will perturb results
Separate hosts for throughput tests and latency/loss tests is preferred
  Throughput tests can cause increased latency and loss
  Latency tests on a throughput host are still useful however
1Gbps vs 10Gbps testers
  There are a number of problem that only show up at speeds above 1Gbps
Virtual Machines do not always work well as perfSONAR hosts (use specific)
  Clock sync issues are a bit of a factor
  throughput is reduced significantly for 10G hosts
  VM technology and motherboard technology has come a long way, YMMV
  NDT/NAGIOS/SNMP/1G BWCTL are good choices for a VM, OWAMP/10G BWCTL are not

## Slide 33: perfSONAR Deployment Locations
Critical to deploy such that you can test with useful semantics
perfSONAR hosts allow parts of the path to be tested separately
  Reduced visibility for devices between perfSONAR hosts
  Must rely on counters or other means where perfSONAR can’t go
Effective test methodology derived from protocol behavior
  TCP suffers much more from packet loss as latency increases
  TCP is more likely to cause loss as latency increases
  Testing should leverage this in two ways
    Design tests so that they are likely to fail if there is a problem
    Mimic the behavior of production traffic as much as possible
  Note: don’t design your tests to succeed
    The point is not to “be green” even if there are problems
    The point is to find problems when they come up so that the problems are fixed quickly
Notes: A lot of people want to prove that they are not the problem, and design their tests to succeed. This is not helpful.

## Slide 34: Sample Site Deployment

## Slide 35: The Science DMZ: Network Monitoring w/ perfSONAR
Questions?
Jason Zurawski - zurawski@es.net
Brian Tierney – bltierney@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net