## Slide 1: Science DMZ: Conclusion & Discussion
An Overview in Emerging (and not) Networking Technologies
Terena Networking Conference (TNC2014)
Dublin, Ireland
May 19th 2014
Jason Zurawski, Brian Tierney, Mary Hester
ESnet Science Engagement
With contributions from S. Balasubramanian, B. Johnston, A. Lake, E. Dart, L. Rotman, E. Pouyoul and others @ ESnet

## Slide 2: Section Objectives
  Summarize Technical Objectives
  Discuss the Role of Scientific Engagement
  Review Success Stories that Feature each Science DMZ Component
Notes: This should not be news. The news is that there is convergence on how to support things in the network space.

## Slide 3: Overview
Part 1:
  What is ESnet?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
Part 4:
  PerfSONAR
Conclusions & Discussion

## Slide 4: The Data Transfer Superfecta: “Science DMZ” Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Engagement with Network Users
Dedicated Systems for Data Transfer
perfSONAR
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase

## Slide 5: The Capability Gap
“It is estimated that the transfer of multiple terabytes of output to a Core Data Node would take much longer via the internet (by means of normal network hardware and conduits) than via physical disks, which is why the data will usually be transferred using portable hard disks. ”
CMIP5 Data Submission website (Climate)
http://cmip-pcmdi.llnl.gov/cmip5/submit.html
Excerpt from a recent email between an ALS Beamline Scientist and ESnet Engagement describing a particular university user’s perceptions:
From the user:
"So, my question is, do you think that I need to set up my computer for [data transfer] if we are downloading our data and then doing all of our work on our local machines? I am so pressed for time that I do not want to go through that whole process if we only need it for a day or so . . . .”
From the beamline scientist:
“This user is in the Bay Area, and has spent many days in the past making special trips up [to LBNL] to the beamline to copy data, so the person knows what a pain that is. But apparently that pain is perceived by that user as preferable to the pain of setting up [data transfer].”
Notes: Data increases lead to challenges
    Data sets increasing beyond capacity of portable media
    Portable media has worked for generations – significant upheaval in workflow
Most don’t have success using the network or don’t know how
Not scalable (technically or financially) to support data growth
Not useful, there is a better way
Climate Coupled Model Intercomparison Project
PCMBI

## Slide 6: Challenges to Network Adoption
Networks are large and complicated and the causes of performance issues are complicated for users
User’s performance expectations are low (“The network is too slow”, “I tried it and it didn’t work”).
Cultural change is hard (“we’ve always shipped disks!”).
Scientists want to do science not IT support
Notes: It’s the network stupid, except when its not
psychological
100s of people in LHC were there to set up and configure, fix everything
Technology becomes a barrier to the science – logging in twice to Globus Online
Smaller collaboration – 1-2 people, between buying an IT person or a grad student, go with grad student

## Slide 7: ESnet’s Vision
    Collaborations at every scale, in every domain, will have the information and tools they need to achieve maximum benefit from global networks.
    Scientific progress is completely unconstrained by the physical location of instruments, people, computational resources, or data.

## Slide 8: Understanding Data Trends
Notes: Requirements workshops for all six program offices within the DOE office of Science

## Slide 9
Success Stories: Science Workflow Consultation
Notes: X-ray tomography beamline
General purpose network
Windows shares on an old computer with not enough storage
Data acquisition uses LabView
Data written to shared drive on firewalled Windows server
Analysis done on workstations
  High-powered Windows hosts
  Mix of proprietary and open-source tools
  Scientists can be physically present or use Remote Desktop
Data export post-analysis – physical transport of portable media
  USB hard drives

## Slide 10: Improved Workflow Infrastructure
Notes: Dedicated infrastructure, built for performance, outside the general purpose network, clear path to NERSC
Data acquisition uses LabView
Data written to SAMBA share on beamline Linux DTN
  Writing via SAMBA is faster than local disk on acquisition computer
  Data are TIFF files ~10MB each, ~1000 files per data set
  Current max performance is ~200MB/sec
Automated workflow pushes data to NERSC for analysis
  Workflow managed using signal files
  Data set is rolled up into an HDF5 file
  Python scripts drive Globus Online CLI
  Data transferred to NERSC DTNs at ~300MB/sec
Analysis results pulled back to beamline DTN
  Additional analysis done on workstations (still use some proprietary tools)
  Primary data export is via Globus Online from beamline DTN

## Slide 11: User Workflow: Beamline 8.3.2
Users
Publications
1. Allocation
2. Endstation
3. Sample
4. Control Software
5. Data Collection
6. Data Transfer / Management
7. Data Processing
9. Write and edit
8. Data Analysis / Info Extraction / Visualization / Simulation

## Slide 12: SLAC / LCLS NERSC (http://my.es.net)
All NERSC Traffic
PS II Study

## Slide 13: Science DMZ: Conclusion & Discussion
Questions?
Jason Zurawski - zurawski@es.net
Brian Tierney – bltierney@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net