## Slide 1: The Science DMZ: Architecture & Security
An Overview in Emerging (and not) Networking Technologies
Terena Networking Conference (TNC2014)
Dublin, Ireland
May 19th 2014
Jason Zurawski, Brian Tierney, Mary Hester
ESnet Science Engagement
With contributions from S. Balasubramanian, B. Johnston, A. Lake, E. Dart, L. Rotman, E. Pouyoul and others @ ESnet

## Slide 2: Section Objectives
  Learn about Scientific Network Drivers
  Explore Barriers to Scientific Network Use
  Introduce the Science DMZ Design Paradigm
  Experiment with Network Architectural Considerations
  Discuss the Impacts of Enterprise Network Security on Scientific Workflows
  Evaluate Alternative Network Security Approaches
Notes: This should not be news. The news is that there is convergence on how to support things in the network space.

## Slide 3: What is there to worry about?
© Owen Humphreys/National Geographic Traveler Photo Contest 2013
Genomics
  Sequencer data volume increasing 12x over the next 3 years
  Sequencer cost decreasing by 10x over same time period
High Energy Physics
  LHC experiments produce & distribute petabytes of data/year
  Peak data rates increase 3-5x over 5 years
Light Sources
  Many detectors on a Moore’s Law curve
  Data volumes rendering previous operational models obsolete
Common Threads
  Increased capability, greater need for data mobility due to span/depth of collaboration space
  Global is the new local. Research is no longer done within a domain. End to end involves many fiefdoms to cross – and yes this becomes your problem when your users are impacted
Notes: This should not be news. The news is that there is convergence on how to support things in the network space.

## Slide 4: Overview
Part 1:
  What is ESnet?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
Part 4:
  PerfSONAR
Conclusions & Discussion

## Slide 5: ESnet Supports DOE Office of Science
Notes: This low-res map shows why most of our data flows terminate outside the national lab complex.
  =-=-=-=-=-=-=-=-=-
ESnet - the Energy Sciences Network - is an SC program whose primary mission is to enable the large-scale science of the Office of Science that depends on:
  Multi-institution, world-wide collaboration
  Data mobility: sharing of massive amounts of data
  Distributed data management and processing
  Distributed simulation, visualization, and computational steering
  Collaboration with the US and International Research and Education community
  =-=-=-=-=-=-=-=-=-
ESnet connects the Office of Science National Laboratories and user facilities to each other and to collaborators worldwide
Ames, Argonne, Brookhaven, Fermilab, Lawrence Berkeley, Oak Ridge, Pacific Northwest, Princeton Plasma Physics, SLAC, and Thomas Jefferson National Accelerator Facility,

## Slide 6: Wide Area Network is Engineered for Elephants

## Slide 7
Physical pipe that leaks water at rate of .0046% by volume.


Network ‘pipe’ that drops packets at rate of .0046%.


Result
100% of data transferred, slowly, at <<5% optimal speed.
Elephant Flows Place Great Demands on Networks
Result 99.9954% of water transferred.
essentially fixed
determined by speed of light
Through heroic engineering, we can minimize packet loss.
Assumptions: 10Gbps TCP flow, 80ms RTT.
See Eli Dart, Lauren Rotman, Brian Tierney, Mary Hester, and Jason Zurawski. The Science DMZ: A Network Design Pattern for Data-Intensive Science. In Proceedings of the IEEE/ACM Annual SuperComputing Conference (SC13), Denver CO, 2013.
Notes: It turns out a network has to be almost perfect in order to move the elephant flows effectively.
This is a little bit counterintuitive.
We have to take special care in engineering for the elephant flows.
Irony: van jacobsen 1986 – 88.

## Slide 8: Time to Raise Your Network Expectations: Time to Copy 1 Terabyte
On a…
    10 Mbps network: 300 hrs (12.5 days)
    100 Mbps network: 30 hrs
    1 Gbps network: 3 hrs (are your disks fast enough?)
    10 Gbps network: 20 minutes (need really fast disks and filesystems)
  These figures assume some headroom left for other users
    Compare these speeds to:
      USB 2.0 portable disk
        20-30 hours to load 1 Terabyte
© 2013 FedEx
© 2013 Western Digital
See Also: http://what-if.xkcd.com/31/

## Slide 9: Sample Data Transfer Rates
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/

## Slide 10: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is important?
  Correctness
  Consistency
  Performance
© Dog Shaming 2012
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
Notes: If networks are so important, we need to make them useful

## Slide 11: Which leads us to the Science DMZ…
Significant commonality in issues encountered with science collaborations … and similar solution set
  The causes of poor data transfer performance fit into a few categories with similar solutions
    Un-tuned/under-powered hosts
    Packet loss issues
    Security devices
  A successful model has emerged – the Science DMZ
    This model successfully in use by CMS/ATLAS, ESG, NERSC, ORNL, ALS, and others
The Science DMZ is a design pattern for network performance.
  Not all implementations look the same, but share common features
  Some choices don’t make sense for everyone – Know Your Network

## Slide 12: The Science DMZ in 1 Slide
Consists of four key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with users on the nature of their scientific workflows and use cases
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
© 2013 Globus

## Slide 13: Overview
Part 1:
  What is ESnet?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
Part 4:
  PerfSONAR
Conclusions & Discussion

## Slide 14: Science DMZ Background
The data mobility performance requirements for data intensive science are beyond what can typically be achieved using traditional methods
  Default host configurations (TCP, filesystems, NICs)
  Converged network architectures designed for commodity traffic
  Conventional security tools and policies
  Legacy data transfer tools (e.g. SCP)
  Wait-for-trouble-ticket operational models for network performance
The Science DMZ model describes a performance-based approach
  Dedicated infrastructure for wide-area data transfer
    Well-configured data transfer hosts with modern tools
    Capable network devices
    High-performance data path which does not traverse commodity LAN
  Proactive operational models that enable performance
    Well-deployed test and measurement tools (perfSONAR)
    Periodic testing to locate issues instead of waiting for users to complain
  Security posture well-matched to high-performance science applications
Notes: The Science DMZ model is a set of ideas – the diagrams that follow are examples.

## Slide 15: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)

## Slide 16: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Notes: On a 10 Gb/s LAN path the impact of low packet loss rates is minimal
On a 10 Gb/s WAN path the impact of low packet loss rates is enormous
Beyond your metro area, zero loss is essentially required for performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 17: How Do We Accommodate TCP?
High-performance wide area TCP flows must get loss-free service
  Sufficient bandwidth to avoid congestion
  Deep enough buffers in routers and switches to handle bursts
    Especially true for long-distance flows due to packet behavior
    No, this isn’t buffer bloat
Equally important – the infrastructure must be verifiable so that clean service can be provided
  Stuff breaks
    Hardware, software, optics, bugs, …
    How do we deal with it in a production environment?
  Must be able to prove a network device or path is functioning correctly
    Regular active tests should be run - perfSONAR
  Small footprint is a huge win
    Fewer the number of devices = easier to locate the source of packet loss

## Slide 18: Overview
Part 1:
  What is ESnet?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
Part 4:
  PerfSONAR
Conclusions & Discussion

## Slide 19: Traditional Network DMZ
DMZ – “Demilitarized Zone”
  Network segment near the site perimeter with different security policy
  Commonly used architectural element for deploying WAN-facing services (e.g. email, DNS, web)
Traffic for WAN-facing services does not traverse the LAN
  WAN flows are isolated from LAN traffic
  Infrastructure for WAN services is specifically configured for WAN
Separation of security policy improves both LAN and WAN
  No conflation of security policy between LAN hosts and WAN services
  DMZ hosts provide specific services
  LAN hosts must traverse the same ACLs as WAN hosts to access DMZ
Do the same thing for science – Science DMZ

## Slide 20: The Data Transfer Superfecta: Science DMZ Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase

## Slide 21: Science DMZ Takes Many Forms
There are a lot of ways to combine these things – it all depends on what you need to do
  Small installation for a project or two
  Facility inside a larger institution
  Institutional capability serving multiple departments/divisions
  Science capability that consumes a majority of the infrastructure
Some of these are straightforward, others are less obvious
Key point of concentration: eliminate sources of packet loss / packet friction

## Slide 22: Ad Hoc DTN Deployment
Notes: DTN node deep within campus infrastructure.

## Slide 23: Legacy Method: Ad Hoc DTN Deployment
This is often what gets tried first
Data transfer node deployed where the owner has space
  This is often the easiest thing to do at the time
  Straightforward to turn on, hard to achieve performance
If lucky, perfSONAR is at the border
  This is a good start
  Need a second one next to the DTN
Entire LAN path has to be sized for data flows
Entire LAN path is part of any troubleshooting exercise
This usually fails to provide the necessary performance.
Notes: Previous slide is diagram for this; just say these things while showing previous slide

## Slide 24: Common LAN config: Multiple Ingress Data Flows, Common Egress
Hosts will typically send packets at the speed of their interface (1G, 10G, etc.)
  Instantaneous rate, not average rate
  If TCP has window available and data to send, host sends until there is either no data or no window
Hosts moving big data (e.g. DTNs) can send large bursts of back-to-back packets
  This is true even if the average rate as measured over seconds is slower (e.g. 4Gbps)
  On microsecond time scales, there is often congestion
  Router or switch must queue packets or drop them

## Slide 25: Router and Switch Output Queues
Interface output queue allows the router or switch to avoid causing packet loss in cases of momentary congestion
In network devices, queue depth (or ‘buffer’) is often a function of cost
  Cheap, fixed-config LAN switches (especially in the 10G space) have inadequate buffering. Imagine a 10G ‘data center’ switch as the guilty party
  Cut-through or low-latency Ethernet switches typically have inadequate buffering (the whole point is to avoid queuing!)
Expensive, chassis-based devices are more likely to have deep enough queues
  Juniper MX and Alcatel-Lucent 7750 used in ESnet backbone
  Other vendors make such devices as well - details are important
  Thx to Jim: http://people.ucsc.edu/~warner/buffer.html
This expense is one driver for the Science DMZ architecture – only deploy the expensive features where necessary

## Slide 26: Prototype Science DMZ Data Path

## Slide 27: Small-scale Science DMZ Deployment
Add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners
  Add-on to production infrastructure – lower risk
Notes: This text goes with previous slide

## Slide 28: Support For Multiple Projects
Science DMZ architecture allows multiple projects to put DTNs in place
  Modular architecture
  Centralized location for data servers
This may or may not work well depending on institutional politics
  Issues such as physical security can make this a non-starter
  On the other hand, some shops already have service models in place
On balance, this can provide a cost savings – it depends
  Central support for data servers vs. carrying data flows
  How far do the data flows have to go?

## Slide 29: Multiple Projects

## Slide 30: Supercomputer Center Deployment
High-performance networking is assumed in this environment
  Data flows between systems, between systems and storage, wide area, etc.
  Global filesystem often ties resources together
    Portions of this may not run over Ethernet (e.g. IB)
    Implications for Data Transfer Nodes
“Science DMZ” may not look like a discrete entity here
  By the time you get through interconnecting all the resources, you end up with most of the network in the Science DMZ
  This is as it should be – the point is appropriate deployment of tools, configuration, policy control, etc.
Office networks can look like an afterthought, but they aren’t
  Deployed with appropriate security controls
  Office infrastructure need not be sized for science traffic

## Slide 31: Supercomputer Center Data Path

## Slide 32: Major Data Site Deployment
In some cases, large scale data service is the major driver
  Huge volumes of data – ingest, export
  Individual DTNs don’t exist here – data transfer clusters
Single-pipe deployments don’t work
  Everything is parallel
    Networks (Nx10G LAGs, soon to be Nx100G)
    Hosts – data transfer clusters, no individual DTNs
    WAN connections – multiple entry, redundant equipment
  Choke points (e.g. enterprise firewalls) cause problems

## Slide 33: Data Site – Architecture

## Slide 34: Distributed Science DMZ
Fiber-rich environment enables distributed Science DMZ
  No need to accommodate all equipment in one location
  Allows the deployment of institutional science service
WAN services arrive at the site in the normal way
Dark fiber distributes connectivity to Science DMZ services throughout the site
  Departments with their own networking groups can manage their own local Science DMZ infrastructure
  Facilities or buildings can be served without building up the business network to support those flows
Security is potentially more complex
  Remote infrastructure must be monitored
  Solutions depend on relationships with security groups

## Slide 35: Distributed Science DMZ – Dark Fiber

## Slide 36: Multiple Science DMZs – Dark Fiber

## Slide 37: Common Threads
Two common threads exist in all these examples
Accommodation of TCP
  Wide area portion of data transfers traverses purpose-built path
  High performance devices that don’t drop packets
Ability to test and verify
  When problems arise (and they always will), they can be solved if the infrastructure is built correctly
  Small device count makes it easier to find issues
  Multiple test and measurement hosts provide multiple views of the data path
    perfSONAR nodes at the site and in the WAN
    perfSONAR nodes at the remote site

## Slide 38: Network Research Project Requirements
Science DMZ model can be used to support research
Some research projects are networking research projects
  The network is both the environment and the subject of research
  Science DMZ is a good fit for several reasons
    Isolate research from production when research is in the unstable phase
    Separation of administrative control
Notes: Joe Breen Tale …

## Slide 39: Science DMZ With Separate Research Area
Notes: Research DMZ with separate connection to border router

## Slide 40: Science DMZ With Separate Research Area
Notes: Research DMZ as extension of production DMZ; can also be used to test new hardware before putting it into production.

## Slide 41: Equipment – Routers and Switches
Requirements for Science DMZ gear are different
  No need to go for the kitchen sink list of services
  A Science DMZ box only needs to do a few things, but do them well
  Support for the latest LAN integration magic with your Windows Active Directory environment is probably not super-important
  A clean architecture is important
    How fast can a single flow go?
    Are there any components that go slower than interface wire speed?
There is a temptation to go cheap
  Hey, it only needs to do a few things, right?
  You typically don’t get what you don’t pay for
    (You sometimes don’t get what you pay for either)

## Slide 42: Some Stuff We Think Is Important
Deep interface queues
  Output queue or VOQ – doesn’t matter
  What TCP sees is what matters – fan-in is *not* your friend
  No, this isn’t buffer bloat
Good counters
  We like the ability to reliably count *every* packet associated with a particular flow, address pair, etc
    Very helpful for debugging packet loss
    Must not affect performance (just count it, don’t punt it)
    sflow support if possible
  If the box is going to drop a packet, it should increment a counter somewhere indicating that it dropped the packet
    Magic vendor permissions and hidden commands should not be necessary
    Some boxes just lie – run away!
Single-flow performance should be wire-speed

## Slide 43: New Technology, New Bugs
Bugs happen.
  Data integrity (traffic forwarded, but with altered data payload)
  Packet loss
  Interface wedge
  Optics flaps
Monitoring systems are indispensable
Finding and fixing issues is sometimes hard
  Rough guess – difficulty exponent is degrees of freedom
    Vendors/platforms, administrative domains, time zones
Takeaway – don’t skimp on test gear (at least maintain your perfSONAR boxes)

## Slide 44: Summary So Far
There is no single “correct” way build a Science DMZ
  These are design patterns, not rules
It depends on things like:
  site requirements
  existing resources
  availability of dark fiber
  budget
The main point is to reduce the opportunities for packet loss, and be able to find loss if it’s present

## Slide 45: Overview
Part 1:
  What is ESnet?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
Part 4:
  PerfSONAR
Conclusions & Discussion

## Slide 46: Outline
Enterprise Firewall issues
Non-firewall security options
Touch on organizational structures

## Slide 47: Let’s Talk About Enterprise Firewalls
A firewall’s job is to enhance security by blocking activity that might compromise security
  This means that a firewall’s job is to prevent things from happening
  Traditional firewall policy doctrine dictates a default-deny policy
    Find out what business you need to do
    Block everything else
Firewalls are typically designed for commodity or enterprise environments
  This makes sense from the firewall designer’s perspective – lots of IT spending in commodity environments
  Firewall design choices are well-matched to commodity traffic profile
    High device count, high user count, high concurrent flow count
    Low per-flow bandwidth
    Highly capable inspection and analysis of business applications
Notes: Block everything else – note that this has contributed to the current circumstance where lots of applications are tunneled over protocols that can’t be blocked for business reasons

## Slide 48: Firewall Performance Example From Brown University
Notes: Note: all links 10G, perfsonar hosts only 1G.

## Slide 49
Results to host behind the firewall:
Brown University Example

## Slide 50
In front of the firewall:
Brown University Example

## Slide 51
Want more proof – lets look at a measurement tool through the firewall.
  Measurement tools emulate a well behaved application
‘Outbound’, not filtered:
  nuttcp -T 10 -i 1 -p 10200 bwctl.newy.net.internet2.edu
  92.3750 MB / 1.00 sec = 774.3069 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.2879 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.3019 Mbps 0 retrans
  111.7500 MB / 1.00 sec = 938.1606 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.3198 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.2653 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.1931 Mbps 0 retrans
  111.9375 MB / 1.00 sec = 938.4808 Mbps 0 retrans
  111.6875 MB / 1.00 sec = 937.6941 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.3610 Mbps 0 retrans
  1107.9867 MB / 10.13 sec = 917.2914 Mbps 13 %TX 11 %RX 0 retrans 8.38 msRTT
Brown University – TCP Dynamics

## Slide 52
‘Inbound’, filtered:
  nuttcp -r -T 10 -i 1 -p 10200 bwctl.newy.net.internet2.edu
  4.5625 MB / 1.00 sec = 38.1995 Mbps 13 retrans
  4.8750 MB / 1.00 sec = 40.8956 Mbps 4 retrans
  4.8750 MB / 1.00 sec = 40.8954 Mbps 6 retrans
  6.4375 MB / 1.00 sec = 54.0024 Mbps 9 retrans
  5.7500 MB / 1.00 sec = 48.2310 Mbps 8 retrans
  5.8750 MB / 1.00 sec = 49.2880 Mbps 5 retrans
  6.3125 MB / 1.00 sec = 52.9006 Mbps 3 retrans
  5.3125 MB / 1.00 sec = 44.5653 Mbps 7 retrans
  4.3125 MB / 1.00 sec = 36.2108 Mbps 7 retrans
  5.1875 MB / 1.00 sec = 43.5186 Mbps 8 retrans
  53.7519 MB / 10.07 sec = 44.7577 Mbps 0 %TX 1 %RX 70 retrans 8.29 msRTT
Through the Firewall

## Slide 53: tcptrace output: with and without a firewall
firewall
No firewall

## Slide 54: Science DMZ Security Model
Goal – disentangle security policy and enforcement for science flows from security for business systems
Rationale
  Science flows are relatively simple from a security perspective
  Narrow application set on Science DMZ
    Data transfer, data streaming packages
    No printers, document readers, web browsers, building control systems, staff desktops, etc.
  Security controls that are typically implemented to protect business resources often cause performance problems
Notes: Note that in the diagrams the security policy control mechanisms are part of the Science DMZ switch/router

## Slide 55: In Big Data Science, Performance Is a Core Requirement Too
Core information security principles
  Confidentiality, Integrity, Availability (CIA)
In data-intensive science, performance is an additional core mission requirement (CIAP)
  CIA principles are important, but if the performance isn’t there the science mission fails
  This isn’t about “how much” security you have, but how the security is implemented
  We need to be able to appropriately secure systems in a way that does not compromise performance

## Slide 56: Science DMZ Placement Outside the Enterprise Firewall
The Science DMZ resources are placed outside the enterprise firewall for performance reasons
  The meaning of this is specific – Science DMZ traffic does not traverse the firewall data plane
  This has nothing to do with whether packet filtering is part of the security enforcement toolkit
Lots of heartburn over this, especially from the perspective of a conventional firewall manager
  Lots of organizational policy directives mandating firewalls
  Firewalls are designed to protect converged enterprise networks
  Why would you put critical assets outside the firewall???
The answer is that firewalls are typically a poor fit for high-performance science applications

## Slide 57: The Ubiquitous Firewall
The workhorse device of network security – the firewall – has a poor track record in high-performance contexts
  Firewalls are typically designed to support a large number of users/devices, each with low throughput requirements
    Data intensive science typically generates a much smaller number of connections that are much higher throughput
Modern firewalls are far more than a packet filter:
• Decode certain application protocols (IDS/IPS functionality, URL filter, etc.)
• Rewrite headers (e.g. NAT)
• VPN Gateway
None of these are relevant to Science DMZ applications
Notes: Lots of problems in history - signed vs. unsigned 32-bit int bug in sequence tracking, elimination of RFC1323, others

## Slide 58: Firewalls vs Router Access Control Lists
When you ask a firewall administrator to allow data transfers through the firewall, what do they ask for?
  IP address of your host
  IP address of the remote host
  Port range
  That looks like an ACL to me – I can do that on the router!
Firewalls make expensive, low-performance ACL filters compared to the ACL capabilities are typically built into the router
  Router ACLs do not drop traffic permitted by policy, while enterprise firewalls can
Notes: Remember – we have mission requirements for high performance scientific data mobility, and business requirements for cost efficiency. A firewall mandate is an expensive solution that is a poor match for the task at hand and jeopardizes the scientific mission of the organization.

## Slide 59: Firewall Capabilities and Science Traffic
Firewalls have a lot of sophistication in an enterprise setting
  Application layer protocol analysis (HTTP, POP, MSRPC, etc.)
  Built-in VPN servers
  User awareness
Data-intensive science flows don’t match this profile
  Common case – data on filesystem A needs to be on filesystem Z
    Data transfer tool verifies credentials over an encrypted channel
    Then open a socket or set of sockets, and send data until done (1TB, 10TB, 100TB, …)
  One workflow can use 10% to 50% or more of a 10G network link
Do we have to use a firewall?

## Slide 60: Is it possible to get a enterprise firewall that can handle 10G flows?
Yes, but just barely, and it will cost around $500K.
  Will this $500K give you any added security over router ACLs?
10G host interfaces have been around for 10 years, and true 10G firewalls for only a couple years
How long will it take for there to be a true 40G firewall? Or 100G?

## Slide 61: What’s Inside Your Firewall?
“But wait – we don’t do this anymore!”
  It is true that vendors are working toward line-rate 10G firewalls, and some may even have them now
  10GE has been deployed in science environments for over 10 years
  Firewall internals have only recently started to catch up with the 10G world
  100GE is being deployed now, 40Gbps host interfaces are available now
  Firewalls are behind again
In general, IT shops want to get 5+ years out of a firewall purchase
  This often means that the firewall is years behind the technology curve
  Whatever you deploy now, that’s the hardware feature set you get
  When a new science project tries to deploy data-intensive resources, they get whatever feature set was purchased several years ago

## Slide 62: The Firewall State Table
Many firewalls use a state table to improve performance
  State table lookup is fast
  No need to process entire ruleset for every packet
  Also allows session tracking (e.g. TCP sequence numbers)
State table built dynamically
  Incoming packets are matched against the state table
  If no state table entry, go to the ruleset
  If permitted by ruleset, create state table entry
  Remove state table entry after observing connection teardown
Semantically similar to punt-and-switch model of traffic forwarding used on many older routers

## Slide 63: State Table Issues
If the state table is not pruned, it will overflow
  Not all connections close cleanly
    I shut my laptop and go to a meeting
    Software crashes happen
  Some attacks try to fill state tables
Solution: put a timer on state table entries
  When a packet matches the state table entry, update the timer
  If the timer expires, delete the state table entry
What if I just pause for a few minutes?
  This turns out to be a problem – state table timers are typically in the 5-15 minute range, while host keepalive timers are 2 hours
  If a connection pauses (e.g. to wait for a large transfer), the firewall will delete the state table entry from under it – connection hangs
  I have seen this in production environments

## Slide 64: Outline
Enterprise Firewall issues
Non-firewall security options
Touch on organizational structures

## Slide 65: Security Without Enterprise Firewalls
Data intensive science traffic interacts poorly with firewalls
Does this mean we ignore security? NO!
  We must protect our systems
  We just need to find a way to do security that does not prevent us from getting the science done
Key point – security policies and mechanisms that protect the Science DMZ should be implemented so that they do not compromise performance

## Slide 66: If Not Firewalls, Then What?
Remember – the goal is to protect systems in a way that allows the science mission to succeed
There are multiple ways to solve this – some are technical, and some are organizational/sociological
Note: this is harder than just putting up a firewall and thinking you are done
Notes: It will probably work better because the firewall isn’t doing that much for high-performance DTNs anyway

## Slide 67: Other Security Mechanisms: ACLs
Aggressive access lists
  More useful with project-specific DTNs
  If the purpose of the DTN is to exchange data with a small set of remote collaborators, the ACL is pretty easy to write
  Large-scale data distribution servers are hard to handle this way (but then, the firewall ruleset for such a service would be pretty open too)
Limitation of the application set
  One of the reasons to limit the application set in the Science DMZ is to make it easier to protect
  Keep unnecessary applications off the DTN (and watch for them anyway using a host IDS – take violations seriously)

## Slide 68: Other Security Mechanisms: Network IDS
Intrusion Detection Systems (IDS)
  One example is Bro – http://bro-ids.org/
  Bro is high-performance and battle-tested
    Bro protects several high-performance national assets
    Bro can be scaled with clustering: http://www.bro-ids.org/documentation/cluster.html
  Other IDS solutions are available also

## Slide 69: What Is Bro?
69
Packet Capture
Traffic Inspection
Attack Detection
Flexibility
Abstraction
Data Structures
Log Recording
“Domain-specific Python”
NetFlow
syslog
Flexibility
Abstraction
Data Structures

## Slide 70: The Bro Platform
70
Vulnerabilit.Mgmt
Intrusion Detection
File Analysis
Compliance Monitoring
Traffic Measure-ment
Traffic Control
Network
Programming Language
Packet Processing
Standard Library
Platform
Apps
Tap
Open Source
BSD License

## Slide 71: Bro Cluster Ecosystem
71
Tap
Bro
Internal Network
Internet
Bro Client Communication Library
Broccoli
Events
Events
State
Broccoli Ruby
Broccoli Python
(Broccoli Perl)
External Scripts
Functionality
BroControl
Control
User Interface
Output
Bro
Bro
Bro
Bro
Packets
Load-Balancer
BroControl
Control
Output
User Interface
“Workers”
“Manager”
“Frontend”

## Slide 72: Other Security Mechanisms: Host IDS
Using a Host IDS is recommended for hosts in a Science DMZ
There are several open source solutions that have been recommended:
OSSec: http://www.ossec.net/
Rkhunter: http://rkhunter.sourceforge.net (rootkit detection + FIM)
chkrootkit: http://chkrootkit.org/
Logcheck: http://logcheck.org (log monitoring)
Fail2ban: http://www.fail2ban.org/wiki/index.php/Main_Page
denyhosts: http://denyhosts.sourceforge.net/

## Slide 73: Other Security Mechanisms
Blackhole Routing to block attacks
Netflow, IPFIX, sflow, etc. can provide visibility
Openflow and SDN
  Using Openflow to control access to a network-based service seems pretty obvious
  There is clearly a hole in the ecosystem with the label “Openflow Firewall” – I really hope someone is working on this (it appears so)
  This could significantly reduce the attack surface for any authenticated network service
  This would only work if the Openflow device had a robust data plane

## Slide 74: Outline
Enterprise Firewall issues
Non-firewall security options
Touch on organizational structures

## Slide 75: Collaboration Within The Organization
All stakeholders should collaborate on Science DMZ design, policy, and enforcement
The security people have to be on board
  Remember: security people already have political cover – it’s called the firewall
  If a host gets compromised, the security officer can say they did their due diligence because there was a firewall in place
  If the deployment of a Science DMZ is going to jeopardize the job of the security officer, expect pushback
The Science DMZ is a strategic asset, and should be understood by the strategic thinkers in the organization
  Changes in security models
  Changes in operational models
  Enhanced ability to compete for funding
  Increased institutional capability – greater science output

## Slide 76: The Science DMZ: Architecture & Security
Questions?
Jason Zurawski - zurawski@es.net
Brian Tierney – bltierney@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net