## Slide 1: The Science DMZ: Data Transfer Nodes (DTNs) & Tools
An Overview in Emerging (and not) Networking Technologies
Terena Networking Conference (TNC2014)
Dublin, Ireland
May 19th 2014
Jason Zurawski, Brian Tierney, Mary Hester
ESnet Science Engagement
With contributions from S. Balasubramanian, B. Johnston, A. Lake, E. Dart, L. Rotman, E. Pouyoul and others @ ESnet

## Slide 2: Overview
Part 1:
  What is ESnet?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
Part 4:
  PerfSONAR
Conclusions & Discussion

## Slide 3: The Data Transfer Superfecta: Science DMZ Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase

## Slide 4: Data Transfer Node
A DTN server is made of several subsystems. Each needs to perform optimally for the DTN workflow:
Storage: capacity, performance, reliability, physical footprint
Networking: protocol support, optimization, reliability
Motherboard: I/O paths, PCIe subsystem, IPMI
Chassis: adequate power supply, extra cooling
Note: the workflow we are optimizing for here is sequential reads/write of large files, and a moderate number of high bandwidth flows.
We assume this host is dedicated to data transfer, and not doing data analysis/manipulation
Notes: A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem
We will focus only on this workflow: while the Data Transfer Node is tuned to perform at its best for this workflow, it may perform poorly for other workflows: the DTN is a dedicated host.

## Slide 5: Motherboard and Chassis selection
Full 40GE requires a PCI Express gen 3 (aka PCIe gen3) motherboard
  Intel Sandy Bridge or Ivy Bridge (for the most part)
Other considerations are memory speed, number of PCI slots, extra cooling, and an adequate power supply.
Intel’s Sandy/Ivy Bridge (Ivy Bridge is about 20% faster) CPU architecture provides these features, which benefit a DTN:
  PCIe Gen3 support ( up to 16 GB/sec )
  Turbo boost (up to 3.9 Ghz for the i7)
  Faster QPIC for communication between processors
Notes: The motherboard not only incorporates the CPU’s and memory, it is also providing all the busses between the various component of the server. An inadequate motherboard can become a major bottleneck. It is, then, very important to correctly select it. The questions to ask while selecting are:
How many PCI cards will I need ? How many lanes each ?
What is the aggregate throughput I need on my PCI cards ?
How many cores do I need ? At what speed ?
What kind of remote access (maintenance) do I need.

## Slide 6: Memory and PCI Slot Considerations
Memory
  We recommend 32GB of RAM for a DTN node. More is better
PCI Slots
  Be sure to get the right number of the right type of PCI slots for your needs.
  PCI slots are defined by:
    Form factor: This is the length of the slots, referred as the number of PCI lanes it can support. A 16 lane controller is twice as long as a 8 lane controller.
    Number of wired lanes: not all lanes of the slot may be wired. Some 8 lanes controller may only have 4 lanes wired.
    PCIe 2.0 is 500 MB/sec per lane. A typical host supports 8 lane (x8) cards, or up to 4 GB/sec. A high-end host might have 16 lane (x16) slots, or up to 8 GB/sec.
    PCIe 3.0 = Double the above

## Slide 7: PCI Bus Considerations
Make sure the motherboard you select has the right number of slots with the right number of lanes for you planned usage. For example:
  10GE NICs require a 8 lane PCIe-2 slot
  40G/QDR NICs require a 8 lane PCIe-3 slot
  Most RAID controllers require 8 lane PCIe-2 slot
  A high-end Fusion IO ioDrive may require a 16 lane PCIe-3 slot
Possibilities:
SuperMicro X9DR3-F
Sample Dell Server (Poweredge r320-r720)
Sample HP Server (ProLiant DL380p gen8 High Performance model)

## Slide 8: Storage Architectures
There are multiple options for DTN Storage - this does not really impact DTN node design
Storage system
Fiber, Infiniband
Distributed file system
Infiniband, Ethernet
Local storage
Raid, SSD
DTN
Notes: Depending on the deployment environment, a DTN may have different type of storages.
Storage Systems: Those are usually more massive systems (EMC, Netapp, DDN, etc) providing raw volumes to servers. The connectivity is usually fiber, but it can also be infiniband and even ethernet. Typically this architecture benefits storage capacity.
However, it requires, usually, a dedicated HCA and sometimes, a special software stack (OFED)
Dsitributed FileSystem: this is similar to the storage system, except that the exported volumes are not RAW but file system (PNFS, Lustre, GPFS…). This set up is typical of a tiered system: data is acquired and processed, and stored. Then the DTN read from the shared storage.
Local storage: the storage system (just a bunch of drives / JBOD) is packaged with the server. That can from 12 drivers up to 48 drives depending on vendor/model. In addition, external chassis with more drives can be added, connected to the server with SAS or FC. This is ideal for standalone servers since it does not require plumbing for the storage subsystem. However, maintenance is typically more difficult since it does not have all the tooling that usually comes with storage systems.

## Slide 9: Storage Subsystem Selection
Deciding what storage to use in your DTN is based on what you are optimizing for:
  performance, reliability, and capacity, and cost.
SATA disks historically have been cheaper and higher capacity, while SAS disks typically have been the fastest.
  Technologies have been converging (and its hard to keep up)

## Slide 10: SSD Storage
Notes: SSD, cost much more than HD, but a much faster. They come in different packages:
PCIe card: some vendors (Fusion I/O) build PCI cards with SSD. The current maximum capacity is 1TB per card. Since those cards are PCIe, the data transfer between the main memory and the SSD is just limited by the SSD speed and the PCIe speed: in other words, it is really fast (several GB/sec per card). The drawbacks are that 1TB uses a PCIe slot. This design often means that a PCI extender is needed, but if space and performance is an issue, this is the best solution. Those SSD cards can also be an deployment issue: replacing a failed card means that the server must be open.
- HD replacement: some vendors (IBM, WD, etc) have product that a physical replacement for HD: same form factor, same connectivity (SAS, SATA…). Thi allows for easier migration path from HD to SSD, but the performance is limited by the controller. Also, not all controllers are good at controlling SSD drives: always make sure that the controller is “SSD capable”.

## Slide 11: SSD
SSD storage costs much more than traditional hard drives (HD), but are much faster. They come in different styles:
  PCIe card: some vendors (Fusion I/O) build PCI cards with SSD.
    These are the fastest type of SSD: up to several GBytes/sec per card.
      Note that this type of SSD is typically not hot-swapable.
  HD replacement: several vendors now sell SSD-based drives that have the same form factor as traditional drives such as SAS and SATA.
    The downside to this approach is that performance is limited by the RAID controller, and not all controllers work well with SSD.
      Be sure that your RAID controller is “SSD capable”.
Note that the price of SSD is coming down quickly, so a SSD-based solution may be worth considering for your DTNs.

## Slide 12: RAID Controllers
Often optimized for a given workload, rarely for performance.
RAID0 is the fastest of all RAID levels but is also the least reliable.
The performance of the RAID controller is a factor of the number of drives and its own processing engine.

## Slide 13: RAID Controller
Be sure your RAID controller has the following:
>= 1GB of on-board cache
PCIe Gen3 support
dual-core RAID-on-Chip (ROC) processor if you will have more than 8 drives
Notes: Disk controllers, RAID or not, are usually designed for “entreprise”. This usually means that the controller is often configured with RAID 5 or 6. As a consequence, controller are most of the times, not capable of running all the drives at full speed: in enterprise context, there are always a few drives that are hot replacement. A rule of thumb is that if a controller is said to handle up to X drives, it can handle up to 2X/3 drivers at full speed.
Some high end controllers (Areca for instance) are specifically designed for a workflow similar to a DTN workflow: sequential read/write. They may have Gigabytes of SRAM for internal buffering, PCIe x16..
Finally, some RAID controller are specifically designed to scale up. In addition to wire internal drives, they can control external drives, directly or in a daisy chain manner

## Slide 14: Networking Subsystem
Notes: The networking subsystem is the second subsystem after the storage that is critical and will be a bottle neck. The choice of NIC will impact performance.

## Slide 15: Network Subsystem Selection
There is a huge performance difference between cheap and expensive 10G NICs.
  E.g. please don’t cheap out on the NIC – it’s important for an optimized DTN host.
NIC features to look for include:
support for interrupt coalescing
support for MSI-X
TCP Offload Engine (TOE)
support for zero-copy protocols such as RDMA (RoCE or iWARP)
Note that many 10G and 40G NICs come in dual ports, but that does not mean if you use both ports at the same time you get double the performance. Often the second port is meant to be used as a backup port.
  True 2x10G capable cards include the Myricom 10G-PCIE2-8C2-2S and the Mellanox MCX312A-XCBT.

## Slide 16: DTN Tuning http://fasterdata.es.net/science-dmz/DTN/tuning/
Defaults are usually not appropriate for performance.
What needs to be tuned:
BIOS
Firmware
Device Drivers
Networking
File System
Application

## Slide 17: DTN Tuning
Tuning your DTN host is extremely important. We have seen overall IO throughput of a DTN more than double with proper tuning.
Tuning can be as much art as a science. Due to differences in hardware, its hard to give concrete advice.
Here are some tuning settings that we have found do make a difference.
  This tutorial assumes you are running a Redhat-based Linux system, but other types of Unix should have similar tuning nobs.
Note that you should always use the most recent version of the OS, as performance optimizations for new hardware are added to every release.

## Slide 18: Network Tuning
# add to /etc/sysctl.conf
net.core.rmem_max = 33554432
net.core.wmem_max = 33554432
net.ipv4.tcp_rmem = 4096 87380 33554432
net.ipv4.tcp_wmem = 4096 65536 33554432
net.core.netdev_max_backlog = 250000
Add to /etc/rc.local
# increase txqueuelen
/sbin/ifconfig eth2 txqueuelen 10000
/sbin/ifconfig eth3 txqueuelen 10000
# make sure cubic and htcp are loaded
/sbin/modprobe tcp_htcp
/sbin/modprobe tcp_cubic
# set default to CC alg to htcp
net.ipv4.tcp_congestion_control=htcp
# with the Myricom 10G NIC increasing interrupt coalencing helps a lot:
/usr/sbin/ethtool -C ethN rx-usecs 75
And use Jumbo Frames!
Notes: interrupt coalencing is used to avoid flooding the host system with too many interrupts, packets are collected and one single interrupt is generated for multiple packets.
Not all NIC support it
75-100 micro-seconds timeout
Is critical for high performance NIC (10Gb, 40Gb…)

## Slide 19: BIOS Tuning
For PCI gen3-based hosts, you should
enable “turbo boost”,
disable hyperthreading and node interleaving.
More information on BIOS tuning is described in this document:
http://www.dellhpcsolutions.com/assets/pdfs/Optimal_BIOS_HPC_Dell_12G.v1.0.pdf

## Slide 20: I/O Scheduler
The default Linux scheduler is the "fair" scheduler. For a DTN node, we recommend using the "deadline" scheduler instead.
To enable deadline scheduling, add "elevator=deadline" to the end of the "kernel' line in your /boot/grub/grub.conf file, similar to this:
kernel /vmlinuz-2.6.35.7 ro root=/dev/VolGroup00/LogVol00 rhgb quiet elevator=deadline

## Slide 21: Interrupt Affinity
Interrupts are triggered by I/O cards (storage, network). High performance means lot of interrupts per seconds
Interrupt handlers are executed on a core
Depending on the scheduler, core 0 gets all the interrupts, or interrupts are dispatched in a round-robin fashion among the cores: both are bad for performance:
  Core 0 get all interrupts: with very fast I/O, the core is overwhelmed and becomes a bottleneck
  Round-robin dispatch: very likely the core that executes the interrupt handler will not have the code in its L1 cache.
  Two different I/O channels may end up on the same core.

## Slide 22: A simple solution: interrupt binding
Each interrupt is statically bound to a given core (network -> core 1, disk -> core 2)
Works well, but can become an headache and does not fully solve the problem: one very fast card can still overwhelm the core.
Needs to bind application to the same cores for best optimization: what about multi-threaded applications, for which we want one thread = one core ?

## Slide 23: Intel Sandy/Ivy Bridge
Notes: Note: get much better performance if you avoid crossing the QPI.

## Slide 24: Core selection matters! (iperf3 –A N,N option)
Protocol | 40G NIC | “good” core | “bad” core
TCP | Mellanox Chelsio | 37 Gbps 39.5 Gbps | 26 Gbps 5 Gbps
UDP | Mellanox Chelsio | 21 Gbps 22 Gbps | 16 Gbps 16 Gbps
IRQ binding bootscripts
Mellanox: /usr/sbin/set_irq_affinity_bynode.sh 1 ethN
Chelsio: /sbin/t4_perftune.sh
Notes: Tests run on ESnet testbed, all hosts at NERSC, latency = .1ms.
UDP command: iperf3 -c 10.2.2.2 -u –b35g -A9,9 –l8972 –w4m -R
OS = CentOS 6.5, latest drivers from Mellanox/Chelsio web sites (April 2014)

## Slide 25: File System Tuning
We recommend using the ext4 file system in Linux for DTN nodes.
Increasing the amount of "readahead" usually helps on DTN nodes where the workflow is mostly sequential reads.
  However you should test this, as some RAID controllers do this already, and changing this may have adverse affects.
Setting readahead should be done at system boot time. For example, add something like this to /etc/rc.local:
/sbin/blockdev --setra 262144 /dev/sdb
More information on readahead:
http://www.kernel.org/doc/ols/2004/ols2004v2-pages-105-116.pdf

## Slide 26: EXT4 Tuning
The file system should be tuned to the physical layout of the drives.
  Stride and stripe-width are used to align the volume according to the stripe-size of the RAID.
    stride is calculated as Stripe Size / Block Size.
    stripe-width is calculated as Stride * Number of Disks Providing Capacity.
Disabling journaling will also improve performance, but reduces reliability.
Sample mkfs command:
/sbin/mkfs.ext4 /dev/sdb1 –b 4096 –E stride=64 \ stripe-width=768 –O ^has_journal

## Slide 27: File System Tuning (cont.)
There are also tuning settings that are done at mount time. Here are the ones that we have found improve DTN performance:
  data=writeback
    this option forces ext4 to use journaling only for metadata. This gives a huge improvement in write performance
  inode_readahead_blks=64
    this specifies the number of inode blocks to be read ahead by ext4’s readahead algorithm. Default is 32.
  Commit=300
    this parameter tells ext4 to sync its metadata and data every 300s. This reduces the reliability of data writes, but increases performance.
  noatime,nodiratime
    these parameters tells ext4 not to write the file and directory access timestamps.
Sample fstab entry:
/dev/sdb1 /storage/data1 ext4 inode_readahead_blks=64,data=writeback,barrier=0,commit=300,noatime,nodiratime
For more info see: http://kernel.org/doc/Documentation/filesystems/ext4.txt

## Slide 28: RAID Controller
Different RAID controllers provide different tuning controls. Check the documentation for your controller and use the settings recommended to optimize for large file reading.
  You will usually want to disable any “smart” controller built-in options, as they are typically designed for different workflows.
Here are some settings that we found increase performance on a 3ware RAID controller. These settings are in the BIOS, and can be entered by pressing Alt+3 when the system boots up.
Write cache – Enabled
Read cache – Enabled
Continue on Error – Disabled
Drive Queuing – Enabled
StorSave Profile – Performance
Auto-verify – Disabled
Rapid RAID recovery – Disabled

## Slide 29: Virtual memory Subsystem
Setting dirty_background_bytes and dirty_bytes improves write performance.
For our system, the settings that gave best performance was:
  echo 1000000000 > /proc/sys/vm/dirty_bytes
  echo 1000000000 > /proc/sys/vm/dirty_background_bytes
For more information see:
http://www.kernel.org/doc/Documentation/sysctl/vm.txt

## Slide 30: SSD Issues
Tuning your SSD is more about reliability and longevity than performance, as each flash memory cell has a finite lifespan that is determined by the number of "program and erase (P/E)" cycles. Without proper tuning, SSD can die within months.
  never do "write" benchmarks on SSD: this will damage your SSD quickly.
Modern SSD drives and modern OSes should all includes TRIM support, which is important to prolong the live of your SSD. Only the newest RAID controllers include TRIM support (late 2012).
Swap
To prolong SSD lifespan, do not swap on an SSD. In Linux you can control this using the sysctl variable vm.swappiness. E.g.: add this to /etc/sysctl.conf:
    vm.swappiness=1
This tells the kernel to avoid unmapping mapped pages whenever possible.
Avoid frequent re-writing of files (for example during compiling code from source), use a ramdisk file system (tmpfs) for /tmp /usr/tmp, etc.

## Slide 31: ext4 file system tuning for SSD
These mount flags should be used for SSD partitions.
  noatime: Reading accesses to the file system will no longer result in an update to the atime information associated with the file. This eliminates the need for the system to make writes to the file system for files which are simply being read.
  discard: This enables the benefits of the TRIM command as long for kernel version >=2.6.33.
Sample /etc/fstab entry:
/dev/sda1 /home/data ext4 defaults,noatime,discard 0 1
For more information see:
http://wiki.archlinux.org/index.php/Solid_State_Drives

## Slide 32: Benchmarking
Simulating a single thread writing sequentially a file can be done using dd as:
$ dd if=/dev/zero of=/storage/data1/file1 bs=4k count=33554432
Simulating sequentially reading a file is done by:
$ dd if=/storage/data1/file1 of=/dev/null bs=4k

## Slide 33: Overview
Part 1:
  What is ESnet?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
Part 4:
  PerfSONAR
Conclusions & Discussion

## Slide 34: Sample Data Transfer Results
Using the right tool is very important
Sample Results: Berkeley, CA to Argonne, IL (near Chicago). RTT = 53 ms, network capacity = 10Gbps.
    Tool Throughput
    scp: 140 Mbps
    HPN patched scp: 1.2 Gbps
    ftp 1.4 Gbps
    GridFTP, 4 streams 6.6 Gbps (disk limited)
    Note that to get more than 1 Gbps (125 MB/s) disk to disk requires RAID.

## Slide 35: Data Transfer Tools
Parallelism is key
  It is much easier to achieve a given performance level with four parallel connections than one connection
  Several tools offer parallel transfers
Latency interaction is critical
  Wide area data transfers have much higher latency than LAN transfers
  Many tools and protocols assume a LAN
  Examples: SCP/SFTP, HPSS mover protocol

## Slide 36: Why Not Use SCP or SFTP?
Pros:
  Most scientific systems are accessed via OpenSSH
  SCP/SFTP are therefore installed by default
  Modern CPUs encrypt and decrypt well enough for small to medium scale transfers
  Credentials for system access and credentials for data transfer are the same
Cons:
  The protocol used by SCP/SFTP has a fundamental flaw that limits WAN performance
  CPU speed doesn’t matter – latency matters
  Fixed-size buffers reduce performance as latency increases
  It doesn’t matter how easy it is to use SCP and SFTP – they simply do not perform
Verdict: Do Not Use Without Performance Patches

## Slide 37: A Fix For scp/sftp
PSC has a patch set that fixes problems with SSH
  http://www.psc.edu/networking/projects/hpn-ssh/
Significant performance increase
Advantage – this helps rsync too

## Slide 38: Other Data Transfer Tools
FDT = Fast Data Transfer tool from Caltech
  http://monalisa.cern.ch/FDT/
  Java-based, easy to install
  used by CMS project and DYNES NSF Funding effort
bbcp: http://www.slac.stanford.edu/~abh/bbcp/
  supports parallel transfers and socket tuning
  bbcp -P 4 -v -w 2M myfile remotehost:filename
lftp: http://lftp.yar.ru/
  parallel file transfer, socket tuning, HTTP transfers, and more.
  lftp -e 'set net:socket-buffer 4000000; pget -n 4 [http|ftp]://site/path/file; quit'
axel: http://axel.alioth.debian.org/
  simple parallel accelerator for HTTP and FTP.
  axel -n 4 [http|ftp]://site/file

## Slide 39: Commercial Data Transfer Tools
There are several commercial UDP-based tools
  Aspera: http://www.asperasoft.com/
  Data Expedition: http://www.dataexpedition.com/
  TIXstream: http://www.tixeltec.com/tixstream_en.html
These should all do better than TCP on a lossy path
  advantage of these tools less clear on an clean path
They all have different, fairly complicated pricing models

## Slide 40: GridFTP
GridFTP from ANL has features needed to fill the network pipe
  Buffer Tuning
  Parallel Streams
Supports multiple authentication options
  Anonymous
  ssh
  X509
Ability to define a range of data ports
  helpful to get through firewalls
New Partnership with ESnet and Globus Online to support Globus Online for use in Science DMZs

## Slide 41: Globus Transfer Service
ESnet recommends Globus Transfer Service for data transfers to/from the Science DMZ
Key features needed by a Science DMZ
High Performance: parallel streams, small file optimization
Reliability: auto-restart, user-level checksum
Multiple security models: ssh key, X509, Open ID, Shibboleth, etc.
Firewall/NAT traversal support
Easy to install and configure
See: http://globusworld.org/tutorial

## Slide 43: Test Globus using ESnet public DTN’s http://fasterdata.es.net/performance-testing/DTNs/

## Slide 44: Advanced Technical Topic: Speed Mismatch and packet pacing

## Slide 45: Speed Mismatch Issues
More and more often we are seeing problems sending from a faster host to a slower host
  This can look like a network problem (lots of TCP retransmits)
  The network is rarely the bottleneck anymore for many sites
This may be true for:
  10G to 1G host
  10G host to a 2G circuit
  40G to 10G host
  Fast host to slower host
Pacing at the application level does not help
The linux ‘tc’ command does help
  But only up to speeds of 8Gbps
  And perhaps this will just mask problems with under-buffered switches?
http://fasterdata.es.net/host-tuning/packet-pacing/

## Slide 46: But 10G to 1G can work just fine too….

## Slide 47: Compare tcpdumps: kans-pt1.es.net (10G) to eqx-chi-pt1.es.net (1G)

## Slide 48: Compare tcpdumps kans-pt1.es.net (10G) to uct2-net4.uchicago.edu (1G)

## Slide 49: Compare tcpdumps kans-pt1.es.net (10G) to uct2-net4.uchicago.edu (1G) with pacing

## Slide 50: The Science DMZ: Data Transfer Nodes (DTNs) & Tools
Questions?
Jason Zurawski - zurawski@es.net
Brian Tierney – bltierney@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net