## Slide 1: Science DMZ Security
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 2: Overview
Part 1:
  What is Science Engagement?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
  Globus Connect Personal
Part 4:
  perfSONAR
Part 5:
  SDN and the Science DMZ
Conclusions & Discussion

## Slide 3: The Data Transfer Superfecta: “Science DMZ” Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase

## Slide 4: Outline
Science DMZ security model
Enterprise Firewall issues
Non-firewall security options
Touch on organizational structures

## Slide 5: Performance Issues caused by Security Devices

## Slide 6: Science DMZ Security Model
Goal – disentangle security policy and enforcement for science flows from security for business systems
Rationale
  Science flows are relatively simple from a security perspective
  Narrow application set on Science DMZ
    Data transfer, data streaming packages
    No printers, document readers, web browsers, building control systems, staff desktops, etc.
  Security controls that are typically implemented to protect business resources often cause performance problems
Notes: Note that in the diagrams the security policy control mechanisms are part of the Science DMZ switch/router

## Slide 7: In Big Data Science, Performance Is a Core Requirement Too
Core information security principles
  Confidentiality, Integrity, Availability (CIA)
In data-intensive science, performance is an additional core mission requirement (CIAP)
  CIA principles are important, but if the performance isn’t there the science mission fails
  This isn’t about “how much” security you have, but how the security is implemented
  We need to be able to appropriately secure systems in a way that does not compromise performance

## Slide 8: Science DMZ Placement Outside the Enterprise Firewall
The Science DMZ resources are placed outside the enterprise firewall for performance reasons
  The meaning of this is specific – Science DMZ traffic does not traverse the firewall data plane
  This has nothing to do with whether packet filtering is part of the security enforcement toolkit
Lots of heartburn over this, especially from the perspective of a conventional firewall manager
  Lots of organizational policy directives mandating firewalls
  Firewalls are designed to protect converged enterprise networks
  Why would you put critical assets outside the firewall???
The answer is that firewalls are typically a poor fit for high-performance science applications

## Slide 9: Let’s Talk About Enterprise Firewalls
A firewall’s job is to enhance security by blocking activity that might compromise security
  This means that a firewall’s job is to prevent things from happening
  Traditional firewall policy doctrine dictates a default-deny policy
    Find out what business you need to do
    Block everything else
Firewalls are typically designed for commodity or enterprise environments
  This makes sense from the firewall designer’s perspective – lots of IT spending in commodity environments
  Firewall design choices are well-matched to commodity traffic profile
    High device count, high user count, high concurrent flow count
    Low per-flow bandwidth
    Highly capable inspection and analysis of business applications
Notes: Block everything else – note that this has contributed to the current circumstance where lots of applications are tunneled over protocols that can’t be blocked for business reasons

## Slide 10: Firewall Capabilities and Science Traffic
Firewalls have a lot of sophistication in an enterprise setting
  Application layer protocol analysis (HTTP, POP, MSRPC, etc.)
  Built-in VPN servers
  User awareness
Data-intensive science flows don’t match this profile
  Common case – data on filesystem A needs to be on filesystem Z
    Data transfer tool verifies credentials over an encrypted channel
    Then open a socket or set of sockets, and send data until done (1TB, 10TB, 100TB, …)
  One workflow can use 10% to 50% or more of a 10G network link
Do we have to use a firewall?

## Slide 11: Firewalls vs. Router Access Control Lists
When you ask a firewall administrator to allow data transfers through the firewall, what do they ask for?
  IP address of your host
  IP address of the remote host
  Port range
  That looks like an ACL to me – I can do that on the router!
Firewalls make expensive, low-performance ACL filters compared to the ACL capabilities are typically built into the router
Router ACLs do not drop traffic permitted by policy, while enterprise firewalls can (and often do)
Notes: Remember – we have mission requirements for high performance scientific data mobility, and business requirements for cost efficiency. A firewall mandate is an expensive solution that is a poor match for the task at hand and jeopardizes the scientific mission of the organization.

## Slide 12: Is it possible to get a enterprise firewall that can handle 10G flows?
Yes, but just barely, and it will cost around $500K.
  Will this $500K give you any added security over router ACLs?
  This makes sense if the features are useful, and they are often only useful for enterprise environments
10G host interfaces have been around for 10 years, and true 10G firewalls for only a couple years
How long will it take for there to be a true 40G firewall? Or 100G?

## Slide 13: Firewall Performance Example From Brown University
Notes: Note: all links 10G, perfsonar hosts only 1G.

## Slide 14
Results to host behind the firewall:
Brown University Example

## Slide 15
In front of the firewall:
Brown University Example

## Slide 16
Want more proof – lets look at a measurement tool through the firewall.
  Measurement tools emulate a well behaved application
‘Outbound’, not filtered:
  nuttcp -T 10 -i 1 -p 10200 bwctl.newy.net.internet2.edu
  92.3750 MB / 1.00 sec = 774.3069 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.2879 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.3019 Mbps 0 retrans
  111.7500 MB / 1.00 sec = 938.1606 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.3198 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.2653 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.1931 Mbps 0 retrans
  111.9375 MB / 1.00 sec = 938.4808 Mbps 0 retrans
  111.6875 MB / 1.00 sec = 937.6941 Mbps 0 retrans
  111.8750 MB / 1.00 sec = 938.3610 Mbps 0 retrans
  1107.9867 MB / 10.13 sec = 917.2914 Mbps 13 %TX 11 %RX 0 retrans 8.38 msRTT
TCP Dynamics

## Slide 17
‘Inbound’, filtered:
  nuttcp -r -T 10 -i 1 -p 10200 bwctl.newy.net.internet2.edu
  4.5625 MB / 1.00 sec = 38.1995 Mbps 13 retrans
  4.8750 MB / 1.00 sec = 40.8956 Mbps 4 retrans
  4.8750 MB / 1.00 sec = 40.8954 Mbps 6 retrans
  6.4375 MB / 1.00 sec = 54.0024 Mbps 9 retrans
  5.7500 MB / 1.00 sec = 48.2310 Mbps 8 retrans
  5.8750 MB / 1.00 sec = 49.2880 Mbps 5 retrans
  6.3125 MB / 1.00 sec = 52.9006 Mbps 3 retrans
  5.3125 MB / 1.00 sec = 44.5653 Mbps 7 retrans
  4.3125 MB / 1.00 sec = 36.2108 Mbps 7 retrans
  5.1875 MB / 1.00 sec = 43.5186 Mbps 8 retrans
  53.7519 MB / 10.07 sec = 44.7577 Mbps 0 %TX 1 %RX 70 retrans 8.29 msRTT
TCP Dynamics Through Firewall

## Slide 18: tcptrace output: with and without a firewall
firewall
No firewall

## Slide 19: Firewall Internals

## Slide 20: Thought Experiment
We’re going to do a thought experiment
Consider a network between three buildings – A, B, and C
  This is supposedly a 10Gbps network end to end (look at the links on the buildings)
  Building A houses the border router – not much goes on there except the external connectivity
  Lots of work happens in building B – so much so that the processing is done with multiple processors to spread the load in an affordable way, and aggregate the results after
  Building C is where we branch out to other buildings
Every link between buildings is 10Gbps – this is a 10Gbps network, right???

## Slide 21: Notional 10G Network Between Buildings
Notes: If you look at the inside of Building B, it is obvious from a network engineering perspective that this is not a 10Gbps network

## Slide 22: Clearly Not A 10Gbps Network
If you look at the inside of Building B, it is obvious from a network engineering perspective that this is not a 10Gbps network
  Clearly the maximum per-flow data rate is 1Gbps, not 10Gbps
  However, if you convert the buildings into network elements while keeping their internals intact, you get routers and firewalls
  What firewall did the organization buy? What’s inside it?
  Those little 1G “switches” are firewall processors
This parallel firewall architecture has been in use for years
  Slower processors are cheaper
  Typically fine for a commodity traffic load
  Therefore, this design is cost competitive and common

## Slide 23: Notional 10G Network Between Devices
Notes: This parallel firewall architecture has been in use for years
  Slower processors are cheaper
  Typically fine for a commodity traffic load
  Therefore, this design is cost competitive and common

## Slide 24: Notional Network Logical Diagram
Notes: If you’re not allowed to look inside, this is all you see

## Slide 25: What’s Inside Your Firewall?
“But wait – we don’t do this anymore!”
  It is true that vendors are working toward line-rate 10G firewalls, and some may even have them now
  10GE has been deployed in science environments for over 10 years
  Firewall internals have only recently started to catch up with the 10G world
  100GE is being deployed now, 40Gbps host interfaces are available now
  Firewalls are behind again
In general, IT shops want to get 5+ years out of a firewall purchase
  This often means that the firewall is years behind the technology curve
  Whatever you deploy now, that’s the hardware feature set you get
  When a new science project tries to deploy data-intensive resources, they get whatever feature set was purchased several years ago

## Slide 26: The Firewall State Table
Many firewalls use a state table to improve performance
  State table lookup is fast
  No need to process entire ruleset for every packet
  Also allows session tracking (e.g. TCP sequence numbers)
State table built dynamically
  Incoming packets are matched against the state table
  If no state table entry, go to the ruleset
  If permitted by ruleset, create state table entry
  Remove state table entry after observing connection teardown
Semantically similar to punt-and-switch model of traffic forwarding used on many older routers

## Slide 27: State Table Issues
If the state table is not pruned, it will overflow
  Not all connections close cleanly
    I shut my laptop and go to a meeting
    Software crashes happen
  Some attacks try to fill state tables
Solution: put a timer on state table entries
  When a packet matches the state table entry, update the timer
  If the timer expires, delete the state table entry
What if I just pause for a few minutes?
  This turns out to be a problem – state table timers are typically in the 5-15 minute range, while host keepalive timers are 2 hours
  If a connection pauses (e.g. to wait for a large transfer), the firewall will delete the state table entry from under it – connection hangs
  I have seen this in production environments

## Slide 28: Security Without Enterprise Firewalls

## Slide 29: Security Without Enterprise Firewalls
Data intensive science traffic interacts poorly with firewalls
Does this mean we ignore security? NO!
  We must protect our systems
  We just need to find a way to do security that does not prevent us from getting the science done
Key point – security policies and mechanisms that protect the Science DMZ should be implemented so that they do not compromise performance

## Slide 30: If Not Firewalls, Then What?
Remember – the goal is to protect systems in a way that allows the science mission to succeed
There are multiple ways to solve this – some are technical, and some are organizational/sociological
Note: this is harder than just putting up a firewall and thinking you are done
Notes: It will probably work better because the firewall isn’t doing that much for high-performance DTNs anyway

## Slide 31: Other Security Mechanisms: ACLs
Aggressive access lists
  More useful with project-specific DTNs
  If the purpose of the DTN is to exchange data with a small set of remote collaborators, the ACL is pretty easy to write
  Large-scale data distribution servers are hard to handle this way (but then, the firewall ruleset for such a service would be pretty open too)
Limitation of the application set
  One of the reasons to limit the application set in the Science DMZ is to make it easier to protect
  Keep unnecessary applications off the DTN (and watch for them anyway using a host IDS – take violations seriously)

## Slide 32: Other Security Mechanisms: Network IDS
Intrusion Detection Systems (IDS)
  One example is Bro – http://bro-ids.org/
  Bro is high-performance and battle-tested
    Bro protects several high-performance national assets
    Bro can be scaled with clustering: http://www.bro-ids.org/documentation/cluster.html
  Other IDS solutions are available also

## Slide 33: What Is Bro?
Packet Capture
Traffic Inspection
Attack Detection
Flexibility
Abstraction
Data Structures
Log Recording
“Domain-specific Python”
NetFlow
syslog
Flexibility
Abstraction
Data Structures

## Slide 34: The Bro Platform
Vulnerabilit.Mgmt
Intrusion Detection
File Analysis
Compliance Monitoring
Traffic Measure-ment
Traffic Control
Network
Programming Language
Packet Processing
Standard Library
Platform
Apps
Tap
Open Source
BSD License

## Slide 35: Other Security Mechanisms: Host IDS
Using a Host IDS is recommended for hosts in a Science DMZ
There are several open source solutions that have been recommended:
  OSSec: http://www.ossec.net/
  Rkhunter: http://rkhunter.sourceforge.net (rootkit detection + FIM)
  chkrootkit: http://chkrootkit.org/
  Logcheck: http://logcheck.org (log monitoring)
  Fail2ban: http://www.fail2ban.org/wiki/index.php/Main_Page
  denyhosts: http://denyhosts.sourceforge.net/

## Slide 36: Other Security Mechanisms
Blackhole Routing to block attacks
Netflow, IPFIX, sflow, etc. can provide visibility
Openflow and SDN
  Using Openflow to control access to a network-based service seems pretty obvious
  There is clearly a hole in the ecosystem with the label “Openflow Firewall” – I really hope someone is working on this (it appears so)
  This could significantly reduce the attack surface for any authenticated network service
  This would only work if the Openflow device had a robust data plane

## Slide 37: Collaboration Within The Organization
All stakeholders should collaborate on Science DMZ design, policy, and enforcement
The security people have to be on board
  Remember: security people already have political cover – it’s called the firewall
  If a host gets compromised, the security officer can say they did their due diligence because there was a firewall in place
  If the deployment of a Science DMZ is going to jeopardize the job of the security officer, expect pushback
The Science DMZ is a strategic asset, and should be understood by the strategic thinkers in the organization
  Changes in security models
  Changes in operational models
  Enhanced ability to compete for funding
  Increased institutional capability – greater science output

## Slide 38: Science DMZ Security
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 39: Extra Slides

## Slide 40: Sample Security Analysis from the University of Illinois (Nick Buraglio)

## Slide 41: How do we security now?
Firewalls
IPS
ACLs
Black hole routing
IDS
Host IDS
SNMP collection
The first 2 (Firewalls and IPS) are the only ones with performance implications. Can we create a secure environment without them?
Notes: Take what we do now and repurpose what we can. Use ACLs, BHR, IDS in conjunction with an open network. Possibly leverage openflow in the future. Lab work is promising.

## Slide 42: Management and Security Concerns
  “Adding visibility is essential for accountability”
  “Timely mitigation of issues is required”
  “Automated mitigation is highly desirable”*
  “Once you’ve broken into a DMZ host you have an outpost in enemy territory”

## Slide 43: Final Requirements
University of Illinois management, network engineers, and security staff decided on the following for their Science DMZ:
Flow Data for accountability (netflow/sflow/jflow)
SNMP collection for baseline creation and capacity planning
Router ACLs for best practice ingress blocks
Passive network IDS for monitoring (Bro)
Host IDS on all hosts outside the firewall (OSSec)
IDS triggered black hole routing for mitigation
  Triggers from both network and host IDS
Bogon (bogus IP address) filtering

## Slide 44: Bro

## Slide 45: Bro Cluster Ecosystem
Tap
Bro
Internal Network
Internet
Bro Client Communication Library
Broccoli
Events
Events
State
Broccoli Ruby
Broccoli Python
(Broccoli Perl)
External Scripts
Functionality
BroControl
Control
User Interface
Output
Bro
Bro
Bro
Bro
Packets
Load-Balancer
BroControl
Control
Output
User Interface
“Workers”
“Manager”
“Frontend”