## Slide 1: Data Transfer Nodes
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 2: Overview
Part 1:
  What is Science Engagement?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
  Globus Connect Personal
Part 4:
  perfSONAR
Part 5:
  SDN and the Science DMZ
Conclusions & Discussion

## Slide 3: The Data Transfer Superfecta: Science DMZ Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase
Notes: Quick roadmap in the Science DMZ model
Data transfer nodes (both hardware and software) and configuration
Me: Hardware part
Eli: software tools and performance tuning

## Slide 4
Notes: Quick refresher…
Data transfer node (or DTN) is a dedicated server specifically made for high-performing, wide-area data transfers
This is usually connected to a Science DMZ switch connected to the site border router (in a basic campus-based Science DMZ)

## Slide 5: DTN Hardware Selection
Notes: Now onto the first part of the DTN
the Hardware selection
For importance and completeness,
we have to start from the bottom up to build these servers—there is not always a common “out of the box” solution for deploying these (as everyone has different needs, architecture etc.) so it is important to point out a few key things related to the hardware to reduce potential problems and bottlenecks.
We do also have a few reference designs which help out with DTNs as well (on fasterdata.es.net)

## Slide 6: Data Transfer Node
A DTN server is made of several subsystems. Each needs to perform optimally for the DTN workflow:
  Storage: capacity, performance, reliability, physical footprint
  Networking: protocol support, optimization, reliability
  Motherboard: I/O paths, PCIe subsystem, IPMI
  Chassis: adequate power supply, extra cooling
Note: the workflow we are optimizing for here is sequential reads/write of large files, and a moderate number of high bandwidth flows.
We assume this host is dedicated to data transfer, and not doing data analysis/manipulation
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 7: Motherboard and Chassis selection
Chassis
  Extra cooling (for future expansion, unless you buy the system full)
  Make sure the power supply is adequate
Motherboard/CPU
  Intel Sandy Bridge or Ivy Bridge CPU architecture
    Ivy Bridge is about 20% faster
    High clock rate better than high core count for DTNs
    Faster QPIC for communication between processors
  PCI Gen 3 (full 40G requires PCI Gen 3)
  Memory speed – faster is better
    We recommend 32GB of RAM for a DTN node. More is better
  IPMI for remote management
Notes: The questions to ask while making motherboard selection are:
How many cores do you need?
And at what speed ?
What kind of remote access (for maintenance) do you need?
In general, for your motherboard you want to make sure you have
PCI Gen3 capabilities
plenty of memory (both speed and space)
For example,
Intel’s Sandy/Ivy Bridge (Ivy Bridge is about 20% faster) CPU architecture provides these features,
An inadequate motherboard can become a major bottleneck.
It is, then, very important to correctly select it.

## Slide 8: PCI Slot Considerations
PCI slots are defined by:
  Slot width:
    Physical card and form factor
    Max number of lanes
  Lane count:
    Maximum bandwidth per lane
    Most cards will run slower in a slower slot
    Not all cards will use all lanes
Notes: When thinking about the PCI slots, need to ask”
How many PCI cards will you need ? How many lanes each ?
What is the aggregate throughput you need on your PCI cards ?
PCI slots are defined by slot width and lane count
Basically just need to make sure you have the right number for the right PCI slots
RAID controllers, NICs, and anything connected to the network goes through the PCI cards
If its not fast enough, this will be your bottleneck
________________________
  Form Factor: This is the length of the slots, referred as the number of PCI lanes it can support, and cards. A 16 lane controller is twice as long as an 8 lane controller.
  Number of wired lanes: not all lanes of the slot may be wired. Some 8 lane controller may only have 4 lanes wired.
  Bridges
    PCIe 2.0 is 500 MB/sec per lane. A typical host supports 8 lane (x8) slots but only runs at half speed: 4 GB/sec. A high-end host might have 16 lane (x16) slots, or up to 8 GB/sec.
    PCIe 3.0 = Double the above
RAID controllers, NICs and anything connected to the network goes through PCIe—if its not fast enough, this will be the bottleneck.
Make sure the motherboard you select has the right number of slots with the right number of lanes for you planned usage.

## Slide 9: PCI Bus Considerations
Example:
  10GE NICs require an 8 lane PCIe-2 slot
  40G/QDR NICs require an 8 lane PCIe-3 slot
  Most RAID controllers require an 8 lane PCIe-2 slot
  A high-end Fusion-io card may require a 16 lane PCIe-3 slot
Motherboard/system possibilities:
  SuperMicro motherboard X9DR3-F
  Sample Dell Server (Poweredge r320-r720)
  Sample HP Server (ProLiant DL380p gen8 High Performance model)
Notes: Make sure the motherboard you select has the right number of slots with the right number of lanes for you planned usage.
For example, some typical slot requirements are:
  10GE NICs require an 8 lane PCIe-2 slot
  40G/QDR NICs require an 8 lane PCIe-3 slot
  Most RAID controllers require 8 lane PCIe-2 slot
  A high-end Fusion IO ioDrive may require a 16 lane PCIe-3 slot
Here are some possible motherboards to consider
  SuperMicro X9DR3-F
  Sample Dell Server (Poweredge r320-r720)
  Sample HP Server (ProLiant DL380p gen8 High Performance model)
Supermicro is in our reference designs (posted on fasterdata)
But other vendors have servers that can be used as DTNs
Some institutions require long-term support contracts for servers so they tend to want to go with an established vendor (Dell, HP etc.)
All these are capable of 40G though
  ________________________

## Slide 10: Storage Architectures - Internal
DTN with internal RAID is self-contained
  Same CPU, RAM, etc. as DTN with external storage
  No external dependencies for storage
  Deployable anywhere
  Limited scalability
  Storage managed locally (you get whatever tools the RAID controller gives you)
Notes: Next is: what does the storage look like for a DTN?
There are various ways you can bring storage into or to your server
3 main classes
The 1st and most common DTN choice is local storage within the DTN
Perks:
no external dependencies
deployable anywhere
But
limited scalability
and only tools for managing storage come from RAID controllers
_____________
Local storage: the storage system (just a bunch of drives / JBOD) is packaged with the server. That can from 12 drivers up to 48 drives depending on vendor/model. In addition, external chassis with more drives can be added, connected to the server with SAS or FC. This is ideal for standalone servers since it does not require plumbing for the storage subsystem.
However, maintenance is typically more difficult since it does not have all the tooling that usually comes with storage systems.

## Slide 11: Storage Architectures - External
These are essentially the same from a DTN host design perspective
  IB, Ethernet, or Fibrechannel card connects to external storage
  Other system components (CPU, RAM, etc.) the same
  Central storage management, greater flexibility
  Integration with other large-scale resources (e.g. HPC)
Notes: Next two classes are the same from a systems perspective
(main different from a workflow perspective—i.e. double copy workflow for SANs but not with distributed/global file systems)
We see these storage architectures in DTNs at data and HPC facilities
But whatever you choose for storage will depend on your environment, requirements, and resources.
______________________
System reasoning: what kind of card used on the backend to the storage system—FC/Ethernet/Inifiniband look the same
But the workflow is what’s different
No block device communication between DTN kernel Global fs
For SAN and internal disks—DTN kernel sees it as “owning”/managing blocks in SAN or RAID
_____________________________
Distributed file systems—high quality of service
much more reliable
easy to manage
however, typically performance is much lower because they are usually a shared system—don’t know the workload of other users—possibility of contesting traffic
i.e., we see this at data centers/supercomputers
they do have bottlenecks. I/O is the storage controller (EMC is limited to 8G right now)
Same I/O capacity but no bottleneck with infiniband connections.
enterprise level system
IB
56 G/link and easy to aggregate
reliable networking—no packet loss
fairly cheap
Distributed filesystem: this is similar to the storage system, except that the exported volumes are not RAW but file system (PNFS, Lustre, GPFS…). This set up is typical of a tiered system: data is acquired and processed, and stored. Then the DTN read from the shared storage.
Storage Systems: These are usually more massive systems (EMC, Netapp, DDN, etc) providing raw volumes to servers. The connectivity is usually fiber, but it can also be infiniband and ethernet.
This class benefits storage capacity.
POINT: look at what your infrastructure requirements are
how much capacity do you need for the next 3 years—will your system scale the way you want?
how reliable does your storage have to be—source of truth or is it a pain to resend the data if a disk goes down? (i.e., choose your RAID appropriately)
performance of storage what you need? If its 10G—laptops won’t do that
don’t need to invest in super fast storage if you only want to use laptops

## Slide 12: Storage Subsystem Selection
Deciding what storage to use in your DTN is based on what you are optimizing for:
  performance, reliability, capacity, and/or cost
SATA disks historically have been cheaper and higher capacity, while SAS disks typically have been the fastest.
  Technologies have been converging (and its hard to keep up)
Do what you can support well
Notes: Now we are assuming you’ve chosen to go with internal disks/storage for your DTN
Deciding what storage to use in your DTN is based on what you are optimizing for:
  performance, reliability, capacity, or cost.
SATA disks historically have been cheaper and higher capacity, while SAS (SCSI) disks typically have been the fastest.
  Technologies have been converging (and its hard to keep up)
  SATA (lower quality) was more for consumers and SAS for enterprise
  SATA 3 is coming up to speed with SAS performance though
POINT: Choose what you can support well
_____________________________
SATA vs. SAS
Currently no particular reason to choose one over the other
SATA used to be much lower than SAS for performance
With SATA 3 it is comparable performance now
(SATA/SAS drives to RAID controller)
Historically
SATA (lower quality) was more for consumers and SAS for enterprise
Check SATA3!
[SAS/SATA bus that connects computer storage to drives
SAS backplanes are backward compatible with SATA but not SATA 3]
SATA3 and SAS are multipath I/O so roughly the same performance now but SAS is still recommended for non-consumer based workflows.

## Slide 13: SSDs and HDs
SSD storage costs much more than traditional hard drives (HDs), but are much faster. They come in different styles:
  PCIe card: some vendors (Fusion-io) build PCI cards with SSDs.
    These are the fastest type of SSD: up to several GBytes/sec per card.
      Note that this type of SSD is typically not hot-swapable.
  HD replacement: several vendors now sell SSD-based drives that have the same form factor as traditional drives such as SAS and SATA.
    The downside to this approach is that performance is limited by the RAID controller, and not all controllers work well with SSD.
      Be sure that your RAID controller is “SSD capable”.
Note that the price of SSD is coming down quickly, so an SSD-based solution may be worth considering for your DTNs.
Notes:   SSDs have usually been more expensive than HDs
  prices are coming down though
  SSDs do come in a few different shapes now:
  On PCI cards (these are by far the fastest but they are the most expensive)
  And as HD replacements: several vendors now sell SSD-based drives that have the same form factor as traditional drives such as SAS and SATA.
    The downside to this approach is that performance is limited by the RAID controller, and not all controllers work well with SSD.
      Be sure that your RAID controller is “SSD capable”.
  _____________________________________
SSD have much less capacity/performance
every vendor has a different way of dealing with SSDs
some read fast but are WAY slower to write—slower than a hard drive
I.e., 97 GB/sec read with a 20GB/sec write—this is not optimal for a read/write workflow
i.e. laptop mostly does read
SSDs more geared to commodities right now—not great for high performance right now
SSDs not for everyone
Have to go back to WHAT IS YOUR WORKFLOW—i.e., bioinformatics use case with mostly reads, SSDs could be a good choice
For a lot of writes like a beamline at a light source, hard drives may be better
SSDs come in a lot of different packaging
One of the pros for SSDs are that they are good for plug and play
make sure that your RAID controller can deal with SSDs though because it is not always the same for every level

## Slide 14: SSD Form Factors
Notes: Fusion-io with SSDs on PCI cards (go directly to the CPU)
Left: two form factor replacements for HDs
Please note that performance/longevity of the SSD HD replacements is not great
They have a tendency to fail faster
also performance is unreliable: from 1GB to 100MB/s because they use more power, therefore heat up faster, and slowdown
______________________________
SSD $$ is becoming interesting—10X faster than the hard drive
not going to pay more for SSD performance
Performance/$$ is the same
But the catch is CAPACITY is not the same!
_____________________
Right side picture—PCIe card with SSD (this is what Fusion IO is doing this—the best for performance but pretty pricey--8TB was $120,000 last time we checked)
1TB available/card
max performance of an SSD—then no RAID controller in the path—goes directly to CPU
Form factor SSDs fail faster (examples shown on the left side)
SSD performance is not predictable
uses more power than a physical drive
they warm up much more to a point where systems cannot cool them down
internal measurement in systems and the SSDs will slow down (killing performance)
Slow down from 1GBs to 100MB/s—becomes super slow—therefore it is harder to predict how fast your I/O is going to be
On the other hand,
Hard drives are predictable and cooled
_______________________________
SSD, cost much more than HD, but a much faster. They come in different packages:
PCIe card: some vendors (Fusion I/O) build PCI cards with SSD. The current maximum capacity is 1TB per card. Since those cards are PCIe, the data transfer between the main memory and the SSD is just limited by the SSD speed and the PCIe speed: in other words, it is really fast (several GB/sec per card). The drawbacks are that 1TB uses a PCIe slot. This design often means that a PCI extender is needed, but if space and performance is an issue, this is the best solution. Those SSD cards can also be an deployment issue: replacing a failed card means that the server must be open.
- HD replacement: some vendors (IBM, WD, etc) have product that a physical replacement for HD: same form factor, same connectivity (SAS, SATA…). This allows for easier migration path from HD to SSD, but the performance is limited by the controller. Also, not all controllers are good at controlling SSD drives: always make sure that the controller is “SSD capable”.

## Slide 15: RAID Controllers
Often optimized for a given workload, rarely for performance.
RAID0 is the fastest of all RAID levels but is also the least reliable.
The performance of the RAID controller is a factor of the number of drives and its own processing engine.
Notes: In general, RAID controllers are often optimized for a given workload, rarely for performance.
  Trade-offs between reliability and speed.
(Disk controllers, RAID or not, are usually designed for “entreprise”.) This usually means that the controller is often configured with RAID 5 or 6.
RAID0 is the fastest of all RAID levels but is also the least reliable.
As a consequence, controllers are most of the time not capable of running all the drives at full speed:
  A rule of thumb is that if a controller is said to handle up to X drives, it can handle up to 2/3 X drivers at full speed.

## Slide 16: RAID Controller
Be sure your RAID controller has the following:
  >= 1GB of on-board cache
  PCIe Gen3 support
  dual-core RAID-on-Chip (ROC) processor if you will have more than 8 drives
Notes: Some high end controllers (Areca for instance) are specifically designed for a workflow similar to a DTN workflow: sequential read/write. They may have Gigabytes of SRAM for internal buffering, PCIe x16..
Finally, some RAID controllers are specifically designed to scale up. In addition to wire internal drives, they can control external drives, directly or in a daisy chain manner

## Slide 17: Network Subsystem Selection
There is a huge performance difference between cheap and expensive 10G NICs.
  E.g. please don’t cheap out on the NIC – it’s important for an optimized DTN host.
NIC features to look for include:
  support for interrupt coalescing
  support for MSI-X
  TCP Offload Engine (TOE)
  support for zero-copy protocols such as RDMA (RoCE or iWARP)
Note that many 10G and 40G NICs come in dual ports, but that does not mean if you use both ports at the same time you get double the performance. Often the second port is meant to be used as a backup port.
  Myricom 10G-PCIE2-8C2-2S
  Mellanox MCX312A-XCBT
Notes: Last thing in the hardware queue is to think about the Network subsystem
Networking subsystem is the second subsystem after the storage that is critical and could be a major bottle neck.
The choice of your NIC(s) will impact performance.
There is a huge performance difference between cheap and expensive 10G NICs.
  E.g. please don’t cheap out on the NIC – it’s important for an optimized DTN host.
NIC features to look for include:
  support for interrupt coalescing
  support for MSI-X
  TCP Offload Engine (TOE)
  support for zero-copy protocols such as RDMA (RoCE or iWARP)
Note that many 10G and 40G NICs come in dual ports, but that does not mean if you use both ports at the same time you get double the performance. Often the second port is meant to be used as a backup port.
  True 2x10G capable cards include the Myricom 10G-PCIE2-8C2-2S and the Mellanox MCX312A-XCBT.

## Slide 18: Take Home Points
The 2 key “take homes” for hardware are:
  Needs to be expandable and
  Needs to be supportable
Want to avoid experiences like this for data transfers…
http://www.toonpool.com/user/24456/files/computer_time_1515305.jpg
Notes: It is important to pay attention to the hardware
Hardware is especially important because you can be stuck with long-lasting performance bottlenecks if you’re not careful with
components that are incompatible,
have wrong interfaces
or run out of capacity
Want to make sure the hardware you choose/purchase is
-Expandable for future needs at least 3-5 years out
-and supportable—because backyard concoctions can be hard to work with…

## Slide 19: Tuning for Performance http://fasterdata.es.net
Notes: We’ve built the DTN – now we need to configure it

## Slide 20: DTN Tuning http://fasterdata.es.net/science-dmz/DTN/tuning
Defaults are not appropriate for performance.
  What needs to be tuned:
  BIOS
  Firmware
  Device Drivers
  Networking
  File System
  Application

## Slide 21: DTN Tuning
Tuning your DTN host is extremely important. We have seen overall IO throughput of a DTN more than double with proper tuning.
Tuning can be as much art as a science. Due to differences in hardware, its hard to give concrete advice.
Here are some tuning settings that we have found do make a difference.
This tutorial assumes you are running a RedHat-based Linux system, but other Unix flavors should have similar tuning knobs.
Note that you should always use the most recent version of the OS, as performance optimizations for new hardware are added to every release.

## Slide 22: Network Tuning
# add to /etc/sysctl.conf
net.core.rmem_max = 33554432
net.core.wmem_max = 33554432
net.ipv4.tcp_rmem = 4096 87380 33554432
net.ipv4.tcp_wmem = 4096 65536 33554432
net.core.netdev_max_backlog = 250000
Add to /etc/rc.local
# increase txqueuelen
/sbin/ifconfig eth2 txqueuelen 10000
/sbin/ifconfig eth3 txqueuelen 10000
This info (and more) is available on fasterdata, formatted for cut and paste
# make sure cubic and htcp are loaded
/sbin/modprobe tcp_htcp
/sbin/modprobe tcp_cubic
# set default to CC alg to htcp
net.ipv4.tcp_congestion_control=htcp
# with the Myricom 10G NIC
# using interrupt coalencing helps a lot:
/usr/sbin/ethtool -C ethN rx-usecs 75
Please consider jumbo frames, but don’t just blindly turn them on
Notes: interrupt coalencing is used to avoid flooding the host system with too many interrupts, packets are collected and one single interrupt is generated for multiple packets.
Not all NIC support it
75-100 micro-seconds timeout
Is critical for high performance NIC (10Gb, 40Gb…)

## Slide 23: BIOS Tuning
For PCI gen3-based hosts, you should
  enable “turbo boost”,
  disable hyperthreading and node interleaving.
More information on BIOS tuning is described in this document:
  http://www.dellhpcsolutions.com/assets/pdfs/Optimal_BIOS_HPC_Dell_12G.v1.0.pdf

## Slide 24: I/O Scheduler
The default Linux scheduler is the "fair" scheduler. For a DTN node, we recommend using the "deadline" scheduler instead.
To enable deadline scheduling, add "elevator=deadline" to the end of the "kernel' line in your /boot/grub/grub.conf file, similar to this:
kernel /vmlinuz-2.6.35.7 ro root=/dev/VolGroup00/LogVol00 rhgb quiet elevator=deadline

## Slide 25: Interrupt Affinity
Interrupts are triggered by I/O cards (storage, network). High performance means lot of interrupts per second
Interrupt handlers are executed on a core
  Interrupt handler is just code – it gets run for every interrupt
  Cache effects matter (with lots of I/O we’re going to run that code a lot)
Depending on the scheduler, core 0 gets all the interrupts, or interrupts are dispatched in a round-robin fashion among the cores: both are bad for performance:
  Core 0 get all interrupts: with very fast I/O, the core is overwhelmed and becomes a bottleneck
  Round-robin dispatch: very likely the core that executes the interrupt handler will not have the code in its L1 cache.
  Two different I/O channels may end up on the same core.

## Slide 26: A simple solution: interrupt binding
Each interrupt is statically bound to a given core (network -> core 1, disk -> core 2)
Works well, but can become an headache and does not fully solve the problem: one very fast card can still overwhelm the core.
  Still better than all interrupts on one core
  Interrupt coalescing can help reduce interrupt load
Binding applications is more difficult
  Often need to bind application using data to the same cores for best optimization
  What about multi-threaded applications, for which we want one thread = one core?

## Slide 27: Know Your Layout
Where are your cards?
Where are your cores?
Understand what your bindings mean physically
Performance of a given config can be tightly coupled to physical layout
Don’t be afraid to experiment
Notes: For interrupt binding, you need to know where the card is, and where the cores are.

## Slide 28: Firmware
Firmware runs on the card
  NIC, RAID, etc.
  Often different versions, just like drivers
Not all firmware versions have all features
Latest and greatest may not be best
  Bugs happen
  Specific feature enhancements in latest version may not apply to your workload
  This isn’t just theoretical – we have had to revert firmware to regain lost performance

## Slide 29: File System Tuning
We recommend using the ext4 file system in Linux for DTN nodes.
Increasing the amount of "readahead" usually helps on DTN nodes where the workflow is mostly sequential reads.
  However you should test this, as some RAID controllers do this already, and changing this may have adverse affects.
Setting readahead should be done at system boot time. For example, add something like this to /etc/rc.local:
  /sbin/blockdev --setra 262144 /dev/sdb
More information on readahead:
  http://www.kernel.org/doc/ols/2004/ols2004v2-pages-105-116.pdf

## Slide 30: EXT4 Tuning
The file system should be tuned to the physical layout of the drives.
  Stride and stripe-width are used to align the volume according to the stripe-size of the RAID.
    stride is calculated as Stripe Size / Block Size
    stripe-width is calculated as Stride * Number of Disks Providing Capacity.
    Units are disk blocks, not bytes – know your block size (512 or 4096 bytes, typically)
Disabling journaling will also improve performance, but reduces reliability.
  Don’t do this unless you know what your are doing
  Fine for benchmarking and exploration, but don’t run this way in production
Sample mkfs command (disables journal):
  /sbin/mkfs.ext4 /dev/sdb1 –b 4096 –E stride=64 \ stripe-width=768 –O ^has_journal
Notes: Stride size is sometimes called chunk size – the size of the portion of a stripe written to one disk in the raid set. Measured in blocks (512 byte or 4096 byte depending on disk).
Stripe width is stride size times number of disks

## Slide 31: File System Tuning (cont.)
There are also tuning settings that are done at mount time. Here are the ones that we have found improve DTN performance
Note well – many options trade reliability for performance
  Know Your Workflow (just like Know Your Network)
  Is your DTN going to be used as a cache?
  Is the workload predominantly reads (e.g. data service)?
  Is the DTN the source of truth for data sets?
data=writeback
  This option forces ext4 to use journaling only for metadata. This gives a huge improvement in write performance
  Some reliability concerns – understand before deploying
commit=300
  This parameter tells ext4 to sync its metadata and data every 300s (default is 5)
  This reduces the reliability of data writes, but increases performance
barrier=0
  Barriers enforce proper ordering of disk writes, making volatile disk caches safe
  If your cache is battery-backed, this may safely improve performance

## Slide 32: File System Tuning (cont.)
These mount-time options are less risky
inode_readahead_blks=64
  this specifies the number of inode blocks to be read ahead by ext4’s readahead algorithm
  Default is 32 blocks
noatime,nodiratime
  These parameters tells ext4 not to write the file and directory access timestamps.
  Almost always a no-brainer
    Most applications don’t use file or directory access time
    If your application does rely on atime, don’t use this
Sample fstab entry (includes safe and less-safe options):
  /dev/sdb1 /storage/data1 ext4 inode_readahead_blks=64,data=writeback,barrier=0,commit=300,noatime,nodiratime
  For more info see: http://kernel.org/doc/Documentation/filesystems/ext4.txt

## Slide 33: RAID Controller
Different RAID controllers provide different tuning controls. Check the documentation for your controller and use the settings recommended to optimize for large file reading.
  You will usually want to disable any “smart” controller built-in options, as they are typically designed for different workflows.
Here are some settings that we found increase performance on a 3ware RAID controller. These settings are in the BIOS, and can be entered by pressing Alt+3 when the system boots up.
  Write cache – Enabled (reliability check – do you have a battery backup for your RAID cache memory?)
  Read cache – Enabled
  Continue on Error – Disabled
  Drive Queuing – Enabled
  StorSave Profile – Performance
  Auto-verify – Disabled
  Rapid RAID recovery – Disabled

## Slide 34: Virtual memory Subsystem
Setting dirty_background_bytes and dirty_bytes improves write performance.
For our system, the settings that gave best performance were:
  echo 1000000000 > /proc/sys/vm/dirty_bytes
  echo 1000000000 > /proc/sys/vm/dirty_background_bytes
For more information see:
  http://www.kernel.org/doc/Documentation/sysctl/vm.txt

## Slide 35: SSD Issues – Write Sparingly
Tuning your SSD is more about reliability and longevity than performance
  Each flash memory cell has a finite lifespan that is determined by the number of "program and erase (P/E)" cycles
  Without proper tuning, SSD can die within months.
  never do "write" benchmarks on SSD: this will damage your SSD quickly.
TRIM
  Trim informs the SSD when the filesystem no longer needs space
  Important to prolong the life of SSDs
  Modern SSD drives and modern OSes should all include TRIM support
  Only the newest RAID controllers included TRIM support as of late 2012
Swap
  To prolong SSD lifespan, do not swap on an SSD
  In Linux you can control this using the sysctl variable vm.swappiness. E.g.: add this to /etc/sysctl.conf:
    vm.swappiness=1
    This tells the kernel to avoid unmapping mapped pages whenever possible.
Avoid frequent re-writing of files (for example during compiling code from source), use a ramdisk file system (tmpfs) for /tmp /usr/tmp, etc.
Notes: TRIM informs the disk when the filesystem has freed a block
More controllers should support TRIM now – however, make sure you check into this.

## Slide 36: ext4 file system tuning for SSD
These mount flags should be used for SSD partitions.
  noatime,nodiratime:
    File reads will no longer result in an update to the atime information associated with the file
    Eliminates writes to the file system resulting from file reads
  discard: This enables the benefits of the TRIM command as long as kernel version >=2.6.33.
Sample /etc/fstab entry:
  /dev/sda1 /home/data ext4 defaults,noatime,discard 0 1
For more information:
  http://wiki.archlinux.org/index.php/Solid_State_Drives

## Slide 37: Benchmarking
Single-threaded sequential file write:
  $ dd if=/dev/zero of=/storage/data1/file1 bs=4k count=33554432
Single-threaded sequential file read:
  $ dd if=/storage/data1/file1 of=/dev/null bs=4k
Use more to simulate parallel workload
  Use oflag=direct to disable caching

## Slide 38: Overview
Part 1:
  What is Science Engagement?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
  Globus Connect Personal
Part 4:
  perfSONAR
Part 5:
  SDN and the Science DMZ
Conclusions & Discussion

## Slide 39: Sample Data Transfer Results
Using the right tool is very important
  Sample Results: Berkeley, CA to Argonne, IL (near Chicago). RTT = 53 ms, network capacity = 10Gbps.
    Tool Throughput
    scp: 140 Mbps
    HPN patched scp: 1.2 Gbps
    ftp 1.4 Gbps
    GridFTP, 4 streams 6.6 Gbps (disk limited)
            Note that to get more than 1 Gbps (125 MB/s) disk to disk requires RAID.

## Slide 40: Data Transfer Tools
Parallelism is key
  It is much easier to achieve a given performance level with four parallel connections than one connection
  Several tools offer parallel transfers
Latency interaction is critical
  Wide area data transfers have much higher latency than LAN transfers
  Many tools and protocols assume a LAN
  Examples: SCP/SFTP, HPSS mover protocol

## Slide 41: Why Not Use SCP or SFTP?
Pros:
  Most scientific systems are accessed via OpenSSH
  SCP/SFTP are therefore installed by default
  Modern CPUs encrypt and decrypt well enough for small to medium scale transfers
  Credentials for system access and credentials for data transfer are the same
Cons:
  The protocol used by SCP/SFTP has a fundamental flaw that limits WAN performance
  CPU speed doesn’t matter – latency matters
  Fixed-size buffers reduce performance as latency increases
  It doesn’t matter how easy it is to use SCP and SFTP – they simply do not perform
Verdict: Do Not Use Without Performance Patches

## Slide 42: A Fix For scp/sftp
PSC has a patch set that fixes problems with SSH
  http://www.psc.edu/networking/projects/hpn-ssh/
Significant performance increase
Advantage – this helps rsync too

## Slide 43: sftp
Uses same code as scp, so don't use sftp WAN transfers unless you have installed the HPN patch from PSC
But even with the patch, SFTP has yet another flow control mechanism
  By default, sftp limits the total number of outstanding messages to 16 32KB messages.
  Since each datagram is a distinct message you end up with a 512KB outstanding data limit.
  You can increase both the number of outstanding messages ('-R') and the size of the message ('-B') from the command line though.
Sample command for a 128MB window:
  sftp -R 512 -B 262144 user@host:/path/to/file outfile

## Slide 44: FDT
FDT = Fast Data Transfer tool from Caltech
  http://monalisa.cern.ch/FDT/
  Java-based, easy to install
  used by CMS project and DYNES NSF Funding effort

## Slide 45: Other Data Transfer Tools
bbcp: http://www.slac.stanford.edu/~abh/bbcp/
  supports parallel transfers and socket tuning
  bbcp -P 4 -v -w 2M myfile remotehost:filename
lftp: http://lftp.yar.ru/
  parallel file transfer, socket tuning, HTTP transfers, and more.
  lftp -e 'set net:socket-buffer 4000000; pget -n 4 [http|ftp]://site/path/file; quit'
axel: http://axel.alioth.debian.org/
  simple parallel accelerator for HTTP and FTP.
  axel -n 4 [http|ftp]://site/file

## Slide 46: Commercial Data Transfer Tools
There are several commercial UDP-based tools
  Aspera: http://www.asperasoft.com/
  Data Expedition: http://www.dataexpedition.com/
  TIXstream: http://www.tixeltec.com/tixstream_en.html
These should all do better than TCP on a lossy path
  advantage of these tools less clear on an clean path
They all have different, fairly complicated pricing models

## Slide 47: GridFTP
GridFTP from ANL has features needed to fill the network pipe
  Buffer Tuning
  Parallel Streams
Supports multiple authentication options
  Anonymous
  ssh
  X509
Ability to define a range of data ports
  helpful to get through firewalls
Partnership with ESnet and Globus Online to support Globus Online for use in Science DMZs

## Slide 48
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 49: Extra Slides

## Slide 50: DTN Hardware Selection
The typical engineering trade-offs between cost, redundancy, performance, and so forth apply when deciding on what hardware to use for a DTN node
  e.g. redundant power supplies, SATA or SAS disks, cost/performance for RAID controllers, quality of NICs, etc.
We recommend getting a system that can be expanded to meet future storage/bandwidth requirements.
  science data is growing faster than Moore Law, so might as well consider a host that can support 40GE now, even if you only have a 10G network
IMPORTANT: Buying the right hardware is not enough. Extensive tuning is needed for a well optimized DTN.

## Slide 51: Interrupt Binding Considerations
On a multi-processor host, your process might run on one processor, but your I/O interrupts on another processor.
  When this happens there will be a huge performance hit.
    a single 10G NIC can saturate the QPIC that connects the two processors.
  You may want to consider getting a single CPU system, and avoid dual-processor motherboards if you only need 3 PCIe slots.
  If you need to optimize for a small number of very fast (> 6Gbps) flows, this means you will need to manage IQR bindings by hand.
    If you are optimizing for many 500Mbps-1Gbps flows, this will be less of an issue.
    You may be better off doing 4x10GE instead of 1x40GE, as you will have more control mapping IRQs to processors.
The impact of this is even greater with Sandy/Ivy Bridge Hosts, as the PCI bus slots are connected directly to a processor.

## Slide 52: Sample Hardware configuration
Motherboard: SuperMicro X9DR3-F
CPU: 2 x Intel(R) Xeon(R) CPU E5-2667 0 @ 2.90GHz
Memory: 64G ( 8 x 8GiB Kingston DDR3 1600 MHz / 0.6 ns)
RAID: 2 x 3Ware 9750SA-24i (24 ports SAS) connected to CPU 0
  Areca ARC-1882i should be even better, but we have not tested it
Network Controller: Myricom 10G-PCIE2-8C2-2S
  Use Mellanox cards if you are interested in RDMA
Disks: 16 x Seagate 1TB SAS HDD 7,200 RPM drives
Total cost: $12K in mid 2012

## Slide 53: Parallel Streams Help With TCP Congestion Control Recovery Time