## Slide 1: The Importance of Science Engagement
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 2: Overview
Part 1:
  What is Science Engagement?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
  Globus Connect Personal
Part 4:
  perfSONAR
Part 5:
  SDN and the Science DMZ
Conclusions & Discussion

## Slide 3: The Data Transfer Superfecta: Science DMZ Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase
Network Architecture

## Slide 4: Talk Outline
Context Setting
Science Trends
ESnet’s Approach
Requirements Reviews
A Success Story
What Should We Do Together?

## Slide 5: ESnet Supports the DOE Office of Science
Notes: This low-res map shows why most of our data flows terminate outside the national lab complex.
  =-=-=-=-=-=-=-=-=-
ESnet - the Energy Sciences Network - is an SC program whose primary mission is to enable the large-scale science of the Office of Science that depends on:
  Multi-institution, world-wide collaboration
  Data mobility: sharing of massive amounts of data
  Distributed data management and processing
  Distributed simulation, visualization, and computational steering
  Collaboration with the US and International Research and Education community
  =-=-=-=-=-=-=-=-=-
ESnet connects the Office of Science National Laboratories and user facilities to each other and to collaborators worldwide
Ames, Argonne, Brookhaven, Fermilab, Lawrence Berkeley, Oak Ridge, Pacific Northwest, Princeton Plasma Physics, SLAC, and Thomas Jefferson National Accelerator Facility,

## Slide 6: Context Setting
DOE and the NSF (and other agencies) are investing billions of dollars in state-of-the-art cyberinfrastructure to support data-intensive science
Most researchers do not understand the value of these services and have difficulty using them.
A proactive effort is needed to drive adoption and accelerate science output

## Slide 7: Traditional “Big Science”

## Slide 8: Big Science Now Comes in Small Packages
Notes:     Beamline 8.3.2 at the Advanced Light Source is a Synchrotron-based Hard X-ray Micro-Tomography instrument. It allows non-destructive 3-Dimensional imaging of solid objects at a resolution of approximately 1 micron.
    106 increase in data output compared to previous generation
    8 Gbps flows to supercomputer for real-time analysis

## Slide 9: One Beamline Data Flow Tripled Network Use for a DOE Supercomputing Center

## Slide 10: What is there to worry about?
© Owen Humphreys/National Geographic Traveler Photo Contest 2013
High Energy Physics
  LHC experiments produce & distribute petabytes of data/year
  Peak data rates increase 3-5x over 5 years
Genomics
  Sequencer data volume increasing 12x over the next 3 years
  Sequencer cost decreasing by 10x over same time period
Light Sources
    Many detectors on a Moore’s Law curve
    Data volumes rendering previous operational models obsolete
Common Threads
    Increased capability, greater need for data mobility due to span/depth of collaboration space
    Global is the new local. Research is no longer done within a domain. End to end involves many fiefdoms to cross.
Notes: This should not be news. The news is that there is convergence on how to support things in the network space.

## Slide 11
Universities funded by DOE & NSF
BER (genomics, climate)
BES (life & materials science)
CC-NIE awardees (round 1)
CC-NIE awardees (round 2)
Notes: This does not include information about LHC sites – only two of the six DOE science program offices
Thousands and thousands of scientists

## Slide 12: Challenges to Network Adoption
Causes of performance issues are complicated for users.
Lack of communication and collaboration between the CIO’s office and researchers on campus.
Lack of IT expertise within a science collaboration or experimental facility
User’s performance expectations are low (“The network is too slow”, “I tried it and it didn’t work”).
Cultural change is hard (“we’ve always shipped disks!”).
Scientists want to do science not IT support
The Capability Gap

## Slide 13: Vision
    Collaborations at every scale, in every domain, will have the information and tools they need to achieve maximum benefit from global networks.
    Scientific progress is completely unconstrained by the physical location of instruments, people, computational resources, or data.

## Slide 14: Requirements Reviews
http://www.es.net/about/science-requirements/network-requirements-reviews/
ESnet conducts biannual network requirements reviews to determine the current and future science networking requirements for the six DOE Office of Science program offices.
The purpose of these reviews is to accurately characterize the near-term, medium-term and long-term network requirements of the science conducted by each program office.
The reviews attempt to bring about a network-centric understanding of the science process used by the researchers and scientists, to derive network requirements.
We have found this to be an effective method for determining network requirements for ESnet's customer base.
Notes: 2006
ELI + company
Led to science DMZ and other important end site innovations

## Slide 15
High Energy Physics
Nuclear Physics
Basic Energy Research
Fusion Energy Sciences
Advanced Scientific Computing Research
Biological and Environmental Research
Photo courtesy of LBL
Photo courtesy of LBL
Photo courtesy of SLAC
Photo courtesy of PPPL
Photo courtesy of NIST
Photo courtesy of JGI

## Slide 16: How do we know what our scientists need?
Each Program Office has a dedicated requirements review every three years
Two workshops per year, attendees chosen by science programs
Discussion centered on science case studies
    Instruments and Facilities – the “hardware”
    Process of Science – science workflow
Network requirements derived from science case studies + discussions
Reports contain requirements analysis, case study text, outlook
Notes: Two reviews per year, One review per program office every 3 years
Goals –
1. Accurately characterize current and future network requirements
2. Collect network requirements from scientists and Program Office
Structure
Elicit information from managers, scientists and network users regarding usage patterns, science process, instruments and facilities – codify in “Case Studies”
Case studies focus on two different aspects of the science
    Instruments and Facilities – the “hardware” of science
    Process of Science – the way in which the Instruments and Facilities are used in the conduct of the science
    Synthesize network requirements from the Case Studies
ESnet’s core mission is to serve the DOE/SC science programs
    Large-scale data movement
    Network services to enable science
Network implications arise from the conduct of science
    Science instruments and facilities
    Process of science
    How will these change over time?

## Slide 17: 2013 BER Sample Findings: ESGF CMIP5
“It is estimated that the transfer of multiple terabytes of output to a Core Data Node would take much longer via the internet (by means of normal network hardware and conduits) than via physical disks, which is why the data will usually be transferred using portable hard disks. ”
CMIP5 Data Submission website (Climate)
http://cmip-pcmdi.llnl.gov/cmip5/submit.html
Notes: 0-2 years: current budget planning
* 2-5 years: current technological paradigm
* Beyond 5 years: major new facilities, projects, etc.

## Slide 18: 2013 BER Sample Findings: Environmental Molecular Sciences Laboratory (EMSL)
“EMSL frequently needs to ship physical copies of media to users when data sizes exceed a few GB. More often than not, this is due to lack of bandwidth or storage resources at the user's home institution.”

## Slide 19: Understanding Data Trends
Notes: Requirements workshops for all six program offices within the DOE office of Science

## Slide 20: Bringing Requirements Reviews to your campus
Key lessons learned:
Work with research office/program management to sponsor reviews.
Find an advocate/early adopter (or two, or three. . .)
Leverage reviews as an opportunity to create trust and goodwill
    Be immediately responsive, work on the low hanging fruit
Focus on science, data and facilities not “the network”.
Understand language barriers and cultural differences.
    Terminology may differ from collaboration to collaboration (e.g. user vs. beamline scientist)
It’s a continual process

## Slide 21: User Workflow: Beamline 8.3.2
Users
Publications
1. Allocation
2. Endstation
3. Sample
4. Control Software
5. Data Collection
6. Data Transfer / Management
7. Data Processing
9. Write and edit
8. Data Analysis / Info Extraction / Visualization / Simulation

## Slide 22
Science Workflow Consultation
Notes: X-ray tomography beamline
General purpose network
Windows shares on an old computer with not enough storage
Data acquisition uses LabView
Data written to shared drive on firewalled Windows server
Analysis done on workstations
  High-powered Windows hosts
  Mix of proprietary and open-source tools
  Scientists can be physically present or use Remote Desktop
Data export post-analysis – physical transport of portable media
  USB hard drives

## Slide 23: Improved Workflow Infrastructure
Notes: Dedicated infrastructure, built for performance, outside the general purpose network, clear path to NERSC
Data acquisition uses LabView
Data written to SAMBA share on beamline Linux DTN
  Writing via SAMBA is faster than local disk on acquisition computer
  Data are TIFF files ~10MB each, ~1000 files per data set
  Current max performance is ~200MB/sec
Automated workflow pushes data to NERSC for analysis
  Workflow managed using signal files
  Data set is rolled up into an HDF5 file
  Python scripts drive Globus Online CLI
  Data transferred to NERSC DTNs at ~300MB/sec
Analysis results pulled back to beamline DTN
  Additional analysis done on workstations (still use some proprietary tools)
  Primary data export is via Globus Online from beamline DTN

## Slide 24: How do we bridge the gap?
Discussion?
What outreach exists on your campus today?
Are you applying for CC-IIE?
Other challenges?
What have you done that has worked?

## Slide 25: The Importance of Science Engagement
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net