## Slide 1: Science DMZ Architecture
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 2: Community Context
NSF CC-NIE and CC-IIE programs
  Invest in improvements and re-engineering at the campus level to support a range of data transfers supporting computational science and computer networks and systems research
  Support Network Integration activities tied to achieving higher levels of performance, reliability and predictability for science applications and distributed research projects
Significant upgrades at National Laboratories
  Instruments, HPC, network infrastructure to tie it all together
Workshop goal – provide “hit the ground running” background for tackling these challenges. Several topics to be covered:
    Advanced data movement tools and procedures
    Capable network architectures – Science DMZ, SDN
    Federated End-to-End monitoring
Community discussion
    http://fasterdata.es.net/forums/
    https://gab.es.net/mailman/listinfo/sciencedmz
NSF 13-530: http://www.nsf.gov/pubs/2013/nsf13530/nsf13530.htm
NSF 14-521: http://www.nsf.gov/pubs/2014/nsf14521/nsf14521.htm
Notes: Goals and why we put on this workshop. There is software (and a community) there to help

## Slide 3: Overview
Part 1:
  What is Science Engagement?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
  Globus Connect Personal
Part 4:
  perfSONAR
Part 5:
  SDN and the Science DMZ
Conclusions & Discussion

## Slide 4: What is ESnet?
A high-performance network linking DOE Office of Science researchers to global collaborators and resources around the world, including:
    Supercomputer centers
    User Facilities
    Multi-program labs
    Universities
    Connectivity to Internet and Cloud providers
A national DOE user facility providing:
    Tailored data mobility solutions for science
    Dedicated Science Engagement team to support researchers
    Collaboration services e.g. audio/video conferencing
Notes: The U.S. Department of Energy’s Office of Science (“SC”) supports about half of all civilian R&D in the U.S. with about $5B/year in funding (with the National Science Foundation (NSF) funding the other half)
Operates ten National Laboratories and dozens of major scientific user facilities such as synchrotron light sources, neutron sources, particle accelerators, electron and atomic force microscopes, supercomputer centers, etc., that are all available to the US and Global science research community, and many of which generate massive amounts of data and involve large, distributed collaborations
Supports global, large-scale science collaborations such as the LHC at CERN and the ITER fusion experiment in France

## Slide 5
Notes: This is a graph of data, in bytes, transferred every month across the entire DOE complex since January 1990.
This is on a log scale.
This growth here is double that of the commercial Internet currently.
It’s been remarkably consistent for a quarter century.
One thing this shows is that there has not been a sudden explosion in the rate of growth of scientific data.
Instead, what’s happening is that the unrelenting pace of this exponential is beginning to stress and even overwhelm the workflows, tools, and architectures designed to handle it.

## Slide 6: Supporting Science Data
The capabilities required to support scientific data movement involve hardware and software developments at all levels:
  Optical signal transport
  Network routers and switches
  Data transport (TCP is still the norm)
  Network monitoring and testing
  Operating system evolution
  Data movement and management techniques and software
  Evolution of network architectures
  New network services
Technology advances in these areas have resulted in today’s state-of-the-art that makes it possible for science to continue innovating
Notes: RED = topics covered in this tutorial

## Slide 7: Wide Area Network is Engineered for Elephants

## Slide 8: Time to Raise Your Network Expectations: Time to Copy 1 Terabyte
On a…
    10 Mbps network: 300 hrs (12.5 days)
    100 Mbps network: 30 hrs
    1 Gbps network: 3 hrs (are your disks fast enough?)
    10 Gbps network: 20 minutes (need really fast disks and filesystems)
  These figures assume some headroom left for other users
    Compare these speeds to:
      USB 2.0 portable disk
        20-30 hours to load 1 Terabyte
© 2013 FedEx
See Also: http://what-if.xkcd.com/31/

## Slide 9: Sample Data Transfer Rates
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/

## Slide 10: Use Case = End to End Exchange
Alice & Bob are collaborators
    Experts in their field
    Physically separated (common)
    Rely on networks, but are not IT experts (common & expected)
    They know their local IT staff. May also have an adversarial relationship with them (e.g. Alice and Bob are ‘troublemakers’ since they use the network, and expect it to work)
Alice & Bob want to embark on a new project
    Instrument @ one end, processing/analysis @ the other
    Keep in mind they know about the science, not about the technology in the middle
    Use infrastructure they are comfortable with, perhaps cobbled together by local support staff

## Slide 11: Meet Alice & Bob - They are Science Cats
INTERNETS
© 2013 Susan's School Days
© 2013 icanhascheezburger.com
HAI, I CAN HAZ DATA?
MOAR DATA 4 U
K THX BAI

## Slide 12: Expectations & Realities
© Dog Shaming 2012
"In any large system, there is always something broken.”
Jon Postel
Modern networks are large and complicated
Many users will encounter unforeseen (and therefore challenging) situations:
  Upgrading networks breaks them (loss of configuration, etc.)
  Synergy between the new and the old
  Statistical anomalies, e.g. that 7 year old interface will stop working eventually…
Mitigating the risk can (and should) be done in a number of ways:
    Analysis and alteration of architecture
    Careful thought to security/data policies in target areas
  Integration of software designed to exercise the network, and alert/visualize
  Capable hosts and tools for scientific activities

## Slide 13: Meet Alice & Bob; Sad Reality
INTERNETS
© 2013 Susan's School Days
© 2013 icanhascheezburger.com
HAI, I CAN HAZ DATA?
MOAR DATA 4 U
SOOO SLOOOW!
I CAN HAZ TECH SUPPORT?
© 2013 Berkeley Breathed
I CAN HAZ FEDEX?
© 2013 Renee Richardson photography

## Slide 14: Which leads us to the Science DMZ…
Significant commonality in issues encountered with science collaborations … and similar solution set
  The causes of poor data transfer performance fit into a few categories with similar solutions
    Un-tuned/under-powered hosts
      Packet loss issues
      Security devices
  A successful model has emerged – the Science DMZ
    This model successfully in use by CMS/ATLAS, ESG, NERSC, ORNL, ALS, and others
The Science DMZ is a design pattern for network performance.
  Not all implementations look the same, but share common features
  Some choices don’t make sense for everyone – Know Your Network
© 2013 icanhascheezburger.com

## Slide 15: The Science DMZ in 1 Slide
Consists of three key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus and GridFTP
Performance measurement/test node
  perfSONAR
Once it’s up, users often need training – Engagement is key
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
© 2013 Globus

## Slide 16: Science DMZ Background
The data mobility performance requirements for data intensive science are beyond what can typically be achieved using traditional methods
  Default host configurations (TCP, filesystems, NICs)
  Converged network architectures designed for commodity traffic
  Conventional security tools and policies
  Legacy data transfer tools (e.g. SCP)
  Wait-for-trouble-ticket operational models for network performance
The Science DMZ model describes a performance-based approach
  Dedicated infrastructure for wide-area data transfer
    Well-configured data transfer hosts with modern tools
    Capable network devices
    High-performance data path which does not traverse commodity LAN
  Proactive operational models that enable performance
    Well-deployed test and measurement tools (perfSONAR)
    Periodic testing to locate issues instead of waiting for users to complain
  Security posture well-matched to high-performance science applications
Notes: The Science DMZ model is a set of ideas – the diagrams that follow are examples.

## Slide 17: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)

## Slide 18: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Notes: On a 10 Gb/s LAN path the impact of low packet loss rates is minimal
On a 10 Gb/s WAN path the impact of low packet loss rates is enormous
Beyond your metro area, zero loss is essentially required for performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 19: How Do We Accommodate TCP?
High-performance wide area TCP flows must get loss-free service
  Sufficient bandwidth to avoid congestion
  Deep enough buffers in routers and switches to handle bursts
    Especially true for long-distance flows due to packet behavior
    No, this isn’t buffer bloat
Equally important – the infrastructure must be verifiable so that clean service can be provided
  Stuff breaks
    Hardware, software, optics, bugs, …
    How do we deal with it in a production environment?
  Must be able to prove a network device or path is functioning correctly
    Regular active tests should be run - perfSONAR
  Small footprint is a huge win
    Fewer the number of devices = easier to locate the source of packet loss
© 2013 icanhascheezburger.com

## Slide 20: Overview
Part 1:
  What is Science Engagement?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
  Globus Connect Personal
Part 4:
  perfSONAR
Part 5:
  SDN and the Science DMZ
Conclusions & Discussion

## Slide 21: Traditional Network DMZ
DMZ – “Demilitarized Zone”
  Network segment near the site perimeter with different security policy
  Commonly used architectural element for deploying WAN-facing services (e.g. email, DNS, web)
Traffic for WAN-facing services does not traverse the LAN
  WAN flows are isolated from LAN traffic
  Infrastructure for WAN services is specifically configured for WAN
Separation of security policy improves both LAN and WAN
  No conflation of security policy between LAN hosts and WAN services
  DMZ hosts provide specific services
  LAN hosts must traverse the same ACLs as WAN hosts to access DMZ
Do the same thing for science – Science DMZ

## Slide 22: The Data Transfer Superfecta: Science DMZ Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase

## Slide 23: Science DMZ Takes Many Forms
There are a lot of ways to combine these things – it all depends on what you need to do
  Small installation for a project or two
  Facility inside a larger institution
  Institutional capability serving multiple departments/divisions
  Science capability that consumes a majority of the infrastructure
Some of these are straightforward, others are less obvious
Key point of concentration: eliminate sources of packet loss / packet friction

## Slide 24: Ad Hoc DTN Deployment
Notes: DTN node deep within campus infrastructure.

## Slide 25: Legacy Method: Ad Hoc DTN Deployment
This is often what gets tried first
Data transfer node deployed where the owner has space
  This is often the easiest thing to do at the time
  Straightforward to turn on, hard to achieve performance
If lucky, perfSONAR is at the border
  This is a good start
  Need a second one next to the DTN
Entire LAN path has to be sized for data flows
Entire LAN path is part of any troubleshooting exercise
This usually fails to provide the necessary performance.
Notes: Previous slide is diagram for this; just say these things while showing previous slide

## Slide 26: A better approach: simple Science DMZ
Notes: Add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners
  Add-on to production infrastructure – lower risk

## Slide 27: Small-scale Science DMZ Deployment
Add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners
  Add-on to production infrastructure – lower risk
Notes: This text goes with previous slide

## Slide 28: Prototype Science DMZ Data Path

## Slide 29: Prototype With Virtual Circuits
Small virtual circuit prototype can be done in a small Science DMZ
  Perfect example is a Software Defined Networking (SDN) testbed
  Virtual circuit connection may or may not traverse border router
As with any Science DMZ deployment, this can be expanded as need grows
In this particular diagram, Science DMZ hosts can use either the routed or the circuit connection

## Slide 30: Virtual Circuit Prototype Deployment

## Slide 31: Support For Multiple Projects
Science DMZ architecture allows multiple projects to put DTNs in place
  Modular architecture
  Centralized location for data servers
This may or may not work well depending on institutional politics
  Issues such as physical security can make this a non-starter
  On the other hand, some shops already have service models in place
On balance, this can provide a cost savings – it depends
  Central support for data servers vs. carrying data flows
  How far do the data flows have to go?

## Slide 32: Multiple Projects

## Slide 33: Supercomputer Center Deployment
High-performance networking is assumed in this environment
  Data flows between systems, between systems and storage, wide area, etc.
  Global filesystem often ties resources together
    Portions of this may not run over Ethernet (e.g. IB)
    Implications for Data Transfer Nodes
“Science DMZ” may not look like a discrete entity here
  By the time you get through interconnecting all the resources, you end up with most of the network in the Science DMZ
  This is as it should be – the point is appropriate deployment of tools, configuration, policy control, etc.
Office networks can look like an afterthought, but they aren’t
  Deployed with appropriate security controls
  Office infrastructure need not be sized for science traffic

## Slide 34: Supercomputer Center

## Slide 35: Supercomputer Center Data Path

## Slide 36: Major Data Site Deployment
In some cases, large scale data service is the major driver
  Huge volumes of data – ingest, export
  Individual DTNs don’t exist here – data transfer clusters
Single-pipe deployments don’t work
  Everything is parallel
    Networks (Nx10G LAGs, soon to be Nx100G)
    Hosts – data transfer clusters, no individual DTNs
    WAN connections – multiple entry, redundant equipment
  Choke points (e.g. enterprise firewalls) cause problems

## Slide 37: Data Site – Architecture

## Slide 38: Distributed Science DMZ
Fiber-rich environment enables distributed Science DMZ
  No need to accommodate all equipment in one location
  Allows the deployment of institutional science service
WAN services arrive at the site in the normal way
Dark fiber distributes connectivity to Science DMZ services throughout the site
  Departments with their own networking groups can manage their own local Science DMZ infrastructure
  Facilities or buildings can be served without building up the business network to support those flows
Security is potentially more complex
  Remote infrastructure must be monitored
  Solutions depend on relationships with security groups

## Slide 39: Distributed Science DMZ – Dark Fiber

## Slide 40: Multiple Science DMZs – Dark Fiber

## Slide 41: Common Threads
Two common threads exist in all these examples
Accommodation of TCP
  Wide area portion of data transfers traverses purpose-built path
  High performance devices that don’t drop packets
Ability to test and verify
  When problems arise (and they always will), they can be solved if the infrastructure is built correctly
  Small device count makes it easier to find issues
  Multiple test and measurement hosts provide multiple views of the data path
    perfSONAR nodes at the site and in the WAN
    perfSONAR nodes at the remote site

## Slide 42: Network Research Project Requirements
Science DMZ model can be used to support research
Some research projects are networking research projects
  The network is both the environment and the subject of research
  Science DMZ is a good fit for several reasons
    Isolate research from production when research is in the unstable phase
    Separation of administrative control
Notes: Joe Breen Tale …

## Slide 43: Science DMZ With Separate Research Area
Notes: Research DMZ with separate connection to border router

## Slide 44: Science DMZ With Separate Research Area
Notes: Research DMZ as extension of production DMZ; can also be used to test new hardware before putting it into production.

## Slide 45: Science DMZ – Flexible Design Pattern
The Science DMZ design pattern is highly adaptable to research
Deploying a research Science DMZ is straightforward
  The basic elements are the same
    Capable infrastructure designed for the task
    Test and measurement to verify correct operation
    Security policy well-matched to the environment, application set is strictly limited to reduce risk
  Connect the research DMZ to other resources as appropriate
The same ideas apply to supporting an SDN effort
  Test/research areas for development
  Transition to production as technology matures and need dictates
  One possible trajectory follows…

## Slide 46: Science DMZ – Separate SDN Connection
Notes: Initial deployment brings SDN services to research DMZ via a separate link

## Slide 47: Science DMZ – Production SDN Connection
Notes: Once SDN software for the switch platform is solid and operational models are clear, production Science DMZ supports SDN

## Slide 48: Science DMZ – SDN Campus Border
Notes: When the entire production path supports SDN, SDN is another production service on the Science DMZ and we’re back to the original picture
ESnet5 supports routed traffic and OSCARS on the same platform in a similar way

## Slide 49: Equipment – Routers and Switches
Requirements for Science DMZ gear are different
  No need to go for the kitchen sink list of services
  A Science DMZ box only needs to do a few things, but do them well
  Support for the latest LAN integration magic with your Windows Active Directory environment is probably not super-important
  A clean architecture is important
    How fast can a single flow go?
    Are there any components that go slower than interface wire speed?
There is a temptation to go cheap
  Hey, it only needs to do a few things, right?
  You typically don’t get what you don’t pay for
    (You sometimes don’t get what you pay for either)

## Slide 50: Common Circumstance: Multiple Ingress Data Flows, Common Egress
Hosts will typically send packets at the speed of their interface (1G, 10G, etc.)
  Instantaneous rate, not average rate
  If TCP has window available and data to send, host sends until there is either no data or no window
Hosts moving big data (e.g. DTNs) can send large bursts of back-to-back packets
  This is true even if the average rate as measured over seconds is slower (e.g. 4Gbps)
  On microsecond time scales, there is often congestion
  Router or switch must queue packets or drop them

## Slide 51: Output Queue Drops – Common Locations

## Slide 52: Router and Switch Output Queues
Interface output queue allows the router or switch to avoid causing packet loss in cases of momentary congestion
In network devices, queue depth (or ‘buffer’) is often a function of cost
  Cheap, fixed-config LAN switches (especially in the 10G space) have inadequate buffering. Imagine a 10G ‘data center’ switch as the guilty party
  Cut-through or low-latency Ethernet switches typically have inadequate buffering (the whole point is to avoid queuing!)
Expensive, chassis-based devices are more likely to have deep enough queues
  Juniper MX and Alcatel-Lucent 7750 used in ESnet backbone
  Other vendors make such devices as well - details are important
  Thx to Jim: http://people.ucsc.edu/~warner/buffer.html
This expense is one driver for the Science DMZ architecture – only deploy the expensive features where necessary

## Slide 53: “Please tell me – what should I buy??”
We get this question a lot
  Hard to answer for several reasons
  Some have to do with us, and some have to do with you
We can’t endorse anybody
  We can’t recommend one business over another
  No, really – we’ll get slapped
  We are also unable to accept any liability
We have no idea what’s right for your environment
  Different networks are different – specific vendor, multi-vendor, single vendor, management style, home-grown tools, commercial tools, …
  Our goal is to describe our understanding of what works and why
  You are free to use that information in whatever way you see fit
Know Your Network

## Slide 54: You are not alone
Lots of community resources
  Ask folks who have already done it
  Ask the Science DMZ mailing list: sciencedmz@es.net
Vendors can be very helpful – just ask the right questions
  Request an eval box (or preferably two)
  Ask for config examples to implement a particular feature
    E.g. “Please give me the QoS config for the following:”
      1 queue for network control (highest priority) – 5% of interface buffer memory
      1 queue configured for tail-drop (lower priority) – 95% of interface buffer memory
      With that config, how many milliseconds of buffer are in the tail-drop queue when measured at interface wire speed?

## Slide 55: Some Stuff We Think Is Important
Deep interface queues
  Output queue or VOQ – doesn’t matter
  What TCP sees is what matters – fan-in is *not* your friend
  No, this isn’t buffer bloat
Good counters
  We like the ability to reliably count *every* packet associated with a particular flow, address pair, etc
    Very helpful for debugging packet loss
    Must not affect performance (just count it, don’t punt it)
    sflow support if possible
  If the box is going to drop a packet, it should increment a counter somewhere indicating that it dropped the packet
    Magic vendor permissions and hidden commands should not be necessary
    Some boxes just lie – run away!
Single-flow performance should be wire-speed

## Slide 56: Experience With 100G Equipment
ESnet experiences
  Advanced Networking Initiative
  ESnet5 production 100G network
  Helping other people debug their stuff
Important takeaways
  R&E requirements are outside the design spec for most gear
    Results in platform limitations – sometimes can’t be fixed
    You need to be able to identify those limitations before you buy
  R&E requirements are outside the test scenarios for most vendors
    Bugs show up when R&E workload is applied
    You need to be able to troubleshoot those scenarios

## Slide 57: Platform Limitations
We have seen significant limitations in 100G equipment from all vendors with a major presence in R&E
  100G single flow not supported
    Channelized forwarding plane
    Unexplained limitations
    Sometimes the senior sales engineers don’t know!
  Non-determinism in the forwarding plane
    Performance depends on features used (i.e. config-dependent)
    Packet loss that doesn’t show up in counters anywhere
If you can’t find it, nobody will tell you about it
  Vendors don’t know or won’t say
  Watch how you write your procurements
Second-generation equipment seems to be much better
Vendors have been responsive in rolling new code to fix problems

## Slide 58: They Don’t Test For This Stuff
Most sales engineers and support engineers don’t have access to 100G test equipment
  It’s expensive
  Setup of scenarios is time-consuming
R&E traffic profile is different than their standard model
  IMIX (Internet Mix) traffic is normal test profile
    Aggregate web browsers, email, YouTube, Netflix, etc.
    Large flow count, low per-flow bandwidth
    This is to be expected – that’s where the market is
  R&E shops are the ones that get the testing done for R&E profile
    SCinet at Supercomuting conference provides huge value
    But, in the end, it’s up to us – the R&E community

## Slide 59: New Technology, New Bugs
Bugs happen.
  Data integrity (traffic forwarded, but with altered data payload)
  Packet loss
  Interface wedge
  Optics flaps
Monitoring systems are indispensable
Finding and fixing issues is sometimes hard
  Rough guess – difficulty exponent is degrees of freedom
    Vendors/platforms, administrative domains, time zones
Takeaway – don’t skimp on test gear (at least maintain your perfSONAR boxes)

## Slide 60: Summary So Far
There is no single “correct” way build a Science DMZ
  These are design patterns, not rules
It depends on things like:
  site requirements
  existing resources
  availability of dark fiber
  budget
The main point is to reduce the opportunities for packet loss, and be able to find loss if it’s present

## Slide 61: Science DMZ Architecture
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 62: Extra Slides

## Slide 63: Motivation
Science data increasing both in volume and in value
  Higher instrument performance
  Increased capacity for discovery
  Analyses previously not possible
Lots of promise, but only if scientists can actually work with the data
  Data has to get to analysis resources
  Results have to get to people
  People have to share results
Common pain point – data mobility
  Movement of data between instruments, facilities, analysis systems, and scientists is a gating factor for much of data intensive science
  Data mobility is not the only part of data intensive science – not even the most important part
  However, without data mobility data intensive science is hard
We need to move data – how can we do it consistently well?

## Slide 64: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is important?
  Correctness
  Consistency
  Performance
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
Notes: If networks are so important, we need to make them useful