## Slide 1: Introduction to Globus Connect
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 2: Overview
Part 1:
  What is Science Engagement?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
  Globus Connect Personal
Part 4:
  perfSONAR
Part 5:
  SDN and the Science DMZ
Conclusions & Discussion

## Slide 3: The Data Transfer Superfecta: Science DMZ Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase
Notes: Quick roadmap in the Science DMZ model
Data transfer nodes (both hardware and software) and configuration
Me: Hardware part
Eli: software tools and performance tuning

## Slide 4
Notes: Quick refresher…
Data transfer node (or DTN) is a dedicated server specifically made for high-performing, wide-area data transfers
This is usually connected to a Science DMZ switch connected to the site border router (in a basic campus-based Science DMZ)

## Slide 5: Introduction to Globus Some materials courtesy of Raj Kettimuthu (kettimut@anl.gov) and the Computation Institute, University of Chicago, Argonne National Laboratory https://www.globus.org
Notes: Now onto the first part of the DTN
the Hardware selection
For importance and completeness,
we have to start from the bottom up to build these servers—there is not always a common “out of the box” solution for deploying these (as everyone has different needs, architecture etc.) so it is important to point out a few key things related to the hardware to reduce potential problems and bottlenecks.
We do also have a few reference designs which help out with DTNs as well (on fasterdata.es.net)

## Slide 6: “I need a good place to store / backup / archive my (big) research data”
Public Cloud Archive
Mass Store
Campus Store
6 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory
“Using my own Storage” “Paying to use someone else’s”
Notes: A number of common patterns, each supported by Globus—plus services deployed on various campus resources. Explains why so many endpoints!

## Slide 7: “I need to easily, quickly, & reliably move or mirror portions of my data to other places.”
Research Computing HPC Cluster
Lab Server
Campus Home Filesystem
Desktop Workstation
Personal Laptop
XSEDE Resource
Public Cloud
7 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 8: “I need to easily and securely share my data with my colleagues at other institutions & facilities.”
8 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 9: “I need to get data from a scientific instrument to my analysis server.”
Next Gen
Sequencer
Light Sheet Microscope
MRI
Advanced Light Source
9 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 10: Challenge: Manage research data as easily as…
…our pictures
…home entertainment
…our e-mail
10 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 11: What is Globus?
Big data transfer, and sharing…
… delivered via SaaS …
… that is simple, secure, and fast…
… directly from your own storage systems
11 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 12: Reliable, secure, high-performance file transfer
“Fire-and-forget” transfers
Automatic fault recovery
Seamless security integration
Powerful GUI and APIs
Data
Source
Data
Destination
User initiates transfer request
1
Globus
moves and syncs files
2
Globus
notifies user
3
12 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 13: Ability to purchase simple, secure sharing off existing storage systems
Data
Source
User A selects file(s) to share, selects user or group, and sets permissions
1
Globus tracks shared files; no need to move files to cloud storage!
2
User B logs in to Globus and accesses shared file
3
Easily share large data with any user or group
No cloud storage required
13 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 14: Globus is SaaS
Web, command line, and REST interfaces
  Facilities different models of data movement (e.g. user initiated vs. scripted)
Reduced IT operational costs
New features automatically available
Consolidated support & troubleshooting available under service plans
Easy to add your laptop, server, cluster, supercomputer, etc. with Globus Connect
14 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 15: Globus Connect Hands On

## Slide 16: Account Sign Up (or Login)
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 17: Create Account (if needed)
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 18: Logging In (Globus or Alternate)
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 19: Dashboard
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 20: Downloading Globus Connect Personal
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 21: Installing & Starting Software
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 22: Web View: Active Endpoint
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 23: Transfer File
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 24: Transfer File
One Side:
  Find your endpoint (e.g. type your username followed by the ‘#’ symbol – should auto-complete)
Other Side:
  Type ‘esnet#’ and select either ‘lbl’ or ‘anl’ (‘bnl’ is down for maintenance)
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 25: Transfer File
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 26: Transfer File
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 27: Use Cases

## Slide 28
28 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 29: Globus increasingly used to build campus-wide data services
Source: University of Nebraska
Holland Computing Center
Enable campus computing facilities to better utilize high performance network infrastructure
29 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 30: Typical deployment
Science DMZ
+
Globus
Details at: fasterdata.es.net
30 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 31: Firewall configuration
Allow inbound connections to port 2811 (GridFTP control channel), 7512 (MyProxy CA), 443 (OAuth)
Allow inbound connections to ports 50000-51000 (GridFTP data channel)
  If transfers to/from this machine will happen only from/to a known set of endpoints (not common), you can restrict connections to this port range only from those machines
If your firewall restricts outbound connections
  Allow outbound connections if the source port is in the range 50000-51000
31 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 33: “Double Copy” Workflow
DTN sits on border, no filesystem mount into campus resources
  E.g. use of the Globus GUI moves data from remote location to DTN
  Needs to get from DTN into campus
What can be done?
  For short RTT, rsync or scp (with the HPN patch!) could be used
  Create 2nd Globus endpoint inside of campus – move data again through interface
Suggestion – to foster adoption by users, the remote mount (via NFS, LUSTER, whatever) into the campus is a huge selling point. The data ‘shows up’ where it is needed
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 34: “Single Copy” Workflow
DTN sits on border – has a file system mount in through the firewall
  Data orchestration done via the Globus GUI
  When the user attempts to use a cluster/SC resource with the same mounts, the data is waiting for them
Why this works:
  Short RTT from border DTN through campus firewall, using protocols like NFS, can tolerate some loss and delay.
  User doesn’t need to change much of their normal behavior – they just need to learn to pick out the campus DTN as the destination for files
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 35
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://fasterdata.es.net

## Slide 36: Extra Slides

## Slide 37: Globus Connect Server (Optional Hands-On)

## Slide 38: Globus Connect Server https://www.globus.org/globus-connect-server
Similar to Globus Connect Personal – but designed for multi-user shared environments like a DTN
  Typically administered by a campus sysadmin for the benefit of many users
  Allows for multiple forms of authentication (e.g. federated identify, local accounts, Globus credentials)
  Integrates with local and remote (e.g. filesystem mounted) storage.
The following is an overview of how to enable this service on a VM
  Some features such as sharing are premium offerings.
  The basic activity of file transfer is still a free and supported activity.
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 39: Globus Connect Server
Create endpoint in minutes; no complex GridFTP install
Enable all users with local accounts to transfer files
Native packages: RPMs and DEBs
Also available as part of the Globus Toolkit
Local Storage System
(HPC cluster, campus server, …)
Globus Connect Server
MyProxy Online CA
GridFTP Server
Local system users
39 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 40: What we are going to do:
Install Globus Connect Server
Access server as local admin e.g. “root”
Update repo
Install package
Setup Globus Connect Server
Server
ssh
Test Endpoint
Log into Globus (using Globus username)
Transfer a file
1
2
3
Access the newly created endpoint (as local user e.g. “yourname”)
4
40 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 41: Quick Start https://support.globus.org/entries/23857088
Basics:
  Ensure NTP is running and synchronized (use ntpq –p to check this)
  Host has to be connected to the internet, with a real hostname
    Wrong:
    Right:
  Any older version of Globus must be removed (ensures libraries are compatible)
  The system supports the ‘login’ command – this is normal, unless it has been explicitly configured to disallow terminal logins.
Note the following instructions are for RHEL (CentOS/Fedora/SL) systems. Instructions are available on the Globus website for Debian-based installations
A root or sudo-capable account is required for some installation.
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 42: Quick Start (CentOS 5)
If you are not using EPEL, install EPEL:
  http://fedoraproject.org/wiki/EPEL/FAQ
Locate your system’s RPM:
  http://www.globus.org/ftppub/gt5/5.2/stable/installers/repo/
Run a yum update and yum clean all
Download & Install the Repository RPM:
  sudo rpm –hUv http://www.globus.org/ftppub/gt5/5.2/stable/installers/repo/Globus-5.2.stable-config.centos-5-1.noarch.rpm
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 43: Quick Start (CentOS 5)
Install the package via yum:
  yum install globus-connect-server
  Note that around 60 pages will be pulled in, depending on your systems initial configuration
  You will be asked to import a GPG signing key from Globus.org
  A certificate will be created for your host and ‘self signed’. Those that wish to have their certificate signed by a reputable authority can choose to do so. Outside entities that connect to the self-signed certificate will be asked about trust.
Edit the /etc/globus-connect-server.conf file:
  [Endpoint]
  Name= myendpointname
  Public = True
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 44: Configuration file walkthrough
Structure based on .ini format:
  [Section]
  Option
Most common options to configure
  Hostname
  Public
  RestrictedPaths
  Sharing
  SharingRestrictedPaths
  IdentityMethod (CILogon, OAuth)
More details are available at: support.globus.org/forums/22095911
44 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 45: Quick Start (CentOS 5)
Run globus-connect-server-setup
  Note that you will be prompted for a Globus username/password, this will tie the resource to that user
  Facilities such as XSEDE/ESnet maintain a ‘user’ account for all instances they have setup
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 46
46 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 47: Activating via the Web
Log into the web with your Globus Credentials (same as you used in previous step and w/ Globus Connect Personal). Endpoint should show up:
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 48: Activating via the Web
The endpoint needs to be ‘activated’ before it can be used:
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 49: Activating via the Web
Supply account information FROM THE HOST, e.g. the following is an account that is already active on the server we used before:
Note that if you are using federated identiy, this step may be different. Consult Globus documentation
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 50: Activating via the Web
After authenticating, the endpoint is active for a limited amount of time.
The credentials will need to be refreshed, consult documentation to change the expiration time.
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 51: Firewall configuration
Allow inbound connections to port 2811 (GridFTP control channel), 7512 (MyProxy CA), 443 (OAuth)
Allow inbound connections to ports 50000-51000 (GridFTP data channel)
  If transfers to/from this machine will happen only from/to a known set of endpoints (not common), you can restrict connections to this port range only from those machines
If your firewall restricts outbound connections
  Allow outbound connections if the source port is in the range 50000-51000
51 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 53: Transfer (Again)
Notes: What composes a DTN
A DTN server is made of several subsystems:
  Storage
  Networking
  Motherboard
  Chassis
Each needs to perform optimally for the DTN workflow—any of these things components can be the bottleneck if you’re not careful
There is always one thing that prevents you from going faster—eliminate as many bottlenecks as possible with hardware as a start
Only job is big sequential writes and big sequential reads—large file IO
_______________
Also please note the workflow we are optimizing for here is
sequential reads/write of large files, and a moderate number of high bandwidth flows.
A Data Transfer Node is not a processing, rendering, server. Its only workflow is:
Sender host:
1) read data from the storage subsystem
2) send it to the receiver host
Receiver host:
1) read data from the network
2) write it onto the storage subsystem

## Slide 54: Advanced Configuration

## Slide 55: Globus Connect Server Advanced Configuration
Alternative Proxy Configuration
Sharing
Customizing filesystem access
Using host certificates
Using CILogon certificates
Enabling sharing on GT GridFTP server
Configuring multiple GridFTP servers
Setting up an anonymous endpoint
55 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 56: MyProxy OAuth server
Web-based endpoint activation
  Sites run a MyProxy OAuth server
    MyProxy OAuth server in Globus Connect Server
  Users enter username/password only on site’s webpage to activate an endpoint
  Globus gets short-term X.509 credential via OAuth protocol
MyProxy without Oauth
  Site passwords flow through Globus to site MyProxy server
  Globus does not store passwords
  Still a security concern for some sites
56 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 57
57 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 58: Enable sharing on your endpoint
sudo vim /etc/globus-connect-server.conf
Uncomment [GridFTP] Sharing = True
Go to the Web UI Start Transfer page
Select endpoint <username>#<endpointname>
Users can create shared endpoints that point to a specific directory on this endpoint and share with other Globus users
  Note this is a premium offering
58 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 59: Path Restriction
Default configuration:
  All paths allowed, access control handled by the OS
Use RestrictPaths to customize
  Specifies a comma separated list of full paths that clients may access
  Each path may be prefixed by R (read) and/or W (write), or N (none) to explicitly deny access to a path
  '~’ for authenticated user’s home directory, and * may be used for simple wildcard matching.
E.g. Full access to home directory, read access to /data:
  RestrictPaths = RW~,R/data
E.g. Full access to home directory, deny hidden files:
  RestrictPaths = RW~,N~/.*
59 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory
Notes: As the name suggests, it is a server version of Globus Connect, a one click install of GridFTP server for laptops and desktops

## Slide 60: Sharing Path Restriction
Define additional restrictions on which paths your users are allowed to create shared endpoint
Use SharingRestrictPaths to customize
  Same syntax as RestrictPaths
E.g. Full access to home directory, deny hidden files:
  RestrictPaths = RW~,N~/.*
E.g. Full access to public folder under home directory:
  RestrictPaths = RW~/public
E.g. Full access to /project, read access to /scratch:
  RestrictPaths = RW/project,R/scratch
60 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 61: Control sharing access to specific accounts
SharingStateDir can be used to control sharing access to individual accounts
For instance, with SharingStateDir = "/var/globusonline/sharing/$USER”, user "bob" would be enabled for sharing only if a path exists with the name "/var/globusonline/sharing/bob/" and is writable by bob.
61 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 62: Using a host certificate for GridFTP
You can use your GridFTP server with non-Globus clients
  Requires a host certificate, e.g. from OSG
Comment out
  FetchCredentialFromRelay = True
Set
  CertificateFile = <path_to_host_certificate>
  KeyFile = <path_to_private key_associated_with_host_certificate>
  TrustedCertificateDirectory = <path_to_trust_roots>
62 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 63: Single Sign-On with InCommon/CILogon
Requirements
  Your organization’s Shibboleth server must release the ePPN attribute to CILogon
  Your local resource account names must match your institutional identity (InCommon ID)
Set AuthorizationMethod = CILogon in the Globus Connect Server configuration
Set CILogonIdentityProvider = <your_institution_as_listed_in_CILogon_identity_provider_list>
Add CILogon CA to your trustroots
  /var/lib/globus-connect-server/grid-security/certificates/
  Visit ca.cilogon.org/downloads for certificates
63 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 64: Enabling Sharing on a GT GridFTP Installation
Get Globus Sharing CA certificates http://toolkit.globus.org/toolkit/docs/latest-stable/gridftp/securityd2b.tar.gz
Add to your trusted certificates directory (/etc/grid-security/certificates)
Use '-sharing-dn' option in the server as follows: globus-gridftp-server -sharing-dn "/C=US/O=Globus Consortium/OU=Globus Connect User/CN=__transfer__”
Use '-sharing-rp' option to restrict the file paths allowed for sharing: globus-gridftp-server -sharing-rp <path>
http://toolkit.globus.org/toolkit/docs/5.2/5.2.5/gridftp/admin/#idp7491840
64 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 65: Deployment Scenarios
Globus Connect Server components
  Globus-connect-server-io, -id, -web
Default: -io and –id (no –web) on single server
Common options
  Multiple –io servers for load balancing, failover, and performance
  No -id server, e.g. third-party IdP such as CILogon
  -id on separate server, e.g. non-DTN nodes
  -web on either –id server or separate server for OAuth interface
65 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory

## Slide 66: Setting up multiple –io servers
Guidelines
  Use the same .conf file on all servers
  First install on the server running the –id component, then all others
Install Globus Connect Server on all servers
Edit .conf file on one of the servers and set [MyProxy] Server to the hostname of the server you want the –id component installed on
Copy the following files/dirs to all servers
  /etc/globus-connect-server.conf
  /var/lib/globus-connect-server/grid-security/certificates/
Run globus-connect-server-setup on the server running the –id component
Run globus-connect-server-setup on all other servers
Repeat steps 2-5 as necessary to update configurations
66 – © 2014 Computation Institute, University of Chicago, Argonne National Laboratory