## Slide 1: Network Performance Monitoring with perfSONAR
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://www.perfsonar.net

## Slide 2: Overview
Part 1:
  What is Science Engagement?
  Science DMZ Introduction & Motivation
  Science DMZ Architecture
Part 2:
  Science DMZ Security Best Practices
Part 3:
  The Data Transfer Node
  Data Transfer Tools
  Globus Connect Personal
Part 4:
  perfSONAR
Part 5:
  SDN and the Science DMZ
Conclusions & Discussion

## Slide 3: The Data Transfer Superfecta: “Science DMZ” Model
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase

## Slide 4: perfSONAR Outline
Performance Introduction & Motivation
perfSONAR Preliminaries
Deployment & Regular Testing
Maddash Installation & Use
Tool Use
Common Pitfalls
Debugging Strategies
Use Cases & Success Stories

## Slide 5: Test and Measurement – Keeping the Network Clean
The wide area network, the Science DMZ, and all its systems can be functioning perfectly
Eventually something is going to break
  Networks and systems are built with many, many components
  Sometimes things just break – this is why we buy support contracts
Other problems arise as well – bugs, mistakes, whatever
We must be able to find and fix problems when they occur
Why is this so important? Because we use TCP!
Notes: Remember one of the pieces was perfSONAR?

## Slide 6: Where Are The Problems?
Source
Campus
Backbone
S
NREN
Congested or faulty links between domains
Congested intra- campus links
D
Destination
Campus
Latency dependant problems inside domains with small RTT
Regional

## Slide 7: Local Testing Will Not Find Everything
Source
Campus
R&E
Backbone
Regional
D
S
Destination
Campus
Regional
Performance is good when RTT is < ~10 ms
Performance is poor when RTT exceeds ~10 ms
Switch with small buffers

## Slide 8: Soft Network Failures
Soft failures are where basic connectivity functions, but high performance is not possible.
TCP was intentionally designed to hide all transmission errors from the user:
  “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From IEN 129, RFC 716)
Some soft failures only affect high bandwidth long RTT flows.
Hard failures are easy to detect & fix
  soft failures can lie hidden for years!
One network problem can often mask others

## Slide 9: Network Monitoring
All networks do some form monitoring.
  Addresses needs of local staff for understanding state of the network
    Would this information be useful to external users?
    Can these tools function on a multi-domain basis?
Beyond passive methods, there are active tools.
    E.g. often we want a ‘throughput’ number. Can we automate that idea?
    Wouldn’t it be nice to get some sort of plot of performance over the course of a day? Week? Year? Multiple endpoints?
perfSONAR = Measurement Middleware

## Slide 10: perfSONAR Outline
Performance Introduction & Motivation
perfSONAR Preliminaries
Deployment & Regular Testing
Maddash Installation & Use
Tool Use
Common Pitfalls
Debugging Strategies
Use Cases & Success Stories

## Slide 11: perfSONAR
All the previous Science DMZ network diagrams have little perfSONAR boxes everywhere
  The reason for this is that consistent behavior requires correctness
  Correctness requires the ability to find and fix problems
    You can’t fix what you can’t find
    You can’t find what you can’t see
    perfSONAR lets you see
Especially important when deploying high performance services
  If there is a problem with the infrastructure, need to fix it
  If the problem is not with your stuff, need to prove it
    Many players in an end to end path
    Ability to show correct behavior aids in problem localization

## Slide 12: What is perfSONAR?
perfSONAR is a tool to:
  Set network performance expectations
  Find network problems (“soft failures”)
  Help fix these problems
  All in multi-domain environments
These problems are all harder when multiple networks are involved
perfSONAR is provides a standard way to publish active and passive monitoring data
  This data is interesting to network researchers as well as network operators
Notes: Enables Federation
  Service oriented
  Designed with ‘multi-domain’ in mind
Brings together useful tools to address different needs
  Several active and passive tools
  Interface to configure regular testing
  Diagnostic tools ready with ‘0 configuration’
Easy to install, easy to use
  ISO image can be burned to CD/USB key
  ‘Wizard’ interface for configuration
Encouraging people to deploy ‘known good’ measurement points near domain boundaries
  “known good” = hosts that are well configured, enough memory and CPU to drive the network, proper TCP tuning, clean path, etc.
Community Adoption
  Over 600 instances seen world wide as of early May
  20+ countries
  100s of domains

## Slide 13: perfSONAR Toolkit
The “perfSONAR Toolkit” is an open source implementation and packaging of the perfSONAR measurement infrastructure and protocols
  http://www.perfsonar.net
All components are available as RPMs, and bundled into a CentOS 6-based “netinstall” and a “Live CD”
  perfSONAR tools are much more accurate if run on a dedicated perfSONAR host, not on the DTN
Very easy to install and configure
  Usually takes less than 30 minutes

## Slide 14: Toolkit “Beacon” Use Case
The general use case is to establish some set of tests to other locations/facilities
To answer the what/why questions:
  Regular testing with select tools helps to establish patterns – how much bandwidth we would see during the course of the day – or when packet loss appears
  We do this to ‘points of interest’ to see how well a real activity (e.g. Globus transfer) would do.
If performance is ‘bad’, don’t expect much from the data movement tool

## Slide 15: Deployment By The Numbers
Last updated August 2014. Adoption trend increases with each release. CC-NIE and innovation platform helped as well.

## Slide 16: http://stats.es.net/ServicesDirectory/ - 1200+ as of August 2014

## Slide 17: perfSONAR Outline
Performance Introduction & Motivation
perfSONAR Preliminaries
Deployment & Regular Testing
Maddash Installation & Use
Tool Use
Common Pitfalls
Debugging Strategies
Use Cases & Success Stories

## Slide 18: Importance of Regular Testing
We can’t wait for users to report problems and then fix them (soft failures can go unreported for years!)
Things just break sometimes
  Failing optics
  Somebody messed around in a patch panel and kinked a fiber
  Hardware goes bad
Problems that get fixed have a way of coming back
  System defaults come back after hardware/software upgrades
  New employees may not know why the previous employee set things up a certain way and back out fixes
Important to continually collect, archive, and alert on active throughput test results

## Slide 19
Use the correct tool for the Job
  To determine the correct tool, maybe we need to start with what we want to accomplish …
What do we care about measuring?
  Packet Loss, Duplication, out-of-orderness (transport layer)
  Achievable Bandwidth (e.g. “Throughput”)
  Latency (Round Trip and One Way)
  Jitter (Delay variation)
  Interface Utilization/Discards/Errors (network layer)
  Traveled Route
  MTU Feedback
The Metrics

## Slide 20
perfSONAR Dashboard: http://ps-dashboard.es.net

## Slide 21: Regular perfSONAR Tests
We run regular tests to check for two things
  TCP throughput
  One way delay and packet loss
perfSONAR has mechanisms for managing regular testing between perfSONAR hosts
  Statistics collection and archiving
  Graphs
  Dashboard display
  Integrate with NAGIOS
This infrastructure is deployed now – perfSONAR hosts at facilities can take advantage of it
At-a-glance health check for data infrastructure

## Slide 22: Develop a Test Plan
What are you going to measure?
  Achievable bandwidth
    2-3 regional destinations
    4-8 important collaborators
    4-8 (more if you are willing, especially to start) times per day to each destination
    20-30 second tests within a region, longer across oceans and continents
  Loss/Availability/Latency
    OWAMP: ~10-20 collaborators over diverse paths
  Interface Utilization & Errors (via SNMP)
What are you going to do with the results?
  NAGIOS Alerts
  Reports to user community
  Dashboard

## Slide 23: Host Considerations
http://psps.perfsonar.net/toolkit/hardware.html
Dedicated perfSONAR hardware is best
  Server class is a good choice
  Desktop/Laptop/Mini (Mac, Shuttle) can be problematic, but work in a diagnostic capacity
Other applications will perturb results
Separate hosts for throughput tests and latency/loss tests is preferred
  Throughput tests can cause increased latency and loss
  Latency tests on a throughput host are still useful however
1Gbps vs 10Gbps testers
  There are a number of problem that only show up at speeds above 1Gbps
Virtual Machines do not always work well as perfSONAR hosts (use specific)
  Clock sync issues are a bit of a factor
  throughput is reduced significantly for 10G hosts
  VM technology and motherboard technology has come a long way, YMMV
  NDT/NAGIOS/SNMP/1G BWCTL are good choices for a VM, OWAMP/10G BWCTL are not

## Slide 24: perfSONAR Deployment Locations
Critical to deploy such that you can test with useful semantics
perfSONAR hosts allow parts of the path to be tested separately
  Reduced visibility for devices between perfSONAR hosts
  Must rely on counters or other means where perfSONAR can’t go
Effective test methodology derived from protocol behavior
  TCP suffers much more from packet loss as latency increases
  TCP is more likely to cause loss as latency increases
  Testing should leverage this in two ways
    Design tests so that they are likely to fail if there is a problem
    Mimic the behavior of production traffic as much as possible
  Note: don’t design your tests to succeed
    The point is not to “be green” even if there are problems
    The point is to find problems when they come up so that the problems are fixed quickly
Notes: A lot of people want to prove that they are not the problem, and design their tests to succeed. This is not helpful.

## Slide 25: Sample Site Deployment

## Slide 26: perfSONAR Outline
Performance Introduction & Motivation
perfSONAR Preliminaries
Deployment & Regular Testing
Maddash Installation & Use
Tool Use
Common Pitfalls
Debugging Strategies
Use Cases & Success Stories

## Slide 27: Maddash & The Mesh Config
Measurement results are more useful when they can be “seen”, because this implies they will be acted on.
Maddash is a software package that can be used to visualize the results of many perfSONAR tests
The Mesh Config is a way to manage multiple nodes, by giving them a uniform testing schedule
  E.g. this is in contrast to the other method of configuration we d-did – manually entering our tests.
  Changes node from ‘testing as an island’ to being a part of a larger testing strategy

## Slide 28: Performance Island

## Slide 29: Performance Coordination

## Slide 30: Maddash Server Installation

## Slide 31: The Final Result
If you set up at home:
  Organize who will be in it, and decide if you want to do mainly disjoint or mesh testing
  Get the dashboard up first, along with the full config
  Get the remote sites to configure the mesh, and start to review the colors of the dashboard
    Could take some time to get ‘right’
Example:
  http://ps-dashboard.es.net

## Slide 32: perfSONAR Outline
Performance Introduction & Motivation
perfSONAR Preliminaries
Deployment & Regular Testing
Maddash Installation & Use
Tool Use
Common Pitfalls
Debugging Strategies
Use Cases & Success Stories

## Slide 33: Tool Usage
All of the previous examples were discovered, debugged, and corrected through the aide of the tools on the pS Performance Toolkit
Some are run in a diagnostic (e.g. one off) fashion, others are automated
I will go over diagnostic usage of some of the tools:
    OWAMP
    BWCTL

## Slide 34: Hosts Used:
BWCTL Hosts (10G)
    wash-pt1.es.net (McLean VA)
    sunn-pt1.es.net (Sunnyvale CA)
OWAMP Hosts (1G)
    wash-owamp.es.net (McLean VA)
    sunn-owamp.es.net (Sunnyvale CA)
Path
    ~60ms RTT
    traceroute to sunn-owamp.es.net (198.129.254.78), 30 hops max, 60 byte packets
    1 198.124.252.125 (198.124.252.125) 0.163 ms 0.149 ms 0.138 ms
    2 washcr5-ip-c-washsdn2.es.net (134.55.50.61) 0.655 ms washcr5-ip-a-washsdn2.es.net (134.55.42.33) 0.991 ms washcr5-ip-c-washsdn2.es.net (134.55.50.61) 1.324 ms
    3 chiccr5-ip-a-washcr5.es.net (134.55.36.45) 17.884 ms 17.939 ms 18.217 ms
    4 kanscr5-ip-a-chiccr5.es.net (134.55.43.82) 28.980 ms 29.066 ms 29.295 ms
    5 denvcr5-ip-a-kanscr5.es.net (134.55.49.57) 39.515 ms 39.601 ms 39.877 ms
    6 sacrcr5-ip-a-denvcr5.es.net (134.55.50.201) 60.382 ms 60.210 ms 60.437 ms
    7 sunncr5-ip-a-sacrcr5.es.net (134.55.40.6) 63.067 ms 68.035 ms 68.266 ms
    8 sunn-owamp.es.net (198.129.254.78) 62.462 ms 62.445 ms 62.436 ms

## Slide 35: Forcing Bad Performance (to illustrate behavior)
Add 10% Loss to a specific host
  sudo /sbin/tc qdisc delete dev eth0 root
  sudo /sbin/tc qdisc add dev eth0 root handle 1: prio
  sudo /sbin/tc qdisc add dev eth0 parent 1:1 handle 10: netem loss 10%
  sudo /sbin/tc filter add dev eth0 protocol ip parent 1:0 prio 3 u32 match ip dst 198.129.254.78/32 flowid 1:1
Add 10% Duplication to a specific host
  sudo /sbin/tc qdisc delete dev eth0 root
  sudo /sbin/tc qdisc add dev eth0 root handle 1: prio
  sudo /sbin/tc qdisc add dev eth0 parent 1:1 handle 10: netem duplicate 10%
  sudo /sbin/tc filter add dev eth0 protocol ip parent 1:0 prio 3 u32 match ip dst 198.129.254.78/32 flowid 1:1
Add 10% Corruption to a specific host
    sudo /sbin/tc qdisc delete dev eth0 root
    sudo /sbin/tc qdisc add dev eth0 root handle 1: prio
    sudo /sbin/tc qdisc add dev eth0 parent 1:1 handle 10: netem corrupt 10%
    sudo /sbin/tc filter add dev eth0 protocol ip parent 1:0 prio 3 u32 match ip dst 198.129.254.78/32 flowid 1:1
Reorder packets: 50% of packets (with a correlation of 75%) will get sent immediately, others will be delayed by 75ms.
    sudo /sbin/tc qdisc delete dev eth0 root
    sudo /sbin/tc qdisc add dev eth0 root handle 1: prio
    sudo /sbin/tc qdisc add dev eth0 parent 1:1 handle 10: netem delay 10ms reorder 25% 50%
    sudo /sbin/tc filter add dev eth0 protocol ip parent 1:0 prio 3 u32 match ip dst 198.129.254.78/32 flowid 1:1
Reset things
    sudo /sbin/tc qdisc delete dev eth0 root

## Slide 36: Its All About the Buffers
A prequel to using BWCTL – The Bandwidth Delay Product
  The amount of “in flight” data allowed for a TCP connection (BDP = bandwidth * round trip time)
  Example: 1Gb/s cross country, ~100ms
    1,000,000,000 b/s * .1 s = 100,000,000 bits
    100,000,000 / 8 = 12,500,000 bytes
    12,500,000 bytes / (1024*1024) ~ 12MB
  Major OSs default to a base of 64k.
    For those playing at home, the maximum throughput with a TCP window of 64 KByte for RTTs:
      10ms = 50Mbps
      50ms = 10Mbps
      100ms = 5Mbps
    Autotuning does help by growing the window when needed. Do make this work properly, the host needs tuning: https://fasterdata.es.net/host-tuning/
Ignore the math aspect, its really just about making sure there is memory to catch packets. As the speed increases, there are more packets. If there is not memory, we drop them, and that makes TCP sad.
  Memory on hosts, and network gear

## Slide 37: What BWCTL Tells Us
Lets start by describing throughput, which is vague.
  Capacity: link speed
    Narrow Link: link with the lowest capacity along a path
    Capacity of the end-to-end path = capacity of the narrow link
  Utilized bandwidth: current traffic load
  Available bandwidth: capacity – utilized bandwidth
    Tight Link: link with the least available bandwidth in a path
  Achievable bandwidth: includes protocol and host issues (e.g. BDP!)
All of this is “memory to memory”, e.g. we are not involving a spinning disk (more later)
45 Mbps
10 Mbps
100 Mbps
45 Mbps
Narrow Link
Tight Link
source
sink
(Shaded portion shows background traffic)

## Slide 38: BWCTL Example (iperf)
[zurawski@wash-pt1 ~]$ bwctl -T iperf -f m -t 10 -i 2 -c sunn-pt1.es.net
bwctl: 83 seconds until test results available
RECEIVER START
bwctl: exec_line: /usr/bin/iperf -B 198.129.254.58 -s -f m -m -p 5136 -t 10 -i 2.000000
bwctl: run_tool: tester: iperf
bwctl: run_tool: receiver: 198.129.254.58
bwctl: run_tool: sender: 198.124.238.34
bwctl: start_tool: 3598657357.738868
------------------------------------------------------------
Server listening on TCP port 5136
Binding to local address 198.129.254.58
TCP window size: 0.08 MByte (default)
------------------------------------------------------------
[ 16] local 198.129.254.58 port 5136 connected with 198.124.238.34 port 5136
[ ID] Interval Transfer Bandwidth
[ 16] 0.0- 2.0 sec 90.4 MBytes 379 Mbits/sec
[ 16] 2.0- 4.0 sec 689 MBytes 2891 Mbits/sec
[ 16] 4.0- 6.0 sec 684 MBytes 2867 Mbits/sec
[ 16] 6.0- 8.0 sec 691 MBytes 2897 Mbits/sec
[ 16] 8.0-10.0 sec 691 MBytes 2898 Mbits/sec
[ 16] 0.0-10.0 sec 2853 MBytes 2386 Mbits/sec
[ 16] MSS size 8948 bytes (MTU 8988 bytes, unknown interface)
bwctl: stop_tool: 3598657390.668028
RECEIVER END
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 39: BWCTL Example (iperf3)
[zurawski@wash-pt1 ~]$ bwctl -T iperf3 -f m -t 10 -i 2 -c sunn-pt1.es.net
bwctl: 55 seconds until test results available
SENDER START
bwctl: run_tool: tester: iperf3
bwctl: run_tool: receiver: 198.129.254.58
bwctl: run_tool: sender: 198.124.238.34
bwctl: start_tool: 3598657653.219168
Test initialized
Running client
Connecting to host 198.129.254.58, port 5001
[ 17] local 198.124.238.34 port 34277 connected to 198.129.254.58 port 5001
[ ID] Interval Transfer Bandwidth Retransmits
[ 17] 0.00-2.00 sec 430 MBytes 1.80 Gbits/sec 2
[ 17] 2.00-4.00 sec 680 MBytes 2.85 Gbits/sec 0
[ 17] 4.00-6.00 sec 669 MBytes 2.80 Gbits/sec 0
[ 17] 6.00-8.00 sec 670 MBytes 2.81 Gbits/sec 0
[ 17] 8.00-10.00 sec 680 MBytes 2.85 Gbits/sec 0
[ ID] Interval Transfer Bandwidth Retransmits
Sent
[ 17] 0.00-10.00 sec 3.06 GBytes 2.62 Gbits/sec 2
Received
[ 17] 0.00-10.00 sec 3.06 GBytes 2.63 Gbits/sec
iperf Done.
bwctl: stop_tool: 3598657664.995604
SENDER END
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 40: BWCTL Example (nuttcp)
[zurawski@wash-pt1 ~]$ bwctl -T nuttcp -f m -t 10 -i 2 -c sunn-pt1.es.net
bwctl: 73 seconds until test results available
SENDER START
bwctl: exec_line: /usr/bin/nuttcp -vv -p 5001 -i 2.000000 -T 10 -t 198.129.254.58
bwctl: run_tool: tester: nuttcp
bwctl: run_tool: receiver: 198.129.254.58
bwctl: run_tool: sender: 198.124.238.34
bwctl: start_tool: 3598657844.605350
nuttcp-t: v7.1.6: socket
nuttcp-t: buflen=65536, nstream=1, port=5001 tcp -> 198.129.254.58
nuttcp-t: time limit = 10.00 seconds
nuttcp-t: connect to 198.129.254.58 with mss=8948, RTT=62.418 ms
nuttcp-t: send window size = 98720, receive window size = 87380
nuttcp-t: available send window = 74040, available receive window = 65535
nuttcp-r: v7.1.6: socket
nuttcp-r: buflen=65536, nstream=1, port=5001 tcp
nuttcp-r: interval reporting every 2.00 seconds
nuttcp-r: accept from 198.124.238.34
nuttcp-r: send window size = 98720, receive window size = 87380
nuttcp-r: available send window = 74040, available receive window = 65535
131.0625 MB / 2.00 sec = 549.7033 Mbps 1 retrans
725.6250 MB / 2.00 sec = 3043.4964 Mbps 0 retrans
715.0000 MB / 2.00 sec = 2998.8284 Mbps 0 retrans
714.3750 MB / 2.00 sec = 2996.4168 Mbps 0 retrans
707.1250 MB / 2.00 sec = 2965.8349 Mbps 0 retrans
nuttcp-t: 2998.1379 MB in 10.00 real seconds = 307005.08 KB/sec = 2514.9856 Mbps
nuttcp-t: 2998.1379 MB in 2.32 CPU seconds = 1325802.48 KB/cpu sec
nuttcp-t: retrans = 1
nuttcp-t: 47971 I/O calls, msec/call = 0.21, calls/sec = 4797.03
nuttcp-t: 0.0user 2.3sys 0:10real 23% 0i+0d 768maxrss 0+2pf 156+28csw
nuttcp-r: 2998.1379 MB in 10.07 real seconds = 304959.96 KB/sec = 2498.2320 Mbps
nuttcp-r: 2998.1379 MB in 2.36 CPU seconds = 1301084.31 KB/cpu sec
nuttcp-r: 57808 I/O calls, msec/call = 0.18, calls/sec = 5742.21
nuttcp-r: 0.0user 2.3sys 0:10real 23% 0i+0d 770maxrss 0+4pf 9146+24csw
bwctl: stop_tool: 3598657866.949026
SENDER END
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 41: BWCTL Example (nuttcp, [1%] loss)
[zurawski@wash-pt1 ~]$ bwctl -T nuttcp -f m -t 10 -i 2 -c sunn-pt1.es.net
bwctl: 41 seconds until test results available
SENDER START
bwctl: exec_line: /usr/bin/nuttcp -vv -p 5004 -i 2.000000 -T 10 -t 198.129.254.58
bwctl: run_tool: tester: nuttcp
bwctl: run_tool: receiver: 198.129.254.58
bwctl: run_tool: sender: 198.124.238.34
bwctl: start_tool: 3598658394.807831
nuttcp-t: v7.1.6: socket
nuttcp-t: buflen=65536, nstream=1, port=5004 tcp -> 198.129.254.58
nuttcp-t: time limit = 10.00 seconds
nuttcp-t: connect to 198.129.254.58 with mss=8948, RTT=62.440 ms
nuttcp-t: send window size = 98720, receive window size = 87380
nuttcp-t: available send window = 74040, available receive window = 65535
nuttcp-r: v7.1.6: socket
nuttcp-r: buflen=65536, nstream=1, port=5004 tcp
nuttcp-r: interval reporting every 2.00 seconds
nuttcp-r: accept from 198.124.238.34
nuttcp-r: send window size = 98720, receive window size = 87380
nuttcp-r: available send window = 74040, available receive window = 65535
6.3125 MB / 2.00 sec = 26.4759 Mbps 27 retrans
3.5625 MB / 2.00 sec = 14.9423 Mbps 4 retrans
3.8125 MB / 2.00 sec = 15.9906 Mbps 7 retrans
4.8125 MB / 2.00 sec = 20.1853 Mbps 13 retrans
6.0000 MB / 2.00 sec = 25.1659 Mbps 7 retrans
nuttcp-t: 25.5066 MB in 10.00 real seconds = 2611.85 KB/sec = 21.3963 Mbps
nuttcp-t: 25.5066 MB in 0.01 CPU seconds = 1741480.37 KB/cpu sec
nuttcp-t: retrans = 58
nuttcp-t: 409 I/O calls, msec/call = 25.04, calls/sec = 40.90
nuttcp-t: 0.0user 0.0sys 0:10real 0% 0i+0d 768maxrss 0+2pf 51+3csw
nuttcp-r: 25.5066 MB in 10.30 real seconds = 2537.03 KB/sec = 20.7833 Mbps
nuttcp-r: 25.5066 MB in 0.02 CPU seconds = 1044874.29 KB/cpu sec
nuttcp-r: 787 I/O calls, msec/call = 13.40, calls/sec = 76.44
nuttcp-r: 0.0user 0.0sys 0:10real 0% 0i+0d 770maxrss 0+4pf 382+0csw
bwctl: stop_tool: 3598658417.214024
SENDER END
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 42: BWCTL Example (nuttcp, re-ordering)
[zurawski@wash-pt1 ~]$ bwctl -T nuttcp -f m -t 10 -i 2 -c sunn-pt1.es.net
bwctl: 45 seconds until test results available
SENDER START
bwctl: exec_line: /usr/bin/nuttcp -vv -p 5007 -i 2.000000 -T 10 -t 198.129.254.58
bwctl: run_tool: tester: nuttcp
bwctl: run_tool: receiver: 198.129.254.58
bwctl: run_tool: sender: 198.124.238.34
bwctl: start_tool: 3598658824.115013
nuttcp-t: v7.1.6: socket
nuttcp-t: buflen=65536, nstream=1, port=5007 tcp -> 198.129.254.58
nuttcp-t: time limit = 10.00 seconds
nuttcp-t: connect to 198.129.254.58 with mss=8948, RTT=62.433 ms
nuttcp-t: send window size = 98720, receive window size = 87380
nuttcp-t: available send window = 74040, available receive window = 65535
nuttcp-r: v7.1.6: socket
nuttcp-r: buflen=65536, nstream=1, port=5007 tcp
nuttcp-r: interval reporting every 2.00 seconds
nuttcp-r: accept from 198.124.238.34
nuttcp-r: send window size = 98720, receive window size = 87380
nuttcp-r: available send window = 74040, available receive window = 65535
3.4375 MB / 2.00 sec = 14.4176 Mbps 3 retrans
39.5625 MB / 2.00 sec = 165.9376 Mbps 472 retrans
45.5625 MB / 2.00 sec = 191.1028 Mbps 912 retrans
55.9375 MB / 2.00 sec = 234.6186 Mbps 1750 retrans
57.7500 MB / 2.00 sec = 242.2218 Mbps 2434 retrans
nuttcp-t: 210.7074 MB in 10.00 real seconds = 21576.30 KB/sec = 176.7531 Mbps
nuttcp-t: 210.7074 MB in 0.13 CPU seconds = 1622544.64 KB/cpu sec
nuttcp-t: retrans = 6059
nuttcp-t: 3372 I/O calls, msec/call = 3.04, calls/sec = 337.20
nuttcp-t: 0.0user 0.1sys 0:10real 1% 0i+0d 768maxrss 0+2pf 72+10csw
nuttcp-r: 210.7074 MB in 11.25 real seconds = 19175.61 KB/sec = 157.0866 Mbps
nuttcp-r: 210.7074 MB in 0.20 CPU seconds = 1073614.78 KB/cpu sec
nuttcp-r: 4692 I/O calls, msec/call = 2.46, calls/sec = 416.99
nuttcp-r: 0.0user 0.1sys 0:11real 1% 0i+0d 770maxrss 0+4pf 1318+12csw
bwctl: stop_tool: 3598658835.981810
SENDER END
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 43: BWCTL Example (nuttcp, duplication)
[zurawski@wash-pt1 ~]$ bwctl -T nuttcp -f m -t 10 -i 2 -c sunn-pt1.es.net
bwctl: 70 seconds until test results available
SENDER START
bwctl: exec_line: /usr/bin/nuttcp -vv -p 5008 -i 2.000000 -T 10 -t 198.129.254.58
bwctl: run_tool: tester: nuttcp
bwctl: run_tool: receiver: 198.129.254.58
bwctl: run_tool: sender: 198.124.238.34
bwctl: start_tool: 3598659020.747514
nuttcp-t: v7.1.6: socket
nuttcp-t: buflen=65536, nstream=1, port=5008 tcp -> 198.129.254.58
nuttcp-t: time limit = 10.00 seconds
nuttcp-t: connect to 198.129.254.58 with mss=8948, RTT=62.425 ms
nuttcp-t: send window size = 98720, receive window size = 87380
nuttcp-t: available send window = 74040, available receive window = 65535
nuttcp-r: v7.1.6: socket
nuttcp-r: buflen=65536, nstream=1, port=5008 tcp
nuttcp-r: interval reporting every 2.00 seconds
nuttcp-r: accept from 198.124.238.34
nuttcp-r: send window size = 98720, receive window size = 87380
nuttcp-r: available send window = 74040, available receive window = 65535
114.8125 MB / 2.00 sec = 481.5470 Mbps 22 retrans
726.5625 MB / 2.00 sec = 3047.4347 Mbps 0 retrans
711.5625 MB / 2.00 sec = 2984.4841 Mbps 0 retrans
716.3750 MB / 2.00 sec = 3004.7216 Mbps 0 retrans
713.5000 MB / 2.00 sec = 2992.6404 Mbps 0 retrans
nuttcp-t: 2991.1407 MB in 10.00 real seconds = 306290.41 KB/sec = 2509.1311 Mbps
nuttcp-t: 2991.1407 MB in 2.45 CPU seconds = 1250875.20 KB/cpu sec
nuttcp-t: retrans = 22
nuttcp-t: 47859 I/O calls, msec/call = 0.21, calls/sec = 4785.86
nuttcp-t: 0.0user 2.4sys 0:10real 24% 0i+0d 768maxrss 0+2pf 155+30csw
nuttcp-r: 2991.1407 MB in 10.08 real seconds = 303823.24 KB/sec = 2488.9200 Mbps
nuttcp-r: 2991.1407 MB in 2.49 CPU seconds = 1231762.62 KB/cpu sec
nuttcp-r: 58710 I/O calls, msec/call = 0.18, calls/sec = 5823.66
nuttcp-r: 0.0user 2.4sys 0:10real 24% 0i+0d 770maxrss 0+4pf 10146+24csw
bwctl: stop_tool: 3598659043.778699
SENDER END
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 44: What BWCTL May Not be Telling Us
Fasterdata Tunings
  Fasterdata recommends a set of tunings (https://fasterdata.es.net/host-tuning/) that are designed to increase the performance of a single COTS host, on a shared network infrastructure
    What this means is that we don’t recommend ‘maximum’ tuning
  We are assuming (expecting? hoping?) the host can do parallel TCP streams via the data transfer application (e.g. Globus)
  Because of that you don’t want to assign upwards of 256M of kernel memory to a single TCP socket – a sensible amount is 32M/64M, and if you have 4 streams you are getting the benefits of 128M/256M (enough for a 10G cross country flow)
  We also strive for good citizenship – its very possible for a single 10G machine to get 9.9Gbps TCP, we see this often. If its on a shared infrastructure, there is benefit to downtuning buffers.
Can you ignore the above? Sure – overtune as you see fit, KNOW YOUR NETWORK, USERS, AND USE CASES

## Slide 45: What BWCTL May Not be Telling Us
Regular Testing Setup
  If we don’t ‘max tune’, and run a 20/30 second single streamed TCP test (defaults for the toolkit) we are not going to see 9.9Gbps.
  Think critically: TCP ramp up takes 1-5 seconds (depending on latency), and any tiny blip of congestion will cut TCP performance in half.
  It is common (and in my mind - expected) to see regular testing values on clean networks range between 1Gbps and 5Gbps, latency dependent
  Performance has two ranges – really crappy, and expected (where expected has a lot of headroom). You will know when its really crappy (trust me).
Diagnostic Suggestions
  You can max out BWCTL in this capacity
  Run long tests (-T 60), with multiple streams (-P 4), and large windows (-W 128M); go crazy
  It is also VERY COMMON that doing so will produce different results than your regular testing. It’s a different set of test parameters, its not that the tools are deliberately lying.

## Slide 46: What OWAMP Tells Us
OWAMP is a necessity in regular testing – if you aren’t using this you need to be
  Queuing often occurs in a single direction (think what everyone is doing at noon on a college campus)
  Packet loss (and how often/how much occurs over time) is more valuable than throughput
    This gives you a ‘why’ to go with an observation.
  If your router is going to drop a 50B UDP packet, it is most certainly going to drop a 15000B/9000B TCP packet
Overlaying data
  Compare your throughput results against your OWAMP – do you see patterns?
  Alarm on each, if you are alarming (and we hope you are alarming …)

## Slide 47: OWAMP (initial)
[zurawski@wash-owamp ~]$ owping sunn-owamp.es.net
Approximately 12.6 seconds until results available
--- owping statistics from [wash-owamp.es.net]:8885 to [sunn-owamp.es.net]:8827 ---
SID: c681fe4ed67f1b3e5faeb249f078ec8a
first: 2014-01-13T18:11:11.420
last: 2014-01-13T18:11:20.587
100 sent, 0 lost (0.000%), 0 duplicates
one-way delay min/median/max = 31/31.1/31.7 ms, (err=0.00201 ms)
one-way jitter = 0 ms (P95-P50)
Hops = 7 (consistently)
no reordering
--- owping statistics from [sunn-owamp.es.net]:9027 to [wash-owamp.es.net]:8888 ---
SID: c67cfc7ed67f1b3eaab69b94f393bc46
first: 2014-01-13T18:11:11.321
last: 2014-01-13T18:11:22.672
100 sent, 0 lost (0.000%), 0 duplicates
one-way delay min/median/max = 31.4/31.5/32.6 ms, (err=0.00201 ms)
one-way jitter = 0 ms (P95-P50)
Hops = 7 (consistently)
no reordering
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 48: OWAMP (w/ loss)
[zurawski@wash-owamp ~]$ owping sunn-owamp.es.net
Approximately 12.6 seconds until results available
--- owping statistics from [wash-owamp.es.net]:8852 to [sunn-owamp.es.net]:8837 ---
SID: c681fe4ed67f1f0908224c341a2b83f3
first: 2014-01-13T18:27:22.032
last: 2014-01-13T18:27:32.904
100 sent, 12 lost (12.000%), 0 duplicates
one-way delay min/median/max = 31.1/31.1/31.3 ms, (err=0.00502 ms)
one-way jitter = nan ms (P95-P50)
Hops = 7 (consistently)
no reordering
--- owping statistics from [sunn-owamp.es.net]:9182 to [wash-owamp.es.net]:8893 ---
SID: c67cfc7ed67f1f09531c87cf38381bb6
first: 2014-01-13T18:27:21.993
last: 2014-01-13T18:27:33.785
100 sent, 0 lost (0.000%), 0 duplicates
one-way delay min/median/max = 31.4/31.5/31.5 ms, (err=0.00502 ms)
one-way jitter = 0 ms (P95-P50)
Hops = 7 (consistently)
no reordering
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 49: OWAMP (w/ re-ordering)
[zurawski@wash-owamp ~]$ owping sunn-owamp.es.net
Approximately 12.9 seconds until results available
--- owping statistics from [wash-owamp.es.net]:8814 to [sunn-owamp.es.net]:9062 ---
SID: c681fe4ed67f21d94991ea335b7a1830
first: 2014-01-13T18:39:22.543
last: 2014-01-13T18:39:31.503
100 sent, 0 lost (0.000%), 0 duplicates
one-way delay min/median/max = 31.1/106/106 ms, (err=0.00201 ms)
one-way jitter = 0.1 ms (P95-P50)
Hops = 7 (consistently)
1-reordering = 19.000000%
2-reordering = 1.000000%
no 3-reordering
--- owping statistics from [sunn-owamp.es.net]:8770 to [wash-owamp.es.net]:8939 ---
SID: c67cfc7ed67f21d994c1302dff644543
first: 2014-01-13T18:39:22.602
last: 2014-01-13T18:39:31.279
100 sent, 0 lost (0.000%), 0 duplicates
one-way delay min/median/max = 31.4/31.5/32 ms, (err=0.00201 ms)
one-way jitter = 0 ms (P95-P50)
Hops = 7 (consistently)
no reordering
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 50: OWAMP (w/ duplication)
[zurawski@wash-owamp ~]$ owping sunn-owamp.es.net
Approximately 12.6 seconds until results available
--- owping statistics from [wash-owamp.es.net]:8905 to [sunn-owamp.es.net]:8933 ---
SID: c681fe4ed67f228b6b36524c3d3531da
first: 2014-01-13T18:42:20.443
last: 2014-01-13T18:42:30.223
100 sent, 0 lost (0.000%), 11 duplicates
one-way delay min/median/max = 31.1/31.1/33 ms, (err=0.00201 ms)
one-way jitter = 0.1 ms (P95-P50)
Hops = 7 (consistently)
no reordering
--- owping statistics from [sunn-owamp.es.net]:9057 to [wash-owamp.es.net]:8838 ---
SID: c67cfc7ed67f228bb9a5a9b27f4b2d47
first: 2014-01-13T18:42:20.716
last: 2014-01-13T18:42:29.822
100 sent, 0 lost (0.000%), 0 duplicates
one-way delay min/median/max = 31.4/31.5/31.9 ms, (err=0.00201 ms)
one-way jitter = 0 ms (P95-P50)
Hops = 7 (consistently)
no reordering
N.B. This is what perfSONAR Graphs – the average of the complete test

## Slide 51: What OWAMP Tells Us

## Slide 52: perfSONAR Outline
Performance Introduction & Motivation
perfSONAR Preliminaries
Deployment & Regular Testing
Maddash Installation & Use
Tool Use
Common Pitfalls
Debugging Strategies
Use Cases & Success Stories

## Slide 53: Expectation Management
Installing perfSONAR, even on a completely clean network, will not yet you instant line rate results.
  Machine architecture, as well as OS tuning plays a huge role in the equation
  perfSONAR is a stable set of software choices that ride of COTS hardware – some hardware works better than others
  Equally, perfSONAR (and fasterdata.es.net) recommend ‘friendly’ tunings that will not blow the barn doors off of the rest of the network
The following will introduce some expectation management tips.

## Slide 54: Common Pitfalls – “it should be higher!”
There have been some expectation management problems with the tools that we have seen
  Some feel that if they have 10G, they will get all of it
  Some may not understand the makeup of the test
  Some may not know what they should be getting
Lets start with an ESnet to ESnet test, between very well tuned and recent pieces of hardware
5Gbps is “awesome” for:
  A 20 second test
  60ms Latency
  Homogenous servers
  Using fasterdata tunings
  On a shared infrastructure

## Slide 55: Common Pitfalls – “it should be higher!”
Another example, ESnet (Sacremento CA) to Utah, ~20ms of latency
Is it 5Gbps? No, but still outstanding given the environment:
  20 second test
  Heterogeneous hosts
  Possibly different configurations (e.g. similar tunings of the OS, but not exact in terms of things like BIOS, NIC, etc.)
  Different congestion levels on the ends

## Slide 56: Common Pitfalls – “it should be higher!”
Similar example, ESnet (Washington DC) to Utah, ~50ms of latency
Is it 5Gbps? No. Should it be? No! Could it be higher? Sure, run a different diagnostic test.
  Longer latency – still same length of test (20 sec)
  Heterogeneous hosts
  Possibly different configurations (e.g. similar tunings of the OS, but not exact in terms of things like BIOS, NIC, etc.)
  Different congestion levels on the ends
Takeaway – you will know bad performance when you see it. This is consistent and jives with the environment.

## Slide 57: Common Pitfalls – “it should be higher!”
Another Example – the 1st half of the graph is perfectly normal
  Latency of 10-20ms (TCP needs time to ramp up)
  Machine placed in network core of one of the networks – congestion is a fact of life
  Single stream TCP for 20 seconds
The 2nd half is not (e.g. packet loss caused a precipitous drop)
You will know it, when you see it.

## Slide 58: Common Pitfalls – “the tool is unpredictable”
Sometimes this happens:
Is it a “problem”? Yes and no.
Cause: this is called “overdriving” and is common. A 10G host and a 1G host are testing to each other
  1G to 10G is smooth and expected (~900Mbps, Blue)
  10G to 1G is choppy (variable between 900Mbps and 700Mbps, Green)

## Slide 59: Common Pitfalls – “the tool is unpredictable”
A NIC doesn’t stream packets out at some average rate - it’s a binary operation:
  Send (e.g. @ max rate) vs. not send (e.g. nothing)
10G of traffic needs buffering to support it along the path. A 10G switch/router can handle it. So could another 10G host (if both are tuned of course)
A 1G NIC is designed to hold bursts of 1G. Sure, they can be tuned to expect more, but may not have enough physical memory
  Ditto for switches in the path
At some point things ‘downstep’ to a slower speed, that drops packets on the ground, and TCP reacts like it were any other loss event.

## Slide 60: Common Pitfalls – Summary
When in doubt – test again!
  Diagnostic tests are informative – and they should provide more insight into the regular stuff (still do regular testing, of course)
  Be prepared to divide up a path as need be
A poor carpenter blames his tools
  The tools are only as good as the people using them, do it methodically
  Trust the results – remember that they are giving you a number based on the entire environment
If the site isn’t using perfSONAR – step 1 is to get them to do so
  http://www.perfsonar.net
Get some help
  engage@es.net

## Slide 61: perfSONAR Outline
Performance Introduction & Motivation
perfSONAR Preliminaries
Deployment & Regular Testing
Maddash Installation & Use
Tool Use
Common Pitfalls
Debugging Strategies
Use Cases & Success Stories

## Slide 62: WAN Test Methodology – Problem Isolation
Segment-to-segment testing is unlikely to be helpful
  TCP dynamics will be different, and in this case all the pieces do not equal the whole
    E.g. high throughput on a 1ms path with high packet loss vs. the same segment in a longer 20ms path
  Problem links can test clean over short distances
  An exception to this is hops that go thru a firewall
Run long-distance tests
  Run the longest clean test you can, then look for the shortest dirty test that includes the path of the clean test
In order for this to work, the testers need to be already deployed when you start troubleshooting
  ESnet has at least one perfSONAR host at each hub location.
    Many (most?) R&E providers in the world have deployed at least 1
  If your provider does not have perfSONAR deployed ask them why, and then ask when they will have it done
Notes: See map on next slide

## Slide 63: Network Performance Troubleshooting Example
Notes: This is the user perspective

## Slide 64: Wide Area Testing – Full Context
Notes: This is the user perspective with full routed network context (optical transport omitted)

## Slide 65: Wide Area Testing – Long Clean Test
Notes: The long clean test identifies a portion of the infrastructure that is likely not the problem
Note that short-distance tests do not identify clean components!!!

## Slide 66: BWCTL 3rd Party
bwctl –f m –t 10 –i 1 –c 172.31.5.21 –s 172.31.15.21
From a host that has a BWCTL client, I can launch a test to two “other” hosts.
Negotiation on timeslots and test parameters occurs beween the 3 parties
Results are returned to the host that initiated the test
Why do we need this?
  Helps to debug our problem space. I can sit on an ESnet host and launch a test from any of the above
Notes: See map on next slide

## Slide 67: Wide Area Testing – Poorly Performing Tests Illustrate Likely Problem Areas
Notes: Test as much of the wide area path as you can – this gives the test similar TCP dynamics to the real traffic
From a single remote test host, using as much of the path as possible, run the longest clean test you can and the shortest dirty test you can that includes the path of the long clean test.

## Slide 68: Likely Problem Area
Notes: Test as much of the wide area path as you can – this gives the test similar TCP dynamics to the real traffic
From a single remote test host, using as much of the path as possible, run the longest clean test you can and the shortest dirty test you can that includes the path of the long clean test.

## Slide 69: Lessons From This Example
This testing can be done quickly if perfSONAR is already deployed
Huge productivity
  Reasonable hypothesis developed quickly
  Probable administrative domain identified
  Testing time can be short – an hour or so at most
Without perfSONAR cases like this are very challenging
Time to resolution measured in months
In order to be useful for data-intensive science, the network must be fixable quickly, because it will break
The Science DMZ model allows high-performance use of the network, but perfSONAR is necessary to ensure the whole kit functions well
Notes: See map on next slide

## Slide 70: perfSONAR Outline
Performance Introduction & Motivation
perfSONAR Preliminaries
Deployment & Regular Testing
Maddash Installation & Use
Tool Use
Common Pitfalls
Debugging Strategies
Use Cases & Success Stories

## Slide 71: Success Stories
#1 Failing Optic(s)
#2 Penn State University Firewall
#3 University of Colorado Network Design
#4 Host Tuning
#5 Bottleneck Link
#6 R&E vs. Commodity Routing
#7 Extreme Upstream Packet loss
#8 Fiber Cut
#9 Buffer Tuning

## Slide 72: Success Stories - #1 Failing Optic(s)
Second example – another one featuring a backbone
    Similar to frog boiling, hard alarms don’t notice gradual failure
Gb/s
normal performance
degrading performance
repair
one month

## Slide 73: Success Stories - #1 Failing Optic(s)
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Throughput vs. increasing latency on a 10Gb/s link with 0.0046% packet loss
73 – ESnet Science Engagement (engage@es.net) - 9/19/14

## Slide 74: Success Stories - #1 Failing Optic(s) ex 2
Adding an Attenuator to a Noisy (discovered via OWAMP) Link

## Slide 75: Success Stories - #2 PSU
PSU = Firewalls for some. The college of engineering has one, central IT does not

## Slide 76: Success Stories - #2 PSU
Initial Report from network users: performance poor both directions
    Outbound and inbound (normal issue is inbound through protection mechanisms)
From previous diagram – CoE firewalll was tested
    Machine outside/inside of firewall. Test to point 10ms away (Internet2 Washington)
Low, but no retransmissions?
jzurawski@ssstatecollege:~> nuttcp -T 30 -i 1 -p 5679 -P 5678 64.57.16.22
5.8125 MB / 1.00 sec = 48.7565 Mbps 0 retrans
6.1875 MB / 1.00 sec = 51.8886 Mbps 0 retrans
…
6.1250 MB / 1.00 sec = 51.3957 Mbps 0 retrans
6.1250 MB / 1.00 sec = 51.3927 Mbps 0 retrans
184.3515 MB / 30.17 sec = 51.2573 Mbps 0 %TX 1 %RX 0 retrans 9.85 msRTT

## Slide 77: Success Stories – Remember the Brown Firewall?
Note the retransmissions in the Brown case (e.g. a lack of buffering and/or TCP timeouts) … and the lack of them for Penn State
  nuttcp -r -T 10 -i 1 -p 10200 bwctl.newy.net.internet2.edu
  4.5625 MB / 1.00 sec = 38.1995 Mbps 13 retrans
  4.8750 MB / 1.00 sec = 40.8956 Mbps 4 retrans
  4.8750 MB / 1.00 sec = 40.8954 Mbps 6 retrans
  6.4375 MB / 1.00 sec = 54.0024 Mbps 9 retrans
  5.7500 MB / 1.00 sec = 48.2310 Mbps 8 retrans
  5.8750 MB / 1.00 sec = 49.2880 Mbps 5 retrans
  6.3125 MB / 1.00 sec = 52.9006 Mbps 3 retrans
  5.3125 MB / 1.00 sec = 44.5653 Mbps 7 retrans
  4.3125 MB / 1.00 sec = 36.2108 Mbps 7 retrans
  5.1875 MB / 1.00 sec = 43.5186 Mbps 8 retrans
  53.7519 MB / 10.07 sec = 44.7577 Mbps 0 %TX 1 %RX 70 retrans 8.29 msRTT

## Slide 78: Success Stories - #2 PSU
Observation: net.ipv4.tcp_window_scaling did not seem to be working
    64K of buffer is default. Over a 10ms path, this means we can hope to see only 50Mbps of throughput:
    BDP (50 Mbit/sec, 10.0 ms) = 0.06 Mbyte
Implication: something in the path was not respecting the specification in RFC 1323, and was not allowing TCP window to grow
    TCP window of 64 KByte and RTT of 1.0 ms <= 500.00 Mbit/sec.
    TCP window of 64 KByte and RTT of 5.0 ms <= 100.00 Mbit/sec.
    TCP window of 64 KByte and RTT of 10.0 ms <= 50.00 Mbit/sec.
    TCP window of 64 KByte and RTT of 50.0 ms <= 10.00 Mbit/sec.
Reading documentation for firewall:
    TCP flow sequence checking was enabled
    What would happen if this was turn off (both directions?

## Slide 79: Success Stories - #2 PSU
jzurawski@ssstatecollege:~> nuttcp -T 30 -i 1 -p 5679 -P 5678 64.57.16.22
55.6875 MB / 1.00 sec = 467.0481 Mbps 0 retrans
74.3750 MB / 1.00 sec = 623.5704 Mbps 0 retrans
87.4375 MB / 1.00 sec = 733.4004 Mbps 0 retrans
…
91.7500 MB / 1.00 sec = 770.0544 Mbps 0 retrans
88.6875 MB / 1.00 sec = 743.5676 Mbps 28 retrans
69.0625 MB / 1.00 sec = 578.9509 Mbps 0 retrans
2300.8495 MB / 30.17 sec = 639.7338 Mbps 4 %TX 17 %RX 730 retrans 9.88 msRTT

## Slide 80: Success Stories - #2 PSU
Was this impacting people? Oh yes it was:

## Slide 81: Success Stories - #3 CU
Something limiting utilization
Recent upgrades to network left many perplexed.
In addition, the Physics department just purchased 40 new machines, and stacks of switches to support them (1G connected)

## Slide 82: Success Stories - #3 CU – the network

## Slide 83: Success Stories - #3 CU
Fibers were cleaned, no change.
Optics were swapped, no change also.
Dell 6248 Switch was bypassed
  Removed the device dropping packets from the path, but we still see low throughput.
Switch Replacement
  6248 seemed to be dropping because of a lack of internal memory
  Lots of Fan In … too many flows to handle at once
  More capable device: Arista 7000 Series

## Slide 84: Success Stories - #3 CU (network again)

## Slide 85: Success Stories - #3 CU
But … still loss was being seen, Why?
  Something corrupting packets in the path?
  Damaged fiber in the infrastructure (walls)?
Next Steps
  Hardware based evaluation of the infrastructure to check light levels/loss – nothing
  Called Arista:
    … the reason for the drops may be the switching mode being used in a “fan-out situation” (10Gbe > multiple 1Gbe). Instead of operating in the default “cut-through” mode, the switch is forced to drop down into a “store-n-forward” mode where it is limited by buffers.

## Slide 86: Success Stories - #4 Host Tuning
Simple example – play with the settings in /etc/sysctl.conf when running some BWCTL tests.
See if you can pick out when we raised the memory for the TCP window (ignore the blue – this is a known firewall)

## Slide 87: Success Stories - #4 Host Tuning
Another example – long path (~70ms), single stream TCP, 10G cards, tuned hosts
Why the nearly 2x uptick? Adjusted net.ipv4.tcp_rmem/wmem maximums (used in auto tuning) to 64M instead of 16M.
As the path length/throughput expectation increases, this is a good idea. There are limits (e.g. beware of buffer bloat on short RTTs)

## Slide 88: Success Stories - #4 Host Tuning
A more complete view – showing the role of MTUs and host tuning (e.g. ‘its all related’):

## Slide 89: Success Stories - #5 Bottleneck Link
OWAMP used in a campus with too many users and not enough network (ignore the latency lines – NTP was hurting too)

## Slide 90: Success Stories - #6 R&E vs. Commodity Routing
Some campuses don’t need to be told that the R&E path is ‘better’, others need to figure it out on their own.
BWCTL results between PSU and Vanderbilt (science driver was genomics)
    Normally low results over the course of the day. ‘spikes’ at night.
    Traceoutes:
      PSU -> Cogent -> Century Link -> Vanderbilt
      Vanderbilt -> SOX -> NLR (dated) -> 3ROX -> PSU
    Asymmetry is not bad by itself, unless …

## Slide 91: Success Stories - #6 R&E vs. Commodity Routing
  Letting BGP ‘figure it out’ can sometimes lead to issues.
    Yes, shortest path is a good metric in the commercial world.
    R&E should always be preferred to commodity when available
  Managing local prefs can be a ‘pain’ for those that are not used to it. The end result is hard to argue with
  The ‘blue’ line? Over NLR in the dying days – and the Cisco 650x in that region was known to have a bad card/optic that was never replaced (e.g. packet loss all over the place)

## Slide 92: Success Stories - #6 R&E vs. other R&E
  Sometimes things break on R&E too, here is UNL to DESY (Germany), first over Internet2 then over ‘LHCONE’
      Takeaway – there was something wrong with LHCONE …

## Slide 93: Success Stories - #6 R&E vs. other R&E
  Same situation, different location (this time Vanderbilt). This is a PhEDEx (e.g. data movement) graph that shows the transfer rate with LHCONE, and then when Vanderbilt went back to regular Internet2:

## Slide 94: Success Stories - #7 Upstream Packet Loss
  Sometimes its not your fault – this is why monitoring your provider is a good idea:
  Drastic drop in BWCTL normally has a reason …

## Slide 95: Success Stories - #7 Upstream Packet Loss
  Spikes of packet loss, almost always during business hours
  Function of the load on the line/time of day
  This was traced to regional network

## Slide 96: Success Stories - #8 Fiber Cut
  Not that perfSONAR could help fix this (that’s up to your local DOT and provider …), but it does have an interesting signature in terms of loss and latency:

## Slide 97: #9 Buffer Tuning Experiment
2Gbps UDP background data
TCP Test flows, 50ms path
Modify this egress buffer size
Buffer Size | Packets Dropped | TCP Throughput
120 MB | 0 | 8Gbps
60 MB | 0 | 8Gbps
36 MB | 200 | 2Gbps
24 MB | 205 | 2Gbps
12 MB | 204 | 2Gbps
6 MB | 207 | 2Gbps
30 Second test, 2 TCP streams
97 – ESnet Science Engagement (engage@es.net) - 9/19/14

## Slide 98: Success Stories
Key Message(s):
The monitoring infrastructure is sensitive for a reason – so that it finds the problems in all layers of the OSI stack.
End-to-end Video transmission (or just about any other use case) suffers because of a problems that may be unseen or not understood.
Understanding comes from learning to use the tools, learning to trust them, and having universal availability.
Comprehensive solutions will save time in the end – and perfSONAR is that solution

## Slide 99: Network Performance Monitoring with perfSONAR
Jason Zurawski - zurawski@es.net
Mary Hester – mchester@es.net
ESnet Science Engagement – engage@es.net
http://www.perfsonar.net

## Slide 100: Extra Slides – Maddash Installation

## Slide 101: Maddash & The Mesh Config
Measurement results are more useful when they can be “seen”, because this implies they will be acted on.
Maddash is a software package that can be used to visualize the results of many perfSONAR tests
The Mesh Config is a way to manage multiple nodes, by giving them a uniform testing schedule
  E.g. this is in contrast to the other method of configuration we d-did – manually entering our tests.
  Changes node from ‘testing as an island’ to being a part of a larger testing strategy

## Slide 102: Performance Island

## Slide 103: Performance Coordination

## Slide 104: Maddash For OIN
Will go over a couple of things, more/better information available here: http://software.es.net/maddash/
Things I will go over:
  The basics of what the mesh configuration looks like, and the tools used to create it
  Installing maddash server components
  Installing an ‘agent’ on a node, so that it can participate in testing
Things that I won’t go over – but would encourage you to do at home:
  Customizing a configuration file

## Slide 105: Mesh Configuration
Two main types of Meshes you can aim to configure:
  Disjoint: one host (or a set of hosts) testing against other nodes that are ‘beacons’ (e.g. they are not consuming the same specification. Perfect for loose coordination activities
  Full: each host consumes the same measurement specification and you can get a full n:n set of tests. Requires strong coordination efforts.
Lets look at a disjoint specification first. Download this for viewing on your own:
  http://stats.es.net/OIN/disjoint.conf

## Slide 106: Disjoint Mesh Configuration
File has 5 main stanzas:
  Administrative Info (name, who is the admin)
  Node definitions (who is being tested against, or who is making tests)
  Test specifications (type of test to run + parameters)
  Group definitions (tdefining which hosts are involved in a test set)
  Test definition – this is the glue between a specific test and a specific group
Will go over the last 4 (the first is self explanatory)

## Slide 107: Host Definition
<organization>
description OIN Workshop
<site>
description OIN Pod #1
<host>
# BWCTL & OWAMP tester
description 172.31.1.21
address 172.31.1.21
# no_agent 1
<measurement_archive>
type perfsonarbuoy/bwctl
read_url http://172.31.1.21:8085/perfSONAR_PS/services/pSB
write_url 172.31.1.21:8570
</measurement_archive>
<measurement_archive>
type perfsonarbuoy/owamp
read_url http://172.31.1.21:8085/perfSONAR_PS/services/pSB
write_url 172.31.1.21:8569
</measurement_archive>
</host>
</site>
</organization>

## Slide 108: Host Definition
Organization:
  Reserved for broad category (e.g. ESnet is an org that has multiple sites, and multiple hosts per site)
Site:
  Slightly more focused (e.g. ‘Denver’ may have 4 hosts)
Host:
  Specific host running a measurement tool (or more than 1)
“no_agent”:
  If the host has a copy of the configuration for testing, comment this out. If the host is just a beacon, set this to ‘1’

## Slide 109: Test Specification
<test_spec bwctl_halfhour_tcp_test>
# Define a test spec for testing once every half hour
type perfsonarbuoy/bwctl # Perform a bwctl test
tool bwctl/iperf # Use 'iperf' to do the bandwidh test
protocol tcp # Run a TCP bandwidth test
interval 1800 # Run the test every half hour
duration 20 # Perform a 20 second duration test
force_bidirectional 1 # do bidirectional test
random_start_percentage 25 # randomize start time
</test_spec>

## Slide 110: Test Specification
BWCTL/OWAMP/Traceroute specification
Tells how often, how long, any other special parameters
Its common to have many of these – allows you to run more specific tests for different groups of hosts

## Slide 111: Group Definition
<group oin_bwctl_disjoint>
type disjoint
b_member 172.31.1.21
a_member 172.31.2.21
a_member 172.31.3.21
…
a_member 172.31.40.21
</group>

## Slide 112: Group Definition
Groups a set of hosts into a logical unit.
Does not tie them to a test set (yet)
In the disjoint mesh, you have a_members (hosts that are not running the mesh – e.g. beacons) and b_members (hosts that are running the mesh configuration)
Common to have many groups for different purposes.

## Slide 113: Test Definition
<test>
description OIN Disjoint Packet Loss Testing
group oin_owamp_disjoint
test_spec owamp_test
</test>
<test>
description OIN Disjoint Throughput Testing
group oin_bwctl_disjoint
test_spec bwctl_halfhour_tcp_test
</test>

## Slide 114: Full Mesh Configuration
Example to examine:
  http://stats.es.net/OIN/oin-full-mesh_1-20.conf
Same basic layout
Things the same:
  Hosts (except all will have the ‘no_agent’ item commented, since they all need to run an agent against the mesh config)
  Test specifications are the same
  Test definitions are the same

## Slide 115: Full Mesh Configuration
Things different:
  Groups (different type, different member defn):
<group oin_bwctl_disjoint>
type mesh
member 172.31.1.21
member 172.31.2.21
member 172.31.3.21
…
member 172.31.40.21
</group>

## Slide 116: Configuration Conversion
The formats we have seen before are more for humans to better enter in info
The software uses a different format (JSON) to either make the tests, or to display info in the server UI.
Next couple of slides detail how we can convert to JSON, and then publish the files

## Slide 117: Configuration Conversion
Install the JSON builder software:
  sudo yum install perl-perfSONAR_PS-MeshConfig-JSONBuilder
We get a piece of software to make the conversion, we just need to point it to the conf file:
  /opt/perfsonar_ps/mesh_config/bin/build_json oin-full-mesh_1-20.conf > oin-full-mesh_1-20.json
  There may be errors, if so correct them in the conf file
Once we have the JSON file, post it in a public place so others could use it
Version for testing against URLs:
  /opt/perfsonar_ps/mesh_config/bin/validate_json --config_url=XXX

## Slide 118: Maddash Server Installation
Start with installing the software (this command will pull down about 20 packages):
  sudo yum install maddash perl-perfSONAR_PS-MeshConfig-GUIAgent
After install, make a backup of this file: /etc/maddash/maddash-server/maddash.yaml. After that, replace the content with this:
##
# Set the directory where the database will be stored
database: /var/lib/maddash/
##
# Set the host where the REST server listens
serverHost: "localhost"
##
# Activate http and set the port where it listens
http:
port: 8881

## Slide 119: Maddash Server Installation
We need to tell the maddash instance about the JSON file we created, edit this file: /opt/perfsonar_ps/mesh_config/etc/gui_agent_configuration.conf
Add the following (if you are 1-20, if you are 21-40 make the adjustment):
<mesh>
  configuration_url XXX
</mesh>

## Slide 120: Maddash Server Installation
Run the following script:
/opt/perfsonar_ps/mesh_config/bin/generate_gui_configuration
Also use the cron entry (/opt/perfsonar_ps/mesh_config/scripts/cron-mesh_config_gui_agent) in /etc/cron.d
And restart the server:
sudo /etc/init.d/maddash-server restart

## Slide 121: Maddash Server Installation

## Slide 122: Configuring Measurement Agents
The final step is getting the agents running, that should be running an agent with the mesh config
Install the following package:
  sudo yum install perl-perfSONAR_PS-MeshConfig-Agent
Make an edit to this file:
  /opt/perfsonar_ps/mesh_config/etc/agent_configuration.conf

## Slide 123: Configuring Measurement Agents
Add this to the end (if you are 1-20, if you are 21-40 make the adjustment):
<mesh>
  configuration_url xxx
validate_certificate 0
</mesh>
A reboot is normally recommended to get things running
Also use the cron entry (/opt/perfsonar_ps/mesh_config/scripts/cron-mesh_config_agent) in /etc/cron.d

## Slide 124: The Final Result
If you set up at home:
  Organize who will be in it, and decide if you want to do mainly disjoint or mesh testing
  Get the dashboard up first, along with the full config
  Get the remote sites to configure the mesh, and start to review the colors of the dashboard
    Could take weeks to get ‘right’
Example:
  http://ps-dashboard.es.net