## Slide 1: The Science DMZ: A Network Design Pattern for Data-Intensive Science
Jason Zurawski – zurawski@es.net
Science Engagement Engineer, ESnet
Lawrence Berkeley National Laboratory
New Mexico Technology in Education (NMTIE)
November 19th, 2014

## Slide 2: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 3: ESnet at a Glance
High-speed national network, optimized for DOE science missions:
  connecting 40 labs, plants and facilities with >100 networks
  $32.6M in FY14, 42FTE
  older than commercial Internet, growing twice as fast
$62M ARRA grant for 100G upgrade:
  transition to new era of optical networking
  world’s first 100G network at continental scale
Culture of urgency:
  4 awards in past 3 years
  R&D100 Award in FY13
  “5 out of 5” for customer satisfaction in last review
  Dedicated staff to support the mission of science

## Slide 4
Notes: Left hand side is about changing the world. This is important because 80% of ESnet traffic leaves the DOE complex.
Right hand side is about innovation and discovery.
Research challenges:
Challenges of Predictability
Challenges of Flexibility
Challenges of Scale
Challenges of Complexity

## Slide 5: Network as Infrastructure Instrument
    Vision: Scientific progress will be completely unconstrained by the physical location of instruments, people, computational resources, or data.
Notes: Summing up ESnet’s vision in one slide, one phrase…
Physical location of instruments, people, computational resources, data. It just should not matter.
[KSTAR, SNS, ATLAS, EMSL, CRT/NERSC, STAR Detector at RHIC [BNL, NP-funded]]

## Slide 6: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 7: Motivation
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors
  Data movement and data analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult
© 2014, Energy Sciences Network
Notes: Human factors – attention span, ability to manage complexity – these are constant
There is a huge amount of promise in data-intensive science. Effective use of networks can help realize those benefits.
The Science DMZ model helps address the difficulties scientists often experience with using networks.

## Slide 8: Traditional “Big Science”

## Slide 9: Big Science Now Comes in Small Packages
Notes:     Beamline 8.3.2 at the Advanced Light Source is a Synchrotron-based Hard X-ray Micro-Tomography instrument. It allows non-destructive 3-Dimensional imaging of solid objects at a resolution of approximately 1 micron.
    106 increase in data output compared to previous generation
    8 Gbps flows to supercomputer for real-time analysis

## Slide 10: Understanding Data Trends
Notes: Requirements workshops for all six program offices within the DOE office of Science

## Slide 11: Data Mobility in a Given Time Interval
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/
© 2014, Energy Sciences Network
Notes: This succinctly describes what the end to end data path must achieve – network, hosts, storage, application
Green: <= 100Mbps Throughput (almost all domestic locations can do this) – less than Fast Ethernet!
Black: 100Mbps to 10Gbps Throughput (most major research institutions can do this, if its running clean)
Blue 10Gbps to 100Gbps Throughput (emerging at major locations)
Orange > 100Gbps Throughput (future for many)
Note: 1TB/hour and 100TB/week fit easily within 10G of throughput

## Slide 12: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
What is important? Ordered list:
  Correctness
  Consistency
  Performance
© 2014, Energy Sciences Network
Notes: Networks are key. However, the user interface runs on systems at the edges.
The ordered list of important items is derived from the users of the network:
1) If a tool doesn’t behave correctly, the tool is broken – get another tool
2) If the tool doesn’t behave consistently, I can’t organize my life
3) Among the tools that behave correctly and consistently, choose the tool with the required performance that is easiest to use

## Slide 13: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
© 2014, Energy Sciences Network
Notes: The application sees the network as a socket.
The socket interface does not provide path diagnostics or other troubleshooting information.
TCP behaves as it does because of measures taken in the 1980s to fix the congestion collapse of the Internet
TCP makes a promise to the application – TCP will get the data to the other end, or TCP will return an error. TCP makes no promises about performance.

## Slide 14: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
© 2014, Energy Sciences Network
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 15: Working With TCP In Practice
Far easier to support TCP than to fix TCP
  People have been trying to fix TCP for years – limited success
  Like it or not we’re stuck with TCP in the general case
Pragmatically speaking, we must accommodate TCP
  Sufficient bandwidth to avoid congestion
  Zero packet loss
  Verifiable infrastructure
    Networks are complex
    Must be able to locate problems quickly
    Small footprint is a huge win – small number of devices so that problem isolation is tractable
© 2014, Energy Sciences Network
Notes: Do not underestimate the value of three TCP improvements:
RFC1323 (window scaling)
Kernel autotuning
Improved congestion algorithms
However, loss + latency is still a performance killer.
TCP must be accommodated – this is our job as engineers and architects

## Slide 16: Putting A Solution Together
Effective support for TCP-based data transfer
  Design for correct, consistent, high-performance operation
  Design for ease of troubleshooting
Easy adoption is critical
  Large laboratories and universities have extensive IT deployments
  Drastic change is prohibitively difficult
Cybersecurity – defensible without compromising performance
Borrow ideas from traditional network security
  Traditional DMZ
    Separate enclave at network perimeter (“Demilitarized Zone”)
    Specific location for external-facing services
    Clean separation from internal network
  Do the same thing for science – Science DMZ
© 2014, Energy Sciences Network
Notes: In order to accommodate TCP, we need a pragmatic engineering solution that:
Addresses the needs
Is implementable given financial, policy, and cultural constraints
Can be defended – we cannot ignore security

## Slide 17
The Science DMZ Superfecta
© 2014, Energy Sciences Network
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase
17 – ESnet Science Engagement (engage@es.net) - 11/19/14
Notes: The Science DMZ design pattern is a set of composable ideas, including:
The architectural element itself – the Science DMZ enclave
Appropriate security that does not impact performance
Dedicated systems – Data Transfer Nodes
perfSONAR
The elements of the Science DMZ can be combined in a variety of ways depending on the need

## Slide 18: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 19: Abstract or Prototype Deployment
Add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners
  Add-on to production infrastructure – lower risk
© 2014, Energy Sciences Network

## Slide 20: Science DMZ Design Pattern (Abstract)
© 2014, Energy Sciences Network
Notes: This is an abstract cartoon – nobody’s network looks exactly like this
The diagram has no management LAN, no terminal servers, etc.
However, this is the minimum network diagram that shows the essential Science DMZ components:
Science DMZ enclave
DTN
perfSONAR (in the WAN, at the border, in the Science DMZ)
Security policy controls

## Slide 21: Local And Wide Area Data Flows
© 2014, Energy Sciences Network
Notes: The green data path is susceptible to TCP performance problems stemming from packet loss combined with long distances
The red data path is very low latency – loss matters much less here (though too much loss will still cause problems)
Remember the throughput vs. latency graph

## Slide 22: Support For Multiple Projects
Science DMZ architecture allows multiple projects to put DTNs in place
  Modular architecture
  Centralized location for data servers
This may or may not work well depending on institutional politics
  Issues such as physical security can make this a non-starter
  On the other hand, some shops already have service models in place
On balance, this can provide a cost savings – it depends
  Central support for data servers vs. carrying data flows
  How far do the data flows have to go?
© 2014, Energy Sciences Network

## Slide 23: Multiple Projects
© 2014, Energy Sciences Network

## Slide 24: Supercomputer Center Deployment
High-performance networking is assumed in this environment
  Data flows between systems, between systems and storage, wide area, etc.
  Global filesystem often ties resources together
    Portions of this may not run over Ethernet (e.g. IB)
    Implications for Data Transfer Nodes
“Science DMZ” may not look like a discrete entity here
  By the time you get through interconnecting all the resources, you end up with most of the network in the Science DMZ
  This is as it should be – the point is appropriate deployment of tools, configuration, policy control, etc.
Office networks can look like an afterthought, but they aren’t
  Deployed with appropriate security controls
  Office infrastructure need not be sized for science traffic
© 2014, Energy Sciences Network

## Slide 25: Supercomputer Center
© 2014, Energy Sciences Network
Notes: Applying the Science DMZ design patterns to a supercomputer center
Note global filesystem – avoids double-copy workflow between DTNs and compute resources
DTNs are not part of major computational resource, and so are not entangled with its config
Science DMZ does not look discrete – however, the elements are here
Firewall appropriately placed
Security for major resources and DTNs implemented in network core
PerfSONAR for performance assurance

## Slide 26: Supercomputer Center Data Path
© 2014, Energy Sciences Network
Notes: DTNs are not part of major computational resource, and so are not entangled with its config
Note virtual circuit path (OSCARS, ION, SDN, etc)

## Slide 27: Development Environment
One thing that often happens is that an early power user of the Science DMZ is the network engineering group that builds it
  Service prototyping
  Deployment of test applications for other user groups to demonstrate value
The production Science DMZ is just that – production
  Once users are on it, you can’t take it down to try something new
  Stuff that works tends to attract workload
Take-home message: plan for multiple Science DMZs from the beginning – at the very least you’re going to need one for yourself
The Science DMZ model easily accommodates this
© 2014, Energy Sciences Network
Notes: Example of workload – ALS DTN became central to most data handling tasks on the beamline within about a month of deployment
The Science DMZ model can easily be replicated because of its modularity

## Slide 28: Science DMZ – Flexible Design Pattern
The Science DMZ design pattern is highly adaptable to research
Deploying a research Science DMZ is straightforward
  The basic elements are the same
    Capable infrastructure designed for the task
    Test and measurement to verify correct operation
    Security policy well-matched to the environment, application set is strictly limited to reduce risk
  Connect the research DMZ to other resources as appropriate
The same ideas apply to supporting an SDN effort
  Test/research areas for development
  Transition to production as technology matures and need dictates
  One possible trajectory follows…
© 2014, Energy Sciences Network
Notes: The next couple are examples of integrating SDN into a DMZ environment
1st it is experimental, then it gradually moves into production.

## Slide 29: Science DMZ – Separate SDN Connection
© 2014, Energy Sciences Network
Notes: Initial deployment brings SDN services to research DMZ via a separate link

## Slide 30: Science DMZ – Production SDN Connection
© 2014, Energy Sciences Network
Notes: Once SDN software for the switch platform is solid and operational models are clear, production Science DMZ supports SDN

## Slide 31: Science DMZ – SDN Campus Border
© 2014, Energy Sciences Network
Notes: When the entire production path supports SDN, SDN is another production service on the Science DMZ and we’re back to the original picture
ESnet5 supports routed traffic and OSCARS on the same platform in a similar way

## Slide 32: Common Threads
Two common threads exist in all these examples
Accommodation of TCP
  Wide area portion of data transfers traverses purpose-built path
  High performance devices that don’t drop packets
Ability to test and verify
  When problems arise (and they always will), they can be solved if the infrastructure is built correctly
  Small device count makes it easier to find issues
  Multiple test and measurement hosts provide multiple views of the data path
    perfSONAR nodes at the site and in the WAN
    perfSONAR nodes at the remote site
© 2014, Energy Sciences Network

## Slide 33: Multiple Ingress Flows, Common Egress
Hosts will typically send packets at the speed of their interface (1G, 10G, etc.)
  Instantaneous rate, not average rate
  If TCP has window available and data to send, host sends until there is either no data or no window
Hosts moving big data (e.g. DTNs) can send large bursts of back-to-back packets
  This is true even if the average rate as measured over seconds is slower (e.g. 4Gbps)
  On microsecond time scales, there is often congestion
  Router or switch must queue packets or drop them
© 2014, Energy Sciences Network
Notes: A brief introduction to the impacts of buffering on network traffic. Key points:
- Host interfaces ‘burst’ at line rate, and then wait (e.g. it’s binary behavior, not a nice steady pacing at some average rate)
- multiple ingress flows behave differently depending on the architecture of the switch. If its ‘shared’ memory, all may be using the same memory buffer. If each interface has its own, then 1 or 2 bursting may be less impactful on the rest of the interfaces.
- buffer bloat is typically not a concern in a Science DMZ

## Slide 34: Router and Switch Output Queues
Interface output queue allows the router or switch to avoid causing packet loss in cases of momentary congestion
In network devices, queue depth (or ‘buffer’) is often a function of cost
  Cheap, fixed-config LAN switches (especially in the 10G space) have inadequate buffering. Imagine a 10G ‘data center’ switch as the guilty party
  Cut-through or low-latency Ethernet switches typically have inadequate buffering (the whole point is to avoid queuing!)
Expensive, chassis-based devices are more likely to have deep enough queues
  Juniper MX and Alcatel-Lucent 7750 used in ESnet backbone
  Other vendors make such devices as well - details are important
  Thx to Jim: http://people.ucsc.edu/~warner/buffer.html
This expense is one driver for the Science DMZ architecture – only deploy the expensive features where necessary
© 2014, Energy Sciences Network
Notes: Goes along with the previous – output is just as important as input

## Slide 35: Output Queue Drops – Common Locations
© 2014, Energy Sciences Network
Notes: In the outbound direction, traffic from the cluster goes from 10G to 1G on the department core switch – the 10G DTN will burst, causing loss if the 1G output queue is too shallow
In the outbound direction, many 1G workstations can congest a single 1G uplink port
In the inbound direction, 10G of WAN traffic goes to a 1G port facing the department core switch – likely loss location (and on the wide area path to the DTN!)
There are a lot of networks with this sort of problem.
The best way to find the problem is to use perfSONAR

## Slide 36: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 37: Performance Monitoring
Everything may function perfectly when it is deployed
Eventually something is going to break
  Networks and systems are complex
  Bugs, mistakes, …
  Sometimes things just break – this is why we buy support contracts
Must be able to find and fix problems when they occur
Must be able to find problems in other networks (your network may be fine, but someone else’s problem can impact your users)
TCP was intentionally designed to hide all transmission errors from the user:
  “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From RFC793, 1981)
© 2014, Energy Sciences Network
Notes: Remember – TCP promises reliable data delivery, not performance
In order for scientists to see high-performance correct behavior consistently, network engineers must be able to find and fix problems quickly.
Waiting around for trouble tickets is clearly the wrong approach
Not all problems are immediately obvious – many are known as “soft failures”

## Slide 38: Soft Network Failures – Hidden Problems
Hard failures are well-understood
  Link down, system crash, software crash
  Traditional network/system monitoring tools designed to quickly find hard failures
Soft failures result in degraded capability
  Connectivity exists
  Performance impacted
  Typically something in the path is functioning, but not well
Soft failures are hard to detect with traditional methods
  No obvious single event
  Sometimes no indication at all of any errors
Independent testing is the only way to reliably find soft failures
© 2014, Energy Sciences Network
Notes: If something is down hard, it’s easy to find
Soft failures are often visible only from the end systems
This is what makes perfSONAR so valuable – it behaves as an end system behaves, but it measures what the network does
Remember – we want to find the problems BEFORE the users do

## Slide 39: Sample Soft Failures
Rebooted router with full route table
Gradual failure of optical line card
Gb/s
normal performance
degrading performance
repair
one month
© 2014, Energy Sciences Network
Notes: 2 quick examples of soft failures:
The first of these was a Cisco 6509 that had over-filled its route table due to a misconfiguration, but the config had been fixed. The performance problem persisted until the router was rebooted. This could not have been found by auditing the configuration.
The second is a relatively common problem – in a big network there are a lot of pluggable optics packs, and sometimes they just go bad. Often they cause performance problems (soft failure) for a long time before they finally die (hard failure)

## Slide 40: Testing Infrastructure – perfSONAR
perfSONAR is:
  A widely-deployed test and measurement infrastructure
    ESnet, Internet2, US regional networks, international networks
    Laboratories, supercomputer centers, universities
  A suite of test and measurement tools
  A collaboration that builds and maintains the toolkit
By installing perfSONAR, a site can leverage over 1100 test servers deployed around the world
perfSONAR is ideal for finding soft failures
  Alert to existence of problems
  Fault isolation
  Verification of correct operation
© 2014, Energy Sciences Network
Notes: perfSONAR is the gold standard tool for performance testing, measurement, and interdomain troubleshooting in science networks

## Slide 41: perfSONAR Deployment Footprint
© 2014, Energy Sciences Network
Notes: Deployment curve through April 2014

## Slide 42: Lookup Service Directory Search: http://stats.es.net/ServicesDirectory/
© 2014, Energy Sciences Network
Notes: How to find perfSONAR servers and services

## Slide 43: perfSONAR Dashboard: http://ps-dashboard.es.net
© 2014, Energy Sciences Network
Notes: Integrating regular testing into a visualization (ESnet example).
Performance data is public
The tool can trigger alerts to notify NOC staff.
This is a very valuable tool for setting expectations

## Slide 44: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 45: Dedicated Systems – Data Transfer Node
The DTN is dedicated to data transfer
Set up specifically for high-performance data movement
  System internals (BIOS, firmware, interrupts, etc.)
  Network stack
  Storage (global filesystem, Fibrechannel, local RAID, etc.)
  High performance tools
  No extraneous software
Limitation of scope and function is powerful
  No conflicts with configuration for other tasks
  Small application set makes cybersecurity easier
© 2014, Energy Sciences Network
Notes: All aspects of the DTN must be tuned – even the BIOS matters
Limit the scope of the DTN as well – its job is data movement, its job is not to have office software on it.
Craft a specific security profile/policy around its only task.

## Slide 46: Data Transfer Tools For DTNs
Parallelism is important
  It is often easier to achieve a given performance level with four parallel connections than one connection
  Several tools offer parallel transfers, including Globus/GridFTP
Latency interaction is critical
  Wide area data transfers have much higher latency than LAN transfers
  Many tools and protocols assume a LAN
Workflow integration is important
Key tools: Globus Online, HPN-SSH
© 2014, Energy Sciences Network
Notes: DTN is entry point for data from multi-facility workflows – use the right tool for the right job

## Slide 47: Data Transfer Tool Comparison
In addition to the network, using the right data transfer tool is critical
Data transfer test from Berkeley, CA to Argonne, IL (near Chicago). RTT = 53 ms, network capacity = 10Gbps.
    Tool Throughput
    scp: 140 Mbps
    HPN patched scp: 1.2 Gbps
    ftp 1.4 Gbps
    GridFTP, 4 streams 5.4 Gbps
    GridFTP, 8 streams 6.6 Gbps
    Note that to get more than 1 Gbps (125 MB/s) disk to disk requires properly engineered storage (RAID, parallel filesystem, etc.)
© 2014, Energy Sciences Network
Notes: Comparison of legacy and recommended tools.
Note that rsync over HPN-SSH is reasonable in a 1Gbps environment – if you are stuck with rsync over SSH, at least use HPN-SSH.
Globus is now deployed at a large number of major scientific sites – the basic data transfer functionality is free.

## Slide 48: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 49: Science DMZ Security
Goal – disentangle security policy and enforcement for science flows from security for business systems
Rationale
  Science data traffic is simple from a security perspective
  Narrow application set on Science DMZ
    Data transfer, data streaming packages
    No printers, document readers, web browsers, building control systems, financial databases, staff desktops, etc.
  Security controls that are typically implemented to protect business resources often cause performance problems
Separation allows each to be optimized
© 2014, Energy Sciences Network

## Slide 50: Performance Is A Core Requirement
Core information security principles
  Confidentiality, Integrity, Availability (CIA)
  Often, CIA and risk mitigation result in poor performance
In data-intensive science, performance is an additional core mission requirement: CIA  PICA
  CIA principles are important, but if performance is compromised the science mission fails
  Not about “how much” security you have, but how the security is implemented
  Need a way to appropriately secure systems without performance compromises
© 2014, Energy Sciences Network
Notes: You can still have really tight security if you need really tight security – just do it in a way that does not cause performance problems for traffic permitted by policy

## Slide 51: Placement Outside the Firewall
The Science DMZ resources are placed outside the enterprise firewall for performance reasons
  The meaning of this is specific – Science DMZ traffic does not traverse the firewall data plane
  Packet filtering is fine – just don’t do it with a firewall
Lots of heartburn over this, especially from the perspective of a conventional firewall manager
  Lots of organizational policy directives mandating firewalls
  Firewalls are designed to protect converged enterprise networks
  Why would you put critical assets outside the firewall???
The answer is that firewalls are typically a poor fit for high-performance science applications
© 2014, Energy Sciences Network
Notes: Packets do not traverse a firewall device
Firewalls are typically engineered very differently than routers and switches

## Slide 52: Firewall Capabilities and Science Traffic
Firewalls have a lot of sophistication in an enterprise setting
  Application layer protocol analysis (HTTP, POP, MSRPC, etc.)
  Built-in VPN servers
  User awareness
Data-intensive science flows typically don’t match this profile
  Common case – data on filesystem A needs to be on filesystem Z
    Data transfer tool verifies credentials over an encrypted channel
    Then open a socket or set of sockets, and send data until done (1TB, 10TB, 100TB, …)
  One workflow can use 10% to 50% or more of a 10G network link
Do we have to use a firewall?
© 2014, Energy Sciences Network

## Slide 53: Firewalls As Access Lists
When you ask a firewall administrator to allow data transfers through the firewall, what do they ask for?
  IP address of your host
  IP address of the remote host
  Port range
  That looks like an ACL to me!
No special config for advanced protocol analysis – just address/port
Router ACLs are better than firewalls at address/port filtering
  ACL capabilities are typically built into the router
  Router ACLs typically do not drop traffic permitted by policy
© 2014, Energy Sciences Network
Notes: Remember – we have mission requirements for high performance scientific data mobility, and business requirements for cost efficiency.
A firewall mandate is an expensive solution that is a poor match for the task at hand and jeopardizes the scientific mission of the organization.

## Slide 54: Security Without Firewalls
Data intensive science traffic interacts poorly with firewalls
Does this mean we ignore security? NO!
  We must protect our systems
  We just need to find a way to do security that does not prevent us from getting the science done
Key point – security policies and mechanisms that protect the Science DMZ should be implemented so that they do not compromise performance
Traffic permitted by policy should not experience performance impact as a result of the application of policy
© 2014, Energy Sciences Network

## Slide 55: Firewall Performance Example
Observed performance, via perfSONAR, through a firewall:
Observed performance, via perfSONAR, bypassing firewall:
Almost 20 times slower through the firewall
Huge improvement without the firewall
© 2014, Energy Sciences Network
Notes: Real life example, in front of and in back of a firewall that was dramatically impacting performance
perfSONAR is good at finding these issues
Engineers still have to take action to fix the problem

## Slide 56: If Not Firewalls, Then What?
Intrusion Detection Systems (IDS)
  One example is Bro – http://bro-ids.org/
  Bro is high-performance and battle-tested
    Bro protects several high-performance national assets
    Bro can be scaled with clustering: http://www.bro-ids.org/documentation/cluster.html
  Other IDS solutions are available also
Netflow and IPFIX can provide intelligence, but not filtering
Openflow and SDN
  Using Openflow to control access to a network-based service seems pretty obvious
  This could significantly reduce the attack surface for any authenticated network service
  This would only work if the Openflow device had a robust data plane
© 2014, Energy Sciences Network

## Slide 57: If Not Firewalls, Then What? (2)
Aggressive access lists
  More useful with project-specific DTNs
  If the purpose of the DTN is to exchange data with a small set of remote collaborators, the ACL is pretty easy to write
  Large-scale data distribution servers are hard to handle this way (but then, the firewall ruleset for such a service would be pretty open too)
Limitation of the application set
  One of the reasons to limit the application set in the Science DMZ is to make it easier to protect
  Keep desktop applications off the DTN (and watch for them anyway using logging, netflow, etc – take violations seriously)
  This requires collaboration between people – networking, security, systems, and scientists
© 2014, Energy Sciences Network

## Slide 58: Collaboration Within The Organization
All stakeholders should collaborate on Science DMZ design, policy, and enforcement
The security people have to be on board
  Remember: security people already have political cover – it’s called the firewall
  If a host gets compromised, the security officer can say they did their due diligence because there was a firewall in place
  If the deployment of a Science DMZ is going to jeopardize the job of the security officer, expect pushback
The Science DMZ is a strategic asset, and should be understood by the strategic thinkers in the organization
  Changes in security models
  Changes in operational models
  Enhanced ability to compete for funding
  Increased institutional capability – greater science output
© 2014, Energy Sciences Network

## Slide 59: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 60: Challenges to Network Adoption
Causes of performance issues are complicated for users.
Lack of communication and collaboration between the CIO’s office and researchers on campus.
Lack of IT expertise within a science collaboration or experimental facility
User’s performance expectations are low (“The network is too slow”, “I tried it and it didn’t work”).
Cultural change is hard (“we’ve always shipped disks!”).
Scientists want to do science not IT support
The Capability Gap
© 2014, Energy Sciences Network
Notes: The struggle in engagement – management, engineering, and users often have dug in on bad behavior.
This amounts a capability gap – there is a disconnect from the capabilities of the network and the ability of the scientists to effectively use it
To fix this, we need to get everyone working toward a common goal:
- Management must fund and support the base needs of research
- IT is there to support the users in doing things correctly, and having all components work

## Slide 61: Requirements Reviews
http://www.es.net/about/science-requirements/network-requirements-reviews/
The purpose of these reviews is to accurately characterize the near-term, medium-term and long-term network requirements of the science conducted by each program office.
The reviews attempt to bring about a network-centric understanding of the science process used by the researchers and scientists, to derive network requirements.
We have found this to be an effective method for determining network requirements for ESnet's customer base.
Notes: 2006
ELI + company
Led to science DMZ and other important end site innovations

## Slide 62
High Energy Physics
Nuclear Physics
Basic Energy Science
Fusion Energy Sciences
Advanced Scientific Computing Research
Biological and Environmental Research
Photo courtesy of LBL
Photo courtesy of LBL
Photo courtesy of SLAC
Photo courtesy of PPPL
Photo courtesy of NIST
Photo courtesy of JGI

## Slide 63: How do we know what our scientists need?
Each Program Office has a dedicated requirements review every three years
Two workshops per year, attendees chosen by science programs
Discussion centered on science case studies
    Instruments and Facilities – the “hardware”
    Process of Science – science workflow
    Collaborators
    Challenges
Network requirements derived from science case studies + discussions
Reports contain requirements analysis, case study text, outlook
Notes: Two reviews per year, One review per program office every 3 years
Goals –
1. Accurately characterize current and future network requirements
2. Collect network requirements from scientists and Program Office
Structure
Elicit information from managers, scientists and network users regarding usage patterns, science process, instruments and facilities – codify in “Case Studies”
Case studies focus on two different aspects of the science
    Instruments and Facilities – the “hardware” of science
    Process of Science – the way in which the Instruments and Facilities are used in the conduct of the science
    Synthesize network requirements from the Case Studies
ESnet’s core mission is to serve the DOE/SC science programs
    Large-scale data movement
    Network services to enable science
Network implications arise from the conduct of science
    Science instruments and facilities
    Process of science
    How will these change over time?

## Slide 64: 2013 BER Sample Findings: Environmental Molecular Sciences Laboratory (EMSL)
“EMSL frequently needs to ship physical copies of media to users when data sizes exceed a few GB. More often than not, this is due to lack of bandwidth or storage resources at the user's home institution.”

## Slide 65: Overview
ESnet Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
On the Topic of Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 66
The Science DMZ design pattern provides a flexible model for supporting high-performance data transfers and workflows
Key elements:
  Accommodation of TCP
    Sufficient bandwidth to avoid congestion
    Loss-free IP service
  Location – near the site perimeter if possible
  Test and measurement
  Dedicated systems
  Appropriate security
Support for advanced capabilities (e.g. SDN) is much easier with a Science DMZ
Wrapup
© 2014, Energy Sciences Network

## Slide 67: The Science DMZ in 1 Slide
Consists of three key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with end users
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
© 2014, Energy Sciences Network
Notes: Single slide summary

## Slide 68: Links
  ESnet fasterdata knowledge base
    http://fasterdata.es.net/
  Science DMZ paper
    http://www.es.net/assets/pubs_presos/sc13sciDMZ-final.pdf
  Science DMZ email list
    https://gab.es.net/mailman/listinfo/sciencedmz
  perfSONAR
    http://fasterdata.es.net/performance-testing/perfsonar/
    http://www.perfsonar.net
© 2014, Energy Sciences Network

## Slide 69: Thanks!
Jason Zurawski – zurawski@es.net
Science Engagement Engineer, ESnet
Lawrence Berkeley National Laboratory
New Mexico Technology in Education (NMTIE)
November 19th, 2014