## Slide 1: The Science DMZ
Eli Dart, Network Engineer
ESnet Science Engagement
Lawrence Berkeley National Laboratory
BioTeam Science DMZ 101 Webinar
May 18, 2015

## Slide 2: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Data Transfer Nodes & Applications
Science DMZ Security
Wrap Up
Handoff to Jason - perfSONAR
© 2015, Energy Sciences Network

## Slide 3: Motivation
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors
  Data movement and data analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult
© 2015, Energy Sciences Network
Notes: Human factors – attention span, ability to manage complexity – these are constant
There is a huge amount of promise in data-intensive science. Effective use of networks can help realize those benefits.
The Science DMZ model helps address the difficulties scientists often experience with using networks.

## Slide 4: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
What is important? Ordered list:
  Correctness
  Consistency
  Performance
© 2015, Energy Sciences Network
Notes: Networks are key. However, the user interface runs on systems at the edges.
The ordered list of important items is derived from the users of the network:
1) If a tool doesn’t behave correctly, the tool is broken – get another tool
2) If the tool doesn’t behave consistently, I can’t organize my life
3) Among the tools that behave correctly and consistently, choose the tool with the required performance that is easiest to use

## Slide 5: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
  Packet loss in conjunction with latency is a performance killer
© 2015, Energy Sciences Network
Notes: The application sees the network as a socket.
The socket interface does not provide path diagnostics or other troubleshooting information.
TCP behaves as it does because of measures taken in the 1980s to fix the congestion collapse of the Internet
TCP makes a promise to the application – TCP will get the data to the other end, or TCP will return an error. TCP makes no promises about performance.

## Slide 6: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
© 2015, Energy Sciences Network
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 7: Working With TCP In Practice
Far easier to support TCP than to fix TCP
  People have been trying to fix TCP for years – limited success
  Like it or not we’re stuck with TCP in the general case
Pragmatically speaking, we must accommodate TCP
  Sufficient bandwidth to avoid congestion
  Zero packet loss
  Verifiable infrastructure
    Networks are complex
    Must be able to locate problems quickly
    Small footprint is a huge win – small number of devices so that problem isolation is tractable
What if I don’t use TCP?
  TCP benefits are significant, but are not the only reason for Science DMZ
  Architecture, cost, operational benefits
© 2015, Energy Sciences Network
Notes: Do not underestimate the value of three TCP improvements:
RFC1323 (window scaling)
Kernel autotuning
Improved congestion algorithms
However, loss + latency is still a performance killer.
TCP must be accommodated – this is our job as engineers and architects

## Slide 8: Putting A Solution Together
Effective support for TCP-based data transfer
  Design for correct, consistent, high-performance operation
  Design for ease of troubleshooting
Easy adoption is critical
  Large laboratories and universities have extensive IT deployments
  Drastic change is prohibitively difficult
Cybersecurity – defensible without compromising performance
Borrow ideas from traditional network security
  Traditional DMZ
    Separate enclave at network perimeter (“Demilitarized Zone”)
    Specific location for external-facing services
    Clean separation from internal network
  Do the same thing for science – Science DMZ
© 2015, Energy Sciences Network
Notes: In order to accommodate TCP, we need a pragmatic engineering solution that:
Addresses the needs
Is implementable given financial, policy, and cultural constraints
Can be defended – we cannot ignore security

## Slide 9
Dedicated Systems for Data Transfer
Network Architecture
Performance Testing & Measurement
  Data Transfer Node
High performance
Configured specifically for data transfer
Proper tools
Science DMZ
Dedicated network location for high-speed data resources
Appropriate security
Easy to deploy - no need to redesign the whole network
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
The Science DMZ Design Pattern
© 2015, Energy Sciences Network
Notes: The Science DMZ design pattern is a set of composable ideas, including:
The architectural element itself – the Science DMZ enclave
Appropriate security that does not impact performance
Dedicated systems – Data Transfer Nodes
perfSONAR
The elements of the Science DMZ can be combined in a variety of ways depending on the need

## Slide 10: Abstract or Prototype Deployment
Add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners
  Add-on to production infrastructure – lower risk
© 2015, Energy Sciences Network

## Slide 11: Science DMZ Design Pattern (Abstract)
© 2015, Energy Sciences Network
Notes: This is an abstract cartoon – nobody’s network looks exactly like this
The diagram has no management LAN, no terminal servers, etc.
However, this is the minimum network diagram that shows the essential Science DMZ components:
Science DMZ enclave
DTN
perfSONAR (in the WAN, at the border, in the Science DMZ)
Security policy controls

## Slide 12: Local And Wide Area Data Flows
© 2015, Energy Sciences Network
Notes: The green data path is susceptible to TCP performance problems stemming from packet loss combined with long distances
The red data path is very low latency – loss matters much less here (though too much loss will still cause problems)
Remember the throughput vs. latency graph

## Slide 13: Support For Multiple Projects
Science DMZ architecture allows multiple projects to put DTNs in place
  Modular architecture
  Centralized location for data servers
This may or may not work well depending on institutional politics
  Issues such as physical security can make this a non-starter
  On the other hand, some shops already have service models in place
On balance, this can provide a cost savings – it depends
  Central support for data servers vs. carrying data flows
  How far do the data flows have to go?
© 2015, Energy Sciences Network

## Slide 14: Multiple Projects
© 2015, Energy Sciences Network

## Slide 15: Supercomputer Center Deployment
High-performance networking is assumed in this environment
  Data flows between systems, between systems and storage, wide area, etc.
  Global filesystem often ties resources together
    Portions of this may not run over Ethernet (e.g. IB)
    Implications for Data Transfer Nodes
“Science DMZ” may not look like a discrete entity here
  By the time you get through interconnecting all the resources, you end up with most of the network in the Science DMZ
  This is as it should be – the point is appropriate deployment of tools, configuration, policy control, etc.
Office networks can look like an afterthought, but they aren’t
  Deployed with appropriate security controls
  Office infrastructure need not be sized for science traffic
© 2015, Energy Sciences Network

## Slide 16: Supercomputer Center
© 2015, Energy Sciences Network
Notes: Applying the Science DMZ design patterns to a supercomputer center
Note global filesystem – avoids double-copy workflow between DTNs and compute resources
DTNs are not part of major computational resource, and so are not entangled with its config
Science DMZ does not look discrete – however, the elements are here
Firewall appropriately placed
Security for major resources and DTNs implemented in network core
PerfSONAR for performance assurance

## Slide 17: Supercomputer Center Data Path
© 2015, Energy Sciences Network
Notes: DTNs are not part of major computational resource, and so are not entangled with its config
Note virtual circuit path (OSCARS, ION, SDN, etc)

## Slide 18: Major Data Site Deployment
In some cases, large scale data service is the major driver
  Huge volumes of data (Petabytes or more) – ingest, export
  Large number of external hosts accessing/submitting data
Single-pipe deployments don’t work
  Everything is parallel
    Networks (Nx10G LAGs, soon to be Nx100G)
    Hosts – data transfer clusters, no individual DTNs
    WAN connections – multiple entry, redundant equipment
  Choke points (e.g. firewalls) just cause problems
© 2015, Energy Sciences Network

## Slide 19: Data Site – Architecture
© 2015, Energy Sciences Network
Notes: Major data resource (e.g. LHC Tier1)
Lots of parallelism (data transfer clusters)
Firewalls as appropriate
PerfSONAR

## Slide 20: Data Site – Data Path
© 2015, Energy Sciences Network
Notes: The loss-sensitive data path covers the entire network front-end
However – note that the Science DMZ principles are all still here
Especially note security – would you want to drag all this through the enterprise firewall? Far better to do the security in the Science DMZ.

## Slide 21: Distributed Science DMZ
Fiber-rich environment enables a distributed Science DMZ
  No need to accommodate all equipment in one location
  Allows the deployment of institutional science service
WAN services arrive at the site in the normal way
Dark fiber distributes connectivity to Science DMZ services throughout the site
  Departments with their own networking groups can manage their own local Science DMZ infrastructure
  Facilities or buildings can be served without building up the business network to support those flows
Security is more complex
  Remote infrastructure must be monitored
  Several technical remedies exist (arpwatch, no DHCP, separate address space, etc.)
  Solutions depend on relationships with security groups
© 2015, Energy Sciences Network

## Slide 22: Distributed Science DMZ – Dark Fiber
© 2015, Energy Sciences Network
Notes: This provides distributed connectivity to a central Science DMZ

## Slide 23: Multiple Science DMZs – Dark Fiber
© 2015, Energy Sciences Network
Notes: In this case, each Science DMZ can be run separately (e.g. by individual departments or laboratories)

## Slide 24: Common Threads
Two common threads exist in all these examples
Accommodation of TCP
  Wide area portion of data transfers traverses purpose-built path
  High performance devices that don’t drop packets
Ability to test and verify
  When problems arise (and they always will), they can be solved if the infrastructure is built correctly
  Small device count makes it easier to find issues
  Multiple test and measurement hosts provide multiple views of the data path
    perfSONAR nodes at the site and in the WAN
    perfSONAR nodes at the remote site
© 2015, Energy Sciences Network

## Slide 25: Development Environment
One thing that often happens is that an early power user of the Science DMZ is the network engineering group that builds it
  Service prototyping
  Deployment of test applications for other user groups to demonstrate value
The production Science DMZ is just that – production
  Once users are on it, you can’t take it down to try something new
  Stuff that works tends to attract workload
Take-home message: plan for multiple Science DMZs from the beginning – at the very least you’re going to need one for yourself
The Science DMZ model easily accommodates this
© 2015, Energy Sciences Network
Notes: Example of workload – ALS DTN became central to most data handling tasks on the beamline within about a month of deployment
The Science DMZ model can easily be replicated because of its modularity

## Slide 26: But What If I Don’t Use TCP?
Some sites use non-TCP tools/protocols
  Open source (e.g. UDT)
  Commercial (e.g. Aspera)
Does this mean we don’t need a Science DMZ?
  The short answer is no…a Science DMZ is still very valuable
  There are many different reasons
    Tension between security and performance (see next section)
    Offload bandwidth hogs from enterprise network
    Cost savings – consolidate high-performance services, reduce device count
    Flexibility of provisioning, policy application, enforcement
    Flexibility of technology adoption
Flexibility offered by Science DMZ is critical
  Decouple enterprise network (stability is key) from science infrastructure
  How fast can you adapt? How fast must you adapt?
© 2015, Energy Sciences Network
Notes: The flexibility issue is key.
* How fast can your enterprise network change to fit your science needs?
* How fast are your science needs changing?

## Slide 27: Support For New Technologies
The Science DMZ design pattern is highly adaptable to new technologies
  Software Defined Networking (SDN)
  Non-IP protocols (RDMA over Ethernet)
Deploying new technologies in a Science DMZ is straightforward
  The basic elements are the same
    Capable infrastructure designed for the task
    Test and measurement to verify correct operation
    Security policy well-matched to the environment
    Application set strictly limited to reduce security risk
  Change footprint is small – often just a single router or switch
  The rest of the infrastructure need not change
© 2015, Energy Sciences Network

## Slide 28: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Data Transfer Nodes & Applications
Science DMZ Security
Wrap Up
Handoff to Jason - perfSONAR
© 2015, Energy Sciences Network

## Slide 29: Dedicated Systems – Data Transfer Nodes
The DTN is dedicated to data transfer
Set up specifically for high-performance data movement
  System internals (BIOS, firmware, interrupts, etc.)
  Network stack
  Storage (global filesystem, Fibrechannel, local RAID, etc.)
  High performance tools
  No extraneous software
Limitation of scope and function is powerful
  No conflicts with configuration for other tasks
  Small application set makes cybersecurity easier
© 2015, Energy Sciences Network
Notes: All aspects of the DTN must be tuned – even the BIOS matters
Limit the scope of the DTN as well – its job is data movement, its job is not to have office software on it.
Craft a specific security profile/policy around its only task.

## Slide 30: Data Transfer Tools For DTNs
Parallelism is important
  It is often easier to achieve a given performance level with four parallel connections than one connection
  Several tools offer parallel transfers, including Globus/GridFTP
Latency interaction is critical
  Wide area data transfers have much higher latency than LAN transfers
  Many tools and protocols assume a LAN
Workflow integration is important
Key free tools: Globus Online, HPN-SSH
Large Aspera footprint in biomedical space – excellent tool
© 2015, Energy Sciences Network
Notes: DTN is entry point for data from multi-facility workflows – use the right tool for the right job

## Slide 31: Data Transfer Tool Comparison
In addition to the network, using the right data transfer tool is critical
Data transfer test from Berkeley, CA to Argonne, IL (near Chicago). RTT = 53 ms, network capacity = 10Gbps.
    Tool Throughput
    scp: 140 Mbps
    HPN patched scp: 1.2 Gbps
    ftp 1.4 Gbps
    GridFTP, 4 streams 5.4 Gbps
    GridFTP, 8 streams 6.6 Gbps
    Note that to get more than 1 Gbps (125 MB/s) disk to disk requires properly engineered storage (RAID, parallel filesystem, etc.)
© 2015, Energy Sciences Network
Notes: Comparison of legacy and recommended tools.
Note that rsync over HPN-SSH is reasonable in a 1Gbps environment – if you are stuck with rsync over SSH, at least use HPN-SSH.
Globus is now deployed at a large number of major scientific sites – the basic data transfer functionality is free.

## Slide 32: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Data Transfer Nodes & Applications
Science DMZ Security
Wrap Up
Handoff to Jason - perfSONAR
© 2015, Energy Sciences Network

## Slide 33: Science DMZ Security
Goal – disentangle security policy and enforcement for science flows from security for business systems
Rationale
  Science data traffic is simple from a security perspective
  Narrow application set on Science DMZ
    Data transfer, data streaming packages
    No printers, document readers, web browsers, building control systems, financial databases, staff desktops, etc.
  Security controls that are typically implemented to protect business resources often cause performance problems
Separation allows each to be optimized
© 2015, Energy Sciences Network

## Slide 34: Performance Is A Core Requirement
Core information security principles
  Confidentiality, Integrity, Availability (CIA)
  Often, CIA and risk mitigation result in poor performance
In data-intensive science, performance is an additional core mission requirement: CIA  PICA
  CIA principles are important, but if performance is compromised the science mission fails
  Not about “how much” security you have, but how the security is implemented
  Need a way to appropriately secure systems without performance compromises
© 2015, Energy Sciences Network
Notes: You can still have really tight security if you need really tight security – just do it in a way that does not cause performance problems for traffic permitted by policy

## Slide 35: Placement Outside the Firewall
The Science DMZ resources are placed outside the enterprise firewall for performance reasons
  The meaning of this is specific – Science DMZ traffic does not traverse the firewall data plane
  Packet filtering is fine – just don’t do it with a firewall
Lots of heartburn over this, especially from the perspective of a conventional firewall manager
  Lots of organizational policy directives mandating firewalls
  Firewalls are designed to protect converged enterprise networks
  Why would you put critical assets outside the firewall???
The answer is that firewalls are typically a poor fit for high-performance science applications
© 2015, Energy Sciences Network
Notes: Packets do not traverse a firewall device
Firewalls are typically engineered very differently than routers and switches

## Slide 36: Firewall Internals
Typical firewalls are composed of a set of processors which inspect traffic in parallel
  Traffic distributed among processors such that all traffic for a particular connection goes to the same processor
  Simplifies state management
  Parallelization scales deep analysis
Excellent fit for enterprise traffic profile
  High connection count, low per-connection data rate
  Complex protocols with embedded threats
Each processor is a fraction of firewall link speed
  Significant limitation for data-intensive science applications
  Overload causes packet loss – performance crashes
© 2015, Energy Sciences Network
Notes: Each individual processor is typically a fraction of link speed (e.g. eight 1.25Gbps processors for a 10G firewall)

## Slide 37: What’s Inside Your Firewall?
Vendor: “but wait – we don’t do this anymore!”
  It is true that vendors are working toward line-rate 10G firewalls, and some may even have them now
  10GE has been deployed in science environments for over 10 years
  Firewall internals have only recently started to catch up with the 10G world
  100GE is being deployed now, 40Gbps host interfaces are available now
  Firewalls are behind again
In general, IT shops want to get 5+ years out of a firewall purchase
  This often means that the firewall is years behind the technology curve
  Whatever you deploy now, that’s the hardware feature set you get
  When a new science project tries to deploy data-intensive resources, they get whatever feature set was purchased several years ago
© 2015, Energy Sciences Network
Notes: As an element of network design, the enterprise firewall is a poor fit for high-performance scientific applications
Find another way to secure the high-performance scientific applications

## Slide 38: Firewall Capabilities and Science Traffic
Commercial firewalls have a lot of sophistication in an enterprise setting
  Application layer protocol analysis (HTTP, POP, MSRPC, etc.)
  Built-in VPN servers
  User awareness
Data-intensive science flows typically don’t match this profile
  Common case – data on filesystem A needs to be on filesystem Z
    Data transfer tool verifies credentials over an encrypted channel
    Then open a socket or set of sockets, and send data until done (1TB, 10TB, 100TB, …)
  One workflow can use 10% to 50% or more of a 10G network link
Do we have to use a commercial firewall?
© 2015, Energy Sciences Network

## Slide 39: Firewalls As Access Lists
When you ask a firewall administrator to allow data transfers through the firewall, what do they ask for?
  IP address of your host
  IP address of the remote host
  Port range
  That looks like an ACL to me!
No special config for advanced protocol analysis – just address/port
Router ACLs are better than firewalls at address/port filtering
  ACL capabilities are typically built into the router
  Router ACLs typically do not drop traffic permitted by policy
© 2015, Energy Sciences Network
Notes: Remember – we have mission requirements for high performance scientific data mobility, and business requirements for cost efficiency.
A firewall mandate is an expensive solution that is a poor match for the task at hand and jeopardizes the scientific mission of the organization.

## Slide 40: Security Without Firewalls
Data intensive science traffic interacts poorly with firewalls
Does this mean we ignore security? NO!
  We must protect our systems
  We just need to find a way to do security that does not prevent us from getting the science done
Key point – security policies and mechanisms that protect the Science DMZ should be implemented so that they do not compromise performance
Traffic permitted by policy should not experience performance impact as a result of the application of policy
© 2015, Energy Sciences Network

## Slide 41: If Not Firewalls, Then What?
Remember – the goal is to protect systems in a way that allows the science mission to succeed
I like something I heard at NERSC – paraphrasing: “Security controls should enhance the utility of science infrastructure.”
There are multiple ways to solve this – some are technical, and some are organizational/sociological
I’m not going to lie to you – this is harder than just putting up a firewall and closing your eyes
© 2015, Energy Sciences Network
Notes: It will probably work better because the firewall isn’t doing that much for high-performance DTNs anyway

## Slide 42: Other Technical Capabilities
Intrusion Detection Systems (IDS)
  One example is Bro – http://bro-ids.org/
  Bro is high-performance and battle-tested
    Bro protects several high-performance national assets
    Bro can be scaled with clustering: http://www.bro-ids.org/documentation/cluster.html
  Other IDS solutions are available also
Netflow and IPFIX can provide intelligence, but not filtering
Openflow and SDN
  Using Openflow to control access to a network-based service seems pretty obvious
  This could significantly reduce the attack surface for any authenticated network service
  This would only work if the Openflow device had a robust data plane
© 2015, Energy Sciences Network

## Slide 43: Other Technical Capabilities (2)
Aggressive access lists
  More useful with project-specific DTNs
  If the purpose of the DTN is to exchange data with a small set of remote collaborators, the ACL is pretty easy to write
  Large-scale data distribution servers are hard to handle this way (but then, the firewall ruleset for such a service would be pretty open too)
Limitation of the application set
  One of the reasons to limit the application set in the Science DMZ is to make it easier to protect
  Keep desktop applications off the DTN (and watch for them anyway using logging, netflow, etc – take violations seriously)
  This requires collaboration between people – networking, security, systems, and scientists
© 2015, Energy Sciences Network

## Slide 44: Sensitive Data Environments – Challenges
Additional technical requirements
  Encryption in flight
  Firewalls mandated by policy, present in HIPAA risk controls
Significant costs for breaches
  Large dollars
  Reputation
Still significant need for data sharing
  Within context/confines of approved collaborations
  Huge health, scientific, and financial benefits for a working model
© 2015, Energy Sciences Network

## Slide 45: What Is A Firewall?
Marketplace view
  Specific security appliance, with “Firewall” printed on the side
  Lots of protocol awareness, intelligence
  Application awareness
  User awareness (VPN, specific access controls, etc.)
  Designed for large concurrent user count, low per-user bandwidth (enterprise traffic)
IT Organization view
  “Firewall” appliance, purchased from the commercial marketplace
  The place in the network where security policy gets applied
  Owned by the security group, not by the networking group
  Primary risk mitigation mechanism
NIST view (Publication 800-41 rev. 1, Sep. 2009)
  “Firewalls are devices or programs that control the flow of network traffic between networks or hosts that employ differing security postures”
  This is very general, and does not match marketplace view or IT org. view
© 2015, Energy Sciences Network

## Slide 46: NIST Sees Two Firewalls, IT Shop Sees One
Stateful
Stateless
© 2015, Energy Sciences Network
Notes: From NIST perspective, this diagram has two firewalls
From marketplace perspective it has only one
Most IT shops see only one

## Slide 47: Stateful Inspection For Science DMZ Traffic?
Science DMZ traffic profile
  Small number of connections or flows
  Large per-connection data rate (Gigabit scale or higher)
  Large per-connection data volume (Terabyte scale or higher)
Stateless firewall
  Address/port filtering (which systems use which service)
  TCP connection initiation direction (ACK flag)
Stateful firewall adds
  TCP sequence number tracking (but Linux stack is as good or better compared to firewall TCP mitigations)
  Protocol/app analysis (but not for the apps used in DMZ)
  DoS protection (but the Science DMZ assets are filtered already)
© 2015, Energy Sciences Network

## Slide 48: Systems View Of Science Infrastructure
Security is a component, not a gatekeeper
Think about the workflows
Think about the interfaces to data (tools, applications)
  How do collaborators access data?
  How could they access data if the architecture were different?
Think about costs/benefits
  What is a new cancer breakthrough worth?
  $30k for some DTNs – what is that in context?
Think about risks
  What risks do specific technologies mitigate?
  What are opportunity costs of poor performance?
© 2015, Energy Sciences Network

## Slide 49: Collaboration Within The Organization
All stakeholders should collaborate on Science DMZ design, policy, and enforcement
The security people have to be on board
  Remember: security people already have political cover – it’s called the firewall
  If a host gets compromised, the security officer can say they did their due diligence because there was a firewall in place
  If the deployment of a Science DMZ is going to jeopardize the job of the security officer, expect pushback
The Science DMZ is a strategic asset, and should be understood by the strategic thinkers in the organization
  Changes in security models
  Changes in operational models
  Enhanced ability to compete for funding
  Increased institutional capability – greater science output
© 2015, Energy Sciences Network

## Slide 50: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Data Transfer Nodes & Applications
Science DMZ Security
Wrap Up
Handoff to Jason - perfSONAR
© 2015, Energy Sciences Network

## Slide 51: Context: Science DMZ Adoption
DOE National Laboratories
  Both large and small sites
  HPC centers, LHC sites, experimental facilities
NSF CC-NIE and CC*IIE programs leverage Science DMZ
  $40M and counting (CC*DNI awards coming soon, estimate additional $18M to $20M)
  Significant investments across the US university complex, ~130 awards
  Big shoutout to Kevin Thompson and the NSF – these programs are critically important
National Institutes of Health
  100G network infrastructure refresh
US Department of Agriculture
  Agricultural Research Service is building a new science network based on the Science DMZ model
  https://www.fbo.gov/index?s=opportunity&mode=form&tab=core&id=a7f291f4216b5a24c1177a5684e1809b
Other US agencies looking at Science DMZ model
  NASA
  NOAA
Australian Research Data Storage Infrastructure (RDSI)
  Science DMZs at major sites, connected by a high speed network
  https://www.rdsi.edu.au/dashnet
  https://www.rdsi.edu.au/dashnet-deployment-rdsi-nodes-begins
© 2015, Energy Sciences Network

## Slide 52: Context: Community Capabilities
Many Science DMZs directly support science applications
  LHC (Run 2 is coming soon)
  Experiment operation (Fusion, Light Sources, etc.)
  Data transfer into/out of HPC facilities
Many Science DMZs are SDN-ready
  Openflow-capable gear
  SDN research ongoing
High-performance components
  High-speed WAN connectivity
  perfSONAR deployments
  DTN deployments
Metcalfe’s Law of Network Utility
  Value proportional to the square of the number of DMZs? n log(n)?
  Cyberinfrastructure value increases as we all upgrade
© 2015, Energy Sciences Network

## Slide 53: Strategic Impacts
What does this mean?
  We are in the midst of a significant cyberinfrastructure upgrade
  Enterprise networks need not be unduly perturbed 
Significantly enhanced capabilities compared to 3 years ago
  Terabyte-scale data movement is much easier
  Petabyte-scale data movement possible outside the LHC experiments
    3.1Gbps = 1PB/month
    (Try doing that through your enterprise firewall!)
  Widely-deployed tools are much better (e.g. Globus)
Raised expectations for network infrastructures
  Scientists should be able to do better than residential broadband
    Many more sites can now achieve good performance
    Incumbent on science networks to meet the challenge
      Remember the TCP loss characteristics
      Use perfSONAR
  Science experiments assume this stuff works – we can now meet their needs
© 2015, Energy Sciences Network
Notes: I know a group that wants to do 1PB/week – they want to use Globus

## Slide 54: Why Build A Science DMZ?
Data set scale
  Detector output increasing
    1Hz  10Hz  100Hz  1kHz …  1MHz
  HPC scale increasing
    Increased model resolution  increased data size
    Increased HPC capability means additional problems can now be solved
  Sequencers, Mass Spectrometers, …
Data placement
  Move compute to the data?
  Sure, if you can…otherwise you need to move the data
Who needs the raw data?
  Anyone working on processing algorithms for raw data
  Anyone aggregating/integrating data sets (absent perfect prior reduction)
  Anyone doing data analysis for which a canned service does not exist
Without a Science DMZ, this stuff is hard
  Can you assume nobody at your institution will do this kind of work?
  If this kind of work can’t be done, what does that mean in 5 years?
© 2015, Energy Sciences Network
Notes: Data placement – a liquid market in fungible computing allocations does not exist, and is not expected to exist
This ignores network research – e.g. on SDN

## Slide 55
The Science DMZ design pattern provides a flexible model for supporting high-performance data transfers and workflows
Key elements:
  Accommodation of TCP
    Sufficient bandwidth to avoid congestion
    Loss-free IP service
  Location – near the site perimeter if possible
  Test and measurement
  Dedicated systems
  Appropriate security
Support for advanced capabilities (e.g. SDN) is much easier with a Science DMZ
Science DMZ gives flexibility, scaling, incremental provisioning for advanced services
Wrapup
© 2015, Energy Sciences Network

## Slide 56: Links
  ESnet fasterdata knowledge base
    http://fasterdata.es.net/
  Science DMZ paper
    http://www.es.net/assets/pubs_presos/sc13sciDMZ-final.pdf
  Science DMZ email list
    https://gab.es.net/mailman/listinfo/sciencedmz
  perfSONAR
    http://fasterdata.es.net/performance-testing/perfsonar/
    http://www.perfsonar.net
© 2015, Energy Sciences Network

## Slide 57: Thanks!
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
http://fasterdata.es.net/
http://my.es.net/
http://www.es.net/

## Slide 58: Extra Slides
© 2015, Energy Sciences Network

## Slide 59: The Science DMZ in 1 Slide
Consists of three key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with end users
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
© 2015, Energy Sciences Network
Notes: Single slide summary

## Slide 60: Extra Slides – Output Queue Discussion
© 2015, Energy Sciences Network

## Slide 61: Multiple Ingress Flows, Common Egress
Hosts will typically send packets at the speed of their interface (1G, 10G, etc.)
  Instantaneous rate, not average rate
  If TCP has window available and data to send, host sends until there is either no data or no window
Hosts moving big data (e.g. DTNs) can send large bursts of back-to-back packets
  This is true even if the average rate as measured over seconds is slower (e.g. 4Gbps)
  On microsecond time scales, there is often congestion
  Router or switch must queue packets or drop them
© 2015, Energy Sciences Network
Notes: A brief introduction to the impacts of buffering on network traffic. Key points:
- Host interfaces ‘burst’ at line rate, and then wait (e.g. it’s binary behavior, not a nice steady pacing at some average rate)
- multiple ingress flows behave differently depending on the architecture of the switch. If its ‘shared’ memory, all may be using the same memory buffer. If each interface has its own, then 1 or 2 bursting may be less impactful on the rest of the interfaces.
- buffer bloat is typically not a concern in a Science DMZ

## Slide 62: Router and Switch Output Queues
Interface output queue allows the router or switch to avoid causing packet loss in cases of momentary congestion
In network devices, queue depth (or ‘buffer’) is often a function of cost
  Cheap, fixed-config LAN switches (especially in the 10G space) typically have inadequate buffering. Imagine a 10G ‘data center’ switch as the guilty party
  Cut-through or low-latency Ethernet switches typically have inadequate buffering (the whole point is to avoid queuing!)
Expensive, chassis-based devices are more likely to have deep enough queues
  Juniper MX and Alcatel-Lucent 7750 used in ESnet backbone
  Other vendors make such devices as well - details are important
  Thx to Jim: http://people.ucsc.edu/~warner/buffer.html
  This expense is one driver for the Science DMZ architecture – only deploy the expensive features where necessary
© 2015, Energy Sciences Network
Notes: Goes along with the previous – output is just as important as input

## Slide 63: Output Queue Drops – Common Locations
© 2015, Energy Sciences Network
Notes: In the outbound direction, traffic from the cluster goes from 10G to 1G on the department core switch – the 10G DTN will burst, causing loss if the 1G output queue is too shallow
In the outbound direction, many 1G workstations can congest a single 1G uplink port
In the inbound direction, 10G of WAN traffic goes to a 1G port facing the department core switch – likely loss location (and on the wide area path to the DTN!)
There are a lot of networks with this sort of problem.
The best way to find the problem is to use perfSONAR

## Slide 64: Extra Slides – Firewall Internals
© 2015, Energy Sciences Network

## Slide 65: Thought Experiment
We’re going to do a thought experiment
Consider a network between three buildings – A, B, and C
This is supposedly a 10Gbps network end to end (look at the links on the buildings)
Building A houses the border router – not much goes on there except the external connectivity
Lots of work happens in building B – so much that the processing is done with multiple processors to spread the load in an affordable way, and results are aggregated after
Building C is where we branch out to other buildings
Every link between buildings is 10Gbps – this is a 10Gbps network, right???
© 2015, Energy Sciences Network
Notes: Go to next slide, speak to the diagram
The text on this slide is for people looking at the deck who are not present at the talk

## Slide 66: Notional 10G Network Between Buildings
© 2015, Energy Sciences Network
Notes: Building A houses the border router – not much goes on there except the external connectivity
Lots of work happens in building B – so much that the processing is done with multiple processors to spread the load in an affordable way, and results are aggregated after
Building C is where we branch out to other buildings

## Slide 67: Clearly Not A 10Gbps Network
If you look at the inside of Building B, it is obvious from a network engineering perspective that this is not a 10Gbps network
  Clearly the maximum per-flow data rate is 1Gbps, not 10Gbps
  However, if you convert the buildings into network elements while keeping their internals intact, you get routers and firewalls
  What firewall did the organization buy? What’s inside it?
  Those little 1G “switches” are firewall processors
This parallel firewall architecture has been in use for years
  Slower processors are cheaper
  Typically fine for a commodity traffic load
  Therefore, this design is cost competitive and common
© 2015, Energy Sciences Network

## Slide 68: Notional 10G Network Between Devices
© 2015, Energy Sciences Network
Notes: Now, convert the buildings into network devices
Building A becomes a border router
Building B becomes a firewall
Building C becomes a core router

## Slide 69: Notional Network Logical Diagram
© 2015, Energy Sciences Network
Notes: If you’re not allowed to look inside, this is all you see
This network is broken, but unless you know to go look you’ll never know why