## Slide 1: Open Transport Switch A Software Defined Networking Architecture for Transport Networks
Abhinava Sadasivarao, Sharfuddin Syed, Ping Pan, Chris Liou – Infinera
Andy Lake, Chin Guok, Inder Monga – Energy Sciences Network (ESnet)/LBNL
HotSDN Workshop, ACM SIGCOMM, August 2013
Notes: Hi All, This talk is about joint work done by Infinera and Energy Sciences Network – Infinera is an optical equipment vendor, and ESnet runs a 100G US-wide network over 13,000 miles of fiber, a mission network for science as it connects all US national labs and instruments. This talk is a about how we opened the covers under L2 and shone the SDN light on the layers below.

## Slide 2: A multi-layer network: background
…
…
…
packet
transport
Optical amplifiers
Approx. every 80km
Optical Transport Network Element
WDM Link
Data Center/Campus Chicago
Data Center New York
…
…
10/40G
10/40G
100GE
Icons from Cisco product library
WAN
100GE
Transport-
LSP
HO ODU
OMS
OTS
OPS
OTU
OCh OChr
Clients
OTM-n
OTM-0, OTM-nr
PW
S-EC
Service-LSP
LO ODU
B-EC
ETY*
ETY*
ETY*
Packet-optical
transport protocol stack
Layers image Courtesy Martin Vissers, Huawei
Notes: Just a background for the folks who have not played with Wide-Area Networks – the packet-based network drawings hide a lot of complexity in the optical transport layer that enables the ‘worldwide’ internet – metro, long-haul and submarine networks. Each of these devices implement a complex multi-layer stack of protocols from L0 (lambdas) to L2 at the edges for packet-transport. If you think of train stations as ‘routers’, transport networks are the complex mesh of railway lines and switching points that interconnect all these stations together.

## Slide 3: Transport Paradigm is Different!
Packet World
Connectionless
Transport World
Connection (circuit) oriented
EMS/NMS + Cross-connect paradigm
Distributed CP solutions with numerous protocols
Nascent distributed CP, not inline (GMPLS)
Inline control plane (NMS independent)*
Static pipes/configuration, trends to be more dynamic
Dynamic flows
Historically, transport networks have been programmable by
Centralized NMS/OSS.
* Logically centralized model with SDN
Notes: The packet world and transport world are different paradigms. Transport networks are more statically configured, with dynamic / agility needed for protection/restoration in case of a fiber cut. These kind of dynamic services have evolved the transport networks to deploy nascent distributed CP solutions based on GMPLS. So in one way, the SDN architecture resonates well with how optical networks have been managed.

## Slide 4: Motivation
WAN Packet Network
(routers, switches)
Campus
Pkt . network
Data Center
Packet network
WAN
Transport Network
SDN
Controller
SDN
Controller
SDN
Controller
OF
NMS
Proprietary and/or
TL1
Applications
OF
Network Virtualization
Uniform end-to-end control of network resources, agility, application-responsiveness
Services/apps like optical bypass, bandwidth-on-demand, multi-layer TE, virtual overlays
Fast Optical
switching
Campus’s
Optical net.
GMPLS (vendor specific)
Notes: Move optical provisioning under SDN control using the same protocols as in the packet world – rather than depend on a different configuration paradigm. One can leverage the same network virtualization methods and applications built on top of the Network OS. The methods use on the WAN can also be applied to large private enterprise networks or university campuses, as well as, the fast optical switching paradigm within the large data centers.
two questions: why? And what’s the best architecture to do so? OTS

## Slide 5: Use Case: Multi-Layer Optimization
$,W
Router
Optics
Digital
Switching
$$$,kW
Converged Packet/OTN/Optical Layer
IP/MPLS Layer
Next-gen networks drive need for multi-layer representation, topology computation & provisioning
SDN approach facilitates orchestration across layers & domains
Orchestration Application/SDN Controller
Local IP net
Local Enet
Analytics
Provisioning

## Slide 6: Architectural Approach: Abstract and Simplify
  Abstract the interface between packet-optical layers
Open Transport Switch (OTS) abstraction
  OpenFlow controllable, lightweight virtual switch representation of a Transport Network Element
  Capabilities exposed by OTS depends on the optical network element
  Provides all the interfaces needed to provision, control and monitor

## Slide 7: OTS building blocks: a high-level view
OTS-Mgmnt.*
OTS-Control/ Discovery
OTS-Data Plane
OTS Abstraction
Optical Control Plane
Data Transport Plane
Transport switch
hardware
/
N physical interfaces
Resource configuration
Perf. Monitoring
OTS configuration
Topology
Links
State changes
Match-Action for
Creating connections
OFwire ++*
* Recent architectural discussions have decided to not change OFw protocol.
Notes: Explain Topology (no LLDP) – needed for connections
Degraded optical connections, Bit errors.

## Slide 8: OTS Building Blocks (contd.)
Transport switch
hardware
OTS instance (1)
OTS instance (n)
Slice a hardware
device
OTS instance (1)
OTS instance (n)
Virtualize a multi-domain
transport network

## Slide 9: Example #1: Explicit Provisioning (SDN Controller is to provision every flow on every node!)
Ethernet
Switch
Ethernet / DWDM
Ethernet
Switch
A
B
C
D
Ethernet / DWDM
VLAN
100
VLAN
200
VLAN
300
VLAN
400
Wave
X
OTS
OTS
OTS
OTS
SDN
Controller
Topology report:
L1: 10GE
L2: to B, 100GE
A
D
H
E
L2
L4
B
C
G
F
L3
L1
L5
Provisioning (e.g., OpenFlow):
L2-L3 :: map VLAN-200 packets to VIF X

## Slide 10: Example #2: Implicit Provisioning (SDN Controller is to provision every flow on some nodes!)
LSR
LSR
LSR
LSR
POTN
POTN
POTN
POTN
ENET
ENET
ENET
ENET
OTS
OTS
OTS
OTS
OTS
OTS
A
B
C
D
E
F
SDN Controller
Data
Data
Label
Data
Data
ODU
Data
Data
VLAN
Data
A
D
B
C
F
E
MPLS
OTN (GMPLS)
L2 Ethernet
Provisioning:
Setup A-B with BW X
Provisioning:
Setup C-D with BW X
Map data to C-D
Topology export:
Node, link and resource (TED)
Including MPLS for packet, GMPLS of optical…
OTS

## Slide 11: OTS Demo: deployed on Long Island testbed
bnl-tb-wdm-3
bnl-tb-wdm-4
40G
100G
20G
20G
20G L1 Tunnel
SDN Controller communicating with OTS-DataPlane via OpenFlow extensions
Bandwidth on Demand application for Big Data RDMA transport
3 physical transport path options (with varying latencies)
Implicit & explicit provisioning of 10GbE/40GbE services demonstrated
Topology Monitoring App
On-Demand TE App
ESnet SDN Controller
Mellanox
Mellanox
Path #1
Path #2
Path #3
OTS
ESnet LIMAN Production Network
Brookhaven National Laboratory
Testbed
OTS

## Slide 12: Application: Create Circuit

## Slide 13: SDN/OTS: Execute Application Req
Vendor extension

## Slide 14: Application: Circuit Active

## Slide 15: Previous work
Saurav Das, Unified Control Architecture for Packet and Circuit Network Convergence, PhD Thesis, Stanford University, June 2012

## Slide 16: Now to Future
Now
  LIMAN Demonstration: December 2012
  ONF Open Transport Working Group: March 2013
    Use-cases & Architecture: In progress
    Most optical and router companies participating
Future
  Explore Topology and Monitoring
  Network Optimization using multi-layer PCE
  How does protection fit within the architecture?

## Slide 17: Thank you!
imonga at es dot net
Energy Sciences Network
http://www.es.net/inder
Shameless plug: We are hiring and looking for a post-doc & software engineer
to work on SDN topics!
https://lbl.taleo.net/careersection/2/jobdetail.ftl?lang=en&job=75692